## Slide 1: Annual Air Monitoring Data Certification and Concurrence Process

## Slide 2
The Actual Requirement
in CFR Language
§ 58.15 Annual air monitoring data certification.
(a) The State, or where appropriate local, agency shall submit to the EPA Regional Administrator an annual air monitoring data certification letter to certify data collected by FRM, FEM, and ARM monitors at SLAMS and SPM sites that meet criteria in appendix A to this part from January 1 to December 31 of the previous year. ... The annual data certification letter is due by May 1 of each year.“
(b) Along with each certification letter, the state shall submit to the Regional Administrator an annual summary report of all the ambient air quality data collected by FRM, FEM, and ARM monitors at SLAMS and SPM sites. …”
(c) Along with each certification letter, the State shall submit to the Regional Administrator a summary of the precision and accuracy data for all ambient air quality data collected by FRM, FEM, and ARM monitors at SLAMS and SPM sites. …”
URL for AMTIC Cert & Validation: https://www3.epa.gov/ttn/amtic/qacert.html

## Slide 3
Data Certification Information
On AMTIC

## Slide 4
Data Certification Qualifier Values

## Slide 5
Criteria that Generate Green (Acceptable) Warning (Yellow) and “N” Qualifiers (Red)

## Slide 6
Blue shaded rows are evaluations that will be reported (when data is available) but not used in certification flag settings
One Red for any monitor will elicit an AQS recommended “N” flag
Three warnings for any monitor will elicit an AQS recommended “N” flag
Criteria that Generate Green (Acceptable) Warning (Yellow) and “N” Qualifiers (Red)
Notes: The table from this slide and the previous slide are from the Additional Information Document found on the AMTIC website. The document provides information as to how QA and completeness data are evaluated to determine if AQS recommends monitors for (‘Y’) or against (‘N’) certification.

## Slide 7
Preliminaries: What should a certifying agency do?
Review the Certifying Agency role assignments:
  Run the AQS Monitor Description Report – Will show all Agency Roles for each monitor.
  Compare against Monitoring Network Plan
Use AQS (Batch MD transaction or Maintain Monitor) to correct any discrepancies.
  Assumption: The monitor belongs to the certifying agency or an agency that is subordinate to them.

## Slide 8
The Procedure: What does an agency do?
Conduct and complete ambient air quality monitoring and QA as per 40 CFR Part 58 and submit all relevant data to AQS.
Run the Data Certification Report (AMP600) for your Certifying Agency.
  This will calculate a recommended certification flag for each monitor-year based on Part 58 criteria and display the results for all monitors and PQAOs associated with the Certifying Agency.

## Slide 9: Requesting a Data Certification Report

## Slide 10: Request Criteria

## Slide 11
Before Certifying Agency Certification
AMP600 Summary Report
Notes: This is an example of the summary page of an AMP600 – Certification Report. It shows a count of the number of monitors that AQS recommends for or against certification by pollutant, and it shows all monitors where AQS recommends against certification and the reason.

## Slide 12
AMP600- Ozone
Before Certification
No
v
alues
Notes: This is one of the “detail” pages for Ozone, where you can see the statics that are evaluated for each monitor, along with the classification (Green, Yellow, Red) for each statistic, and the monitor as a whole. For a monitor, AQS recommends against certification if any statistic is red, or if there are three or more Yellow statistics.

## Slide 13: The Procedure – Part 2: Data Review
Review the certification report. For ‘N’ recommendations:
  Has any ambient monitoring data not yet been submitted?
  Has any QA/QC data (e.g. Precision and Accuracy transactions) not been submitted?
  Should any ambient monitoring data be invalidated and removed from AQS based on QA/QC results?
Make corrections to AQS data as needed.
Rerun certification report and verify results are final.

## Slide 14
Certification Form for
Certifying Agency
If certifying this data, we’d really like a Certifying Agency qualifier
Notes: This record show a case where the certifying agency did not supply a “State Requested Value”. However, the problem is that AQS will present this on reports with the code “U’, which means that certification was not requested, rather than ‘N’, which means that the monitor fails QA or completeness. (i.e. it is ambiguous.)

## Slide 15
AMP600
After Certifying Agency Certification
Notes: This AMP600 report show records where the Certifying Agency did not request a value.

## Slide 16
After Certifying Agency Certification
AMP600 Summary
Notes: This is the summary section of an AMP600 report where the Certifying Agency did not request a value.

## Slide 17
17
AMP600
After EPA Regional Concurrence
Notes: This report shows after the Region has supplied an ‘N’ value.

## Slide 18
Comment required if Cert Agency changes AQS Recommended Flag
AMP600
After EPA Regional Concurrence
Data changed after certification
Notes: This slide shows two conditions that can be seen on the AMP600 report: The first shows where the EPA concurrence flag will be automatically changed to ‘M’ if the data for a monitor is changed after it was certified. The second shows that if the Certifying Agency requests a Certification Flag that is different than the AQS recommended value, they must provide a justification.

## Slide 19
Certification Form
Since the only qualifier that shows up in AQS is the EPA concurrence qualifier, any change in data by the Monitoring Organization will show up as “M” for modified

## Slide 20
AMP 450 Report
Notes: This is the AMP450 report, where the EPA concurrence value shows up.

## Slide 21
How the AMP600 Works
Found On AMTIC
PQAO Level Flags
For Collocation and PEP, AQS Recommended flags are generated at the PQAO level and then “transfered” back to each site
See “additional Information Related to AMP600 Certification Process” at http://www.epa.gov/ttnamti1/qacert.html
PEP PQAO Critera based on Bias estimate, not completeness
PQAO Criteria Met for Collocation based on CV not completeness
Notes: This slide shows an example of how the PQAO evaluation criteria affects every monitor for the PQAO. The PQAO CV statistic was evaluated to be “Yellow”, so every monitor for the PQAO is evaluated to be “Yellow”. If the PQAO had failed (“Red”) then all of its monitors would have been “Red” (Recommended against certification.)

## Slide 22: What Monitoring Data must Monitoring Agencies Certify by May 1, 2016?
Only data collected by FRM, FEM, and ARM monitors at SLAMS and SPM monitoring stations that meet Appendix A must be certified1. In practice this refers to monitoring data for CO, NO2, SO2 (hourly and 5-minute average data), Ozone, Lead, PM10, PM10-2.5, and PM2.5.
1 Data certification requirements may also be included in auxiliary agreements such as MOA’s between states and operators of industrial networks, for example, SO2 monitors being installed to comply with the Data Requirements Rule.

## Slide 23: Certification Process: Thoughts and Steps Forward
Use it often
  Don’t wait till May to run the report
  It can run on a partial year based on the date the report is run. This may not be perfect but can help.
By the time data is in AQS it may be to late
  Internal QC is critical
Will eventually add outlier statistics.