## Slide 1: NEI Review Module 3: PM Augmentation and TRI Data Broadcast will begin shortly
If you are having difficulties, please email Sally Dombrowski at dombrowski.sally@epa.gov

## Slide 2
Audio information
Type questions in the Q&A pod of the dashboard

## Slide 3: Agenda – Module 3 Overview
Why do we include additional datasets?
PM species in the NEI
How does the PM Augmentation tool work?
PM Aug tool results and caveats
PM Aug tool demo screenshots
Toxics Release Inventory (TRI) and other EPA datasets
2014 NEI Website:
https://www.epa.gov/air-emissions-inventories/2014-national-emissions-inventory-nei-information

## Slide 4: Why do we include additional data sets?
EPA adds additional data to State/Local/Tribe (SLT)-reported data in order to have the most complete inventory for end users.
  National Scale Air Toxics Assessment (NATA)
  Air quality modeling
  Criteria Modeling Platform – National Rule Assessments
  EPA Public Affairs
  International reporting
  EPA’s “Report on the Environment”
Some additional data sets are derived from SLT-reported data
  Chromium speciation
  HAP Augmentation
  PM Augmentation
Other added data sets are from independent sources
  TRI data
  EPA EGU estimates

## Slide 5: PM Augmentation
What PM pollutants are needed in the NEI?
  Air quality models use primary PM10 and PM2.5 (PM10-PRI and PM25-PRI)
    Derive PM-coarse by subtraction
    Black Carbon (EC) and Organic Carbon derived from PM25-PRI
  HAP Augmentation currently uses only PM10-FIL as an input (SLT-reported) pollutant to derive HAPs by ratio
The AERR / What PM pollutants are allowed to be reported to the Emissions Inventory System(EIS)?
  Any combination of PM10-PRI; PM25-PRI; PM-CON; PM10-FIL; PM25-FIL
  Filterable PM components (PM10-FIL, PM25-FIL) refer to particulate matter that may be physically captured on a filter during sampling
  Condensable PM (PM-CON) is gas-phase at stack conditions but condenses to sub-micron liquids or particles after exiting the stack and cooling to ambient conditions
  A few consistency QA checks in the EIS will reject all emissions:
    PM10-PRI must be >= each of these individual components: PM10-FIL, PM25-PRI and PM-CON
    PM25-PRI must be >= each of these individual components: PM25-FIL and PM-CON
    PM10-FIL must be >= PM25-FIL
Current PM Aug process goal is to create all five PM pollutants, consistent with each other
  Another goal is to also preserve SLT PM-PRI estimates, and add missing PM-CON and PM-FIL components only
  Short-term: Clean up the (posted) tool, make more user-friendly
  Longer-term (2017 NEI): Update ratios (emission factors), incorporate into the EIS that also generates specific “Emissions Method Code”

## Slide 6: What does the PM Augmentation tool do?
Uses SLT-reported PM values and control devices for SCCs
Uses large set of look-up tables of ratios of PM species by SCC and up to 2 control devices
Ratios are largely based on AP-42 EFs and size distribution graphs, with some mapping to similar SCCs and controls
Sequence of math steps and ratios to be used depends upon which PM species have been reported by SLT
  31 possible permutations. Common ones are both PM-PRIs reported; both PM-FILs reported; All 5 reported; Only PM10-PRI reported
  See link to 2013 CMAS paper within PM Aug “Tool Description” for all conditional logic steps

## Slide 7: PM Aug tool: How were the emissions calculated?
EIS Facility ID | PSC | State Facility ID | EIS Unit ID | State Unit ID | EIS Process ID | State Process ID | SCC | data_set_short_name | Pollutant Code | Description | Total Emissions | UOM
1013311 | AZDEQ | 492 | 48095013 | 1 | 61072414 | 1 | 20300203 | 2011AZDEQ | PM10-PRI | PM10 Primary (Filt + Cond) | 2.74543 | TON
1013311 | AZDEQ | 492 | 48095013 | 1 | 61072414 | 1 | 20300203 | 2011AZDEQ | PM25-PRI | PM2.5 Primary (Filt + Cond) | 2.74543 | TON
1013311 | AZDEQ | 492 | 48095013 | 1 | 61072414 | 1 | 20300203 | 2011EPA_PM-Aug | PM-CON | PM Condensible | 1.23544 | TON
1013311 | AZDEQ | 492 | 48095013 | 1 | 61072414 | 1 | 20300203 | 2011EPA_PM-Aug | PM10-FIL | PM10 Filterable | 1.50999 | TON
1013311 | AZDEQ | 492 | 48095013 | 1 | 61072414 | 1 | 20300203 | 2011EPA_PM-Aug | PM25-FIL | PM2.5 Filterable | 1.50999 | TON
PM Augmentation Tool, updated version 1.2 posted at:
  https://www.epa.gov/air-emissions-inventories/pm-augmentation
How to look at the calculation?
  Generate EIS process level report
  See Module 1 “Overview” webinar for more details on this report
  Provides dataset name for each process (county/SCC for nonpoint sources)
  PM Aug Tool-generated data reflected as “2014EPA_NonPt_PM-Aug” for nonpoint sources
  In this example, PM-CON, PM10-FIL and PM25-FIL are output from PM Augmentation via state-provided (AZ) PM10-PRI and PM25-PRI data.

## Slide 8: PM Augmentation tool results
Two Output tables : Adds and Overwrites
Adds are new PM species that didn’t appear in the SLT-reported set, which gap-fill where one or more of the five PM pollutants were not reported
Overwrites are for PM species that are in the SLT dataset, but where the logic sequence of the PM Augmentation routines found inconsistencies that are corrected by supplying a value that will be used preferentially over the SLT value
The Overwrites are why EPA PM Aug dataset is above SLT data in the selection hierarchy

## Slide 9: PM Aug tool: 2014 NEI caveats
While EPA provides the PM Augmentation Tool, we discourage using it as-is for several reasons, as documented in the README Word file in the zip package:
  For technical reasons, no augmentation was performed on several sectors such as railways, commercial marine vessels and agricultural field burning
  Overall, do not want to replace (Overwrite) SLT PM estimates with those from the PM Aug tool unless these overrides were “significant” (e.g., 0.01 ton) –particularly when primary PM species were reported and sensible.
  Do not include zero-emissions “adds”
NOTE: Because of these caveats, we stripped out the “Input PM Data – Nonpoint” in the PM Aug Control File –this is contrary to Step 4 in the “PM Augmentation Tool Instructions” PDF

## Slide 10: PM Aug tool: Screenshot demo, Nonpoint
Download tool, extract all files to common directory, open README (Word) and Instructions (PDF)
Open “PM Aug Control File”
Continue following PDF Instructions steps 5 through 7, with care taken to load (or append) only PM data and sources that you wish to augment.

## Slide 11: PM Aug tool screenshot, cont.
Example of PM Aug Overwrite data we decided NOT to use:
Only PM-CON missing, computed as PM10-PRI – PM10-FIL (0.0009) –see Trivial Update step 3.
However, PM25-PRI – PM25-FIL = 0.0008…

## Slide 12: PM Aug tool screenshots, cont.
Only PM-CON missing, computed (Additions output table) as PM10-PRI – PM10-FIL (0.0009)
However, PM25-PRI – PM25-FIL = 0.0008, but PM25-FIL+PM-CON now does not equal PM25-PRI, so, PM Aug Tool generates an OVERWRITE! HOWEVER, we deemed PM25-PRI difference of 0.0001 insignificant.

## Slide 13: TRI Augmentation and other EPA datasets

## Slide 14: TRI dataset
Why do we add Toxics Release Inventory (TRI) data to the NEI?
  To have a more complete inventory for HAPs, where SLT data not available
  Needed for presumably more-accurate risk modeling (e.g., NATA)
How do we add the data?
  TRI reports for Air emissions are a single total per facility for Stack emissions, and a single total per facility for Fugitive emissions, per pollutant
  EIS contains two Emission Processes for each EIS facility that has been matched to a TRI facility, one for Stack, one for Fugitive
  TRI data is Tagged and not used in the NEI if the SLT has reported that HAP (or one of its related HAPs) anywhere within the EIS Facility

## Slide 15: TRI dataset (cont.)
TRI data for 2014 Inventory Year were added to EIS March 15, 2016
The TRI data proposed to be added to EIS for 2014 was posted on the 2014 NEI website in October 2015
The TRI facility IDs that have been matched to EIS facilities are stored in EIS as an Alternate Facility ID, and are available at any time from EIS
There is no adjustment done at EPA to nonpoint estimates (either SLTs or EPAs) due to use of TRI at a facility
The EIS Operating Status of a facility does not impact the TRI use

## Slide 16: Other EPA datasets
EPA EGU: Various sources,
  Heat input throughputs from CAMD CEM and EPA EFs, either AP-42 or some MATS updates not yet in AP-42. CEM data are used for NOX and SO2.
Airports: CAPS & HAPs for aircraft operations and ground support equipment
Rail: carried forward from 2011v2 NEI
Commercial Marine Vessels: Bottom-up
Landfills: Via methane data from GHGRP, used only where no pollutants reported by SLTs
BOEM (Offshore Platforms): Carried forward from 2011v2 NEI
Nonpoint Mercury: Carried forward from 2011v2 NEI
“Carry Forward”: Sources EPA did not estimate for 2014, also carried forward from 2011v2 NEI

## Slide 17: Contact Information
Point
  Ron Ryan, ryan.ron@epa.gov, (919) 541-4330
  Laurel Driver, driver.laurel@epa.gov, (919) 541-2859
    Airports
Mobile Sources
  Laurel Driver, driver.laurel@epa.gov, (919) 541-2859
    On-road
    Non-road
    CMV
    Rail
Fires/Events
  Tesh Rao, rao.venkatesh@epa.gov, (919) 541-1173
    Includes Ag fires
NATA and HAP Augmentation
  Madeleine Strum, strum.madeleine@epa.gov, (919) 541-2383
EIS Support
  Sally Dombrowski, dombrowski.sally@epa.gov, (919) 541-3269
Nonpoint
  Jennifer Snyder, snyder.jennifer@epa.gov, (919) 541-3003
    Oil and Gas
    Solvents
  Rich Mason, mason.rich@epa.gov, (919) 541-3405
    Residential Wood Combustion
    ICI Fuel Combustion
    Mercury
  Rhonda Thompson, thompson.rhonda@epa.gov, (919) 541-5538
    Ag Livestock/Fertilizer/Pesticides/Tilling
    All dust categories
  Lee Tooly, tooly.lee@epa.gov, (919) 541-5292
    Asphalt Paving