## Slide 1: Evaluating Management Actions to Promote Salt Marsh Resilience
Rachel W. Jakuba, PhD, Buzzards Bay Coalition
SNEP Symposium, May 18, 2022
Project Team
Alice Besterman
Joe Costa
Linda Deegan
Wenley Ferguson
Diana Brennan
Neil Ganju

## Slide 2: Salt Marshes in the Landscape
Very productive areas of estuaries (store carbon)
Act like ‘filters’ converting dissolved nutrients into vegetation
Provide physical barrier to buffer storm impacts, flooding, and coastal erosion
Valuable habitat for variety of organisms including mussels, crabs, shrimp, striped bass, osprey, etc.
savebuzzardsbay.org

## Slide 3: Marsh Loss around Buzzards Bay
savebuzzardsbay.org
Westport River
Mattapoisett
Dartmouth

## Slide 4: Understanding Buzzards Bay marsh loss
26 - 66% of salt marsh area lost between 1938 and 2016
Rate of loss increasing
On each island, much of the marsh areas lost were the lowest elevation parts of that island
Relatively low root density at all sites suggests vulnerability to loss due to nitrogen pollution
savebuzzardsbay.org

## Slide 5: Community Concern for Marshes
From an email to the Buzzards Bay Coalition:
“The marsh grass is dying off in patches, leaving just mud that the water now flows into and is creating new smaller canals/rivulets when the tides are high.
The grass die-off is [a] …recent phenomenon, within the last year from what I've seen.
The shoreline itself, which my property abuts, has not changed or been affected yet, though once the marsh goes I would imagine that would soon follow.
This area has brought us so much peace and joy; we are willing to do quite a lot to save it.”
savebuzzardsbay.org

## Slide 6: Marsh Loss around Buzzards Bay
savebuzzardsbay.org
Dartmouth
If the water stays on the marsh for too long, it drowns the plants. Shallow water areas have the potential to expand outward rapidly, killing vegetation and converting interior marsh platform into open water.

## Slide 7: Runnels: Adaptation strategy catching speed
Runnels are small channels to create tidal connection between shallow water on the marsh surface and a creek or ditch, following topographical low areas or existing flow paths, and draining root zone
Wenley Ferguson, Save the Bay, RI began piloting runnels for salt marsh adaptation around 2010
savebuzzardsbay.org

## Slide 8: Project Goals
Synthesize and communicate existing knowledge on runnels
Test pilot runnels in Buzzards Bay
Identify where and when runnels are most effective in the context of marsh loss patterns and environmental conditions in Buzzards Bay
savebuzzardsbay.org

## Slide 9: Runnel Workshop
More than 70 scientists, practitioners, resource managers, regulators and other stakeholders
Opportunity to develop common understanding of potential use for runnels in our region
Break out sessions to examine and rank potential runnel sites

## Slide 10: Journal article
Overview of the history and use of runnels
Case study from Winnapaug Marsh in Rhode Island
Highlights research questions that still need addressing
savebuzzardsbay.org

## Slide 11: Site Visits to Runnels
Staff from all 3 regional mosquito control agencies to look at completed runnels and review the process used for site selection, runnel digging, and permitting.
Stakeholders from Allens Pond and non-profit staff actively engaged in restoration techniques around the watershed.

## Slide 12: Project Goals
Synthesize and communicate existing knowledge on runnels
Test pilot runnels in Buzzards Bay
Identify where and when runnels are most effective in the context of marsh loss patterns and environmental conditions in Buzzards Bay
savebuzzardsbay.org

## Slide 13
Buzzards Bay, Massachusetts

## Slide 14
Buzzards Bay, Massachusetts
Replicated BACI-design
Each marsh:
5 experimental +
5 reference sites

## Slide 15
Buzzards Bay, Massachusetts
Replicated BACI-design
Each marsh:
5 experimental +
5 reference sites
All sites (20)
Vegetation metrics
Photo stations

## Slide 16
Buzzards Bay, Massachusetts
Replicated BACI-design
Each marsh:
5 experimental +
5 reference sites
All sites (20)
Vegetation metrics
Photo stations
Intensive Sites (12)
Elevation
Soil characteristics
Water level
Shear strength
Water quality + TSS
Decomposition
Other environmental variables

## Slide 17
Little Bay
Ocean View
50 m
50 m
Pre-monitoring 2020
Runnels created Oct 2020 - Feb 2021
Monitor through 2023 at least
Experimental-runnel site
Reference site
Intensive site

## Slide 18: Installation

## Slide 19: Initial runnel results
Marsh surface

## Slide 20: Initial runnel results
Before the runnel – extended periods of standing water
Marsh surface

## Slide 21: Initial runnel results
Before the runnel – extended periods of standing water
After the runnel – tidal flooding but no standing water
Marsh surface

## Slide 22: Initial runnel results
Ocean View Farm
Before
Little Bay
Before
After
After
savebuzzardsbay.org

## Slide 23: Project Goals
Synthesize and communicate existing knowledge on runnels
Test pilot runnels in Buzzards Bay
Identify where and when runnels are most effective in the context of marsh loss patterns and environmental conditions in Buzzards Bay
savebuzzardsbay.org

## Slide 24: Lessons Learned
Small scale features that target specific areas of die-back.
Runnels are a valuable tool in an overall marsh management scheme.
Project design is still highly context-specific, so we recommend future runnel projects include individuals with training and experience using the technique, or similar hydrologic management tools.
Multiple partners provided key support.
Continued monitoring will be useful for characterizing potential sites.
savebuzzardsbay.org

## Slide 25: Acknowledgements
Alice Besterman
Joe Costa
Wenley Ferguson
Linda Deegan
Diana Brennan
Neil Ganju
savebuzzardsbay.org
Landowners, Collaborators, Students/Interns
Linda Vanderveer (Dartmouth Natural Resource Trust)
Whitney McClees (Town of Fairhaven)
Hillary Sullivan
Melissa Herring
Gizella Spencer
Julia Holtzer
Kara Falvey
Nico Gentile
Lillie Hoffart
Shea Stobaugh
Dawson Little Jennifer Sepanara

## Slide 26
Marstons Mills River Headwaters Cranberry Bog Restoration Project
Casey D. Chatelain
cchatelain@bcleanwater.org
linkedin.com/in/caseydchatelain

## Slide 30
Watershed Loading Data Courtesy of 2021 Town of Barnstable 208 Compliance Report; Cranberry Bog Data Courtesy of SMAST 2019 Technical Report and BCWC Data Collection
Current Attenuated Watershed Load
46,221 kg N
TMDL
25,643 kg N
Natural Ecosystem Function
Reduction Required to Meet TMDL
20,578 kg N
Cranberry bogs
7,602 kg N

## Slide 31
Map courtesy of Marstons Mills Historical Society

## Slide 32
Thermal Imagery courtesy of EPA Region 1

## Slide 37
2021 | 2022 | 2023 | 2024 | 2025
QAPP Approval |  |  |  | 
Feasibility Study |  |  |  | 
Conceptual Design |  |  |  | 
 | Design and permitting |  |  | 
 |  |  | Construction | 
Monitoring |  |  |  | 

## Slide 39
Marstons Mills River Headwaters Cranberry Bog Restoration Project
Casey D. Chatelain
cchatelain@bcleanwater.org
linkedin.com/in/caseydchatelain

## Slide 40
Teaneck Creek Park Habitat Restoration:
Regenerative Stormwater Conveyance &
Sand Seepage Wetlands
Southeast New England Program 2022 Symposium
Virtual
May 18, 2022
KEVIN DAHMS, PE
WATER RESOURCES ENGINEER
BIOHABITATS, INC.

## Slide 41
OVERVIEW
OVERVIEW
PROJECT BACKGROUND
PROJECT DRIVERS
PROJECT APPROACH
LESSONS LEARNED
41

## Slide 42
PROJECT PARTNERS
PROJECT LEAD
DESIGN
CONSTRUCTION MANAGEMENT
CONTRACTOR
PARTNERS & FUNDING
PROJECT BACKGROUND
42

## Slide 43
PROJECT LOCATION
Teaneck Creek Park, Teaneck, NJ
PROJECT BACKGROUND
43

## Slide 44
PROJECT/SITE HISTORY
PROJECT BACKGROUND
TCC Founded
Wetland Restoration Concept
Remediation Plan
Construction Complete (anticipated)
Habitat Restoration Design
Construction Started
New Trails & Outdoor Classroom
2001
2006
2008
2010
2018
2020
2022
44

## Slide 45
PRE-RESTORATION CONDITIONS
PROJECT BACKGROUND
45

## Slide 46
PRE-RESTORATION CONDITIONS
PROJECT BACKGROUND
Trail system
Art and educational programming
Clay liner
46

## Slide 47
PROJECT DRIVERS
Public experience: noise from adjacent roads, degraded paths, debris piles
Impaired water quality (Dragonfly Pond, Teaneck Creek)
Erosion from stormwater
Infestation of invasive species
PROJECT DRIVERS
47

## Slide 48
PROJECT DRIVERS
PROJECT DRIVERS
Eroding stormwater gullies
Eroding brook
48

## Slide 49
PROJECT DRIVERS
PROJECT DRIVERS
Poor WQ in Dragonfly Pond and Teaneck Creek
49

## Slide 50
PROJECT DRIVERS
PROJECT DRIVERS
Invasive species (throughout)
50

## Slide 51
PROJECT DRIVERS
PROJECT DRIVERS
Debris piles (throughout)
51

## Slide 52
PROJECT DRIVERS
PROJECT DRIVERS
Noise from Degraw Ave
52

## Slide 53
PROJECT DRIVERS
PROJECT DRIVERS
Noise from Degraw Ave
Debris piles (throughout)
Invasive species (throughout)
Poor WQ in Dragonfly Pond and Teaneck Creek
Eroding stormwater gullies
Eroding brook
53

## Slide 54
PROJECT GOALS
Enhance the site’s natural resources
Increase biodiversity
Mitigate erosive forces of stormwater throughout the site
Improve public access and visitor experience
Improve community health and well-being
Educate the public about the park’s habitat and ecology
PROJECT DRIVERS
54

## Slide 55
PROJECT METRICS
Over 20 acres of habitat restoration
430 linear feet of stormwater channel restoration
300 linear feet of trail realignment
16 debris piles removed or capped
PROJECT APPROACH
55

## Slide 56
PROJECT PLANS
Regenerative stormwater conveyance
Sand seepage wetlands
Invasive species management (mechanical/chemical)
Native plantings
Trail rehabilitation
Debris pile removal
Lookout berm creation
PROJECT APPROACH
56

## Slide 57
PROJECT PLANS
Regenerative stormwater conveyance
Sand seepage wetlands
Invasive species management (mechanical/chemical)
Native plantings
Trail rehabilitation
Debris pile removal
Lookout berm creation
PROJECT APPROACH
57

## Slide 58
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
PROJECT APPROACH
58

## Slide 59
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
PROJECT APPROACH
59

## Slide 60
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
PROJECT APPROACH
60

## Slide 61
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
Hillside RSC - Before
PROJECT APPROACH
61

## Slide 62
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
Hillside RSC - After
PROJECT APPROACH
62

## Slide 63
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
Hillside RSC - After
PROJECT APPROACH
63

## Slide 64
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
Oakdene RSC - Before
PROJECT APPROACH
64

## Slide 65
PROJECT DETAILS – REGENERATIVE STORMWATER CONVEYANCE
Oakdene RSC - After
PROJECT APPROACH
65

## Slide 66
PROJECT DETAILS – SAND SEEPAGE WETLANDS
PROJECT APPROACH
66

## Slide 67
PROJECT DETAILS – SAND SEEPAGE WETLANDS
PROJECT APPROACH
67

## Slide 68
PROJECT DETAILS – SAND SEEPAGE WETLANDS
Upper Sand Seepage - Before
PROJECT APPROACH
68

## Slide 69
PROJECT DETAILS – SAND SEEPAGE WETLANDS
Upper Sand Seepage - After
PROJECT APPROACH
Photo Credit: SiteWorks
69

## Slide 70
PROJECT DETAILS – SAND SEEPAGE WETLANDS
Lower Sand Seepage - After
PROJECT APPROACH
70

## Slide 71
PROJECT DETAILS – SAND SEEPAGE WETLANDS
Precedent Project - Maryland
PROJECT APPROACH
Post-Earthwork
Post-Planting
10 Years After Construction
71

## Slide 72
LESSONS LEARNED
Communication to stakeholders
Understanding timeline and schedule
Collaboration between project partners
Phasing of large projects
Site stabilization and vegetation establishment
Multi-pronged invasive species control (and long-term stewardship)
Maintenance of structures
LESSONS LEARNED
72

## Slide 73
Thank You
Questions?
Contact: kdahms@biohabitats.com
73