## Slide 1: DELETE THIS SLIDE PRIOR TO PRESENTATION
This PowerPoint serves as a template presentation which introduces topics related to air quality and is part of a suite of presentations provided by the EPA for the Megacities program.
See speaker notes for an additional description of slide content. Slides should be edited or added to as necessary for your particular needs. Slides with highlighted yellow text require the addition of specific context and information for your city.

## Slide 2: Air Quality Index

## Slide 3: Overview
1. Intro to AQI
2. AQI Communication
3. Calculating AQI
4. Source Data
5. Example

## Slide 4: Section 1: Intro to AQI
1. Intro to AQI
2. AQI Communication
3. Calculating AQI
4. Source Data
5. Example

## Slide 5: What is an Air Quality Index?
An Air Quality Index (AQI) is a communication device to convey to the general public air quality conditions in a standard framework
In the U.S., the EPA bases the AQI on five pollutants:
  ground-level ozone
  particulate matter (PM2.5 and PM10)
  carbon monoxide
  nitrogen dioxide
  sulfur dioxide
Notes: AQI is a communication device to convey to the general public air quality conditions in a standard framework: Transforms weighted values of individual air pollutants into a single, digestible number for the general public​
Typically, the reported AQI will be based on either PM2.5 or ozone, due to elevated air concentrations

## Slide 6: Pollutants in the U.S. AQI
The U.S. EPA has set National Ambient Air Quality Standards (NAAQS) for six principal “criteria” pollutants
  Lead is not considered in the Air Quality Index because sampling occurs over weeks to months, rather than hours
  Criteria pollutants impact human health, and are emitted from numerous or diverse sources
  Regulated at the state or tribal government level
  Standards set without concern for economic cost
Hazardous air pollutants are not included in the AQI, but are regulated
  This list includes pollutants such as benzene, arsenic, cadmium, and nickel
  These pollutants are regulated through emissions standards for relevant industries

## Slide 7: U.S. AQI Levels
Daily AQI Color | Levels of Concern | Values of Index | Description of Air Quality
Green | Good | 0 to 50 | Air quality is satisfactory, and air pollution poses little or no risk.
Yellow | Moderate | 51 to 100 | Air quality is acceptable. However, there may be a risk for some people, particularly those who are unusually sensitive to air pollution.
Orange | Unhealthy for Sensitive Groups | 101 to 150 | Members of sensitive groups may experience health effects. The general public is less likely to be affected.
Red | Unhealthy | 151 to 200 | Some members of the general public may experience health effects; members of sensitive groups may experience more serious health effects.
Purple | Very Unhealthy | 201 to 300 | Health alert: The risk of health effects is increased for everyone.
Maroon | Hazardous | 301 and higher | Health warning of emergency conditions: everyone is more likely to be affected.
AQI Basics | AirNow.gov

## Slide 8: PM2.5 AQI Breakpoints
Roughly consistent with Emergency Action Plans
50: Annual Standard
(12 µg/m3)
100: Short-term Standard
(35 µg/m3)
500: Significant Harm Level
Notes: AQI is a useful communication device, but what are the breakpoints based on? For each pollutant, breakpoints between values in the index are based on pollution standards. ​
Pollutant Standards Index (PSI); created in 1976

## Slide 9: Section 2: AQI Communication
1. Intro to AQI
2. AQI Communication
3. Calculating AQI
4. Source Data
5. Example

## Slide 10: Communication of AQI
In the U.S., Metropolitan Statistical Areas with populations of 350,000 are required to report the AQI daily to the general population
Forecasts are also generally available, but not required
Weather reporting often includes forecasts of AQI
https://www.airnow.gov/sites/default/files/2020-05/aqi-technical-assistance-document-sept2018.pdf

## Slide 11: AQI in Weather Reporting
www.wunderground.com
Notes: Example of a weather report with AQI included​

## Slide 12: AQI in the U.S.
Calculated by pollutant
Based on pollutant-specific breakpoints
  Breakpoints are the highest and lowest pollutant concentrations for a given AQI category
The final value reported is the highest AQI value, with the associated responsible pollutant
Example:
8-hour ozone value of 0.07843 ppm
PM2.5 value of 35.927 µg/m3
CO value of 8.452 ppm

## Slide 13: Section 3: Calculating AQI
1. Intro to AQI
2. AQI Communication
3. Calculating AQI
4. Source Data
5. Example

## Slide 14: Calculating the AQI
Identify the highest concentration among all monitors within each reporting area and truncate as follows:
  Ozone (ppm) – truncate to 3 decimal places
  PM2.5 (µg/m3) – truncate to 1 decimal place
  PM10 (µg/m3) – truncate to integer
  CO (ppm) – truncate to 1 decimal place
  SO2 (ppb) – truncate to integer
  NO2 (ppb) – truncate to integer
Example:
8-hour ozone value of 0.07843 ppm
= 0.078 ppm
PM2.5 value of 35.927 µg/m3
= 35.9 µg/m3
CO value of 8.452 ppm
= 8.4 ppm
Adapted from Technical Assistance Document for the Reporting of Daily Air Quality, EPA

## Slide 15: Calculating the AQI
2. Find the two breakpoints that contain the pollutant concentration
 | Ozone (8-hour) | Ozone (1-hour) | PM2.5 (24-hr) | PM10 (24-hr) | CO (8-hr) | SO2 (1-hr) | NO2 (1-hr)
Good (0 – 50) | 0 - 0.054 |  | 0 - 12.0 | 0 - 54 | 0 - 4.4 | 0 - 35 | 0.53
Moderate (51 – 100) | 0.055 - 0.070 |  | 12.1 - 35.4 | 55 - 154 | 4.5 - 9.4 | 36 - 75 | 54 - 100
Unhealthy for Sensitive Groups (101 – 150) | 0.071 - 0.085 | 0.125 - 0.164 | 35.5 - 55.4 | 155 - 254 | 9.5 - 12.4 | 76 - 185 | 101 - 380
Unhealthy (151 – 200) | 0.086 - 0.105 | 0.165 - 0.204 | 55.5 - 150.4 | 255 - 354 | 12.5 - 15.4 | 186 - 304 | 361 - 649
Very Unhealthy (201 – 300) | 0.106 - 0.200 | 0.205 - 0.404 | 150.5 - 250.4 | 355 - 424 | 15.5 – 30.4 | 305 - 604 (24-hr) | 650 - 1249
Hazardous (301 – 500) |  | 0.405 - 0.604 | 250.5 - 500.4 | 425 - 604 | 30.5 - 50.4 | 605 - 1004 (24-hr) | 1250 - 2049
Example:
8-hour ozone value of 0.078 ppm
PM2.5 value of 35.9 µg/m3
CO value of 8.4 ppm

## Slide 16: Calculating the AQI
3. Calculate the index using the standardizing index
Where:
Example:
O3:
PM2.5:
CO:
Notes: So the AQI itself is just the interpolated value within the identified “breakpoints bin”​

## Slide 17: Calculating the AQI
4. The AQI is the highest index value calculated and the associated responsible pollutant
Example:
O3: 126
PM2.5: 102
CO: 90
The AQI is 126, with ozone as the responsible pollutant

## Slide 18: Section 4: Source Data
1. Intro to AQI
2. AQI Communication
3. Calculating AQI
4. Source Data
5. Example

## Slide 19: Source Data for AQIs
AirNow: Federal Equivalency Monitors (FEMs)
  Embassies monitor PM2.5
IQAir: www.iqair.com
  Sources and calculation methods unclear
air-quality.com
  Sources and calculation methods unclear
The World Air Quality Project: aqicn.org
  Data from environmental protection agencies
  Based on PM2.5 monitoring

## Slide 20: Airnow: U.S.
National Maps | AirNow.gov
Notes: AirNow is a US gov’t website that provides an easy way to look at current and forecasted air quality in the U.S. National maps show where air quality will be worse on a given day, and visitors to the site can also look at site-specific air quality information by selecting a location on the map.​

## Slide 21: AirNow: City-Level AQI
AirNow.gov
Notes: This is an example of a site-specific air quality dashboard on AirNow. Here, visitors can see current air quality in the context of the index, the primary pollutant, and any relevant announcements.

## Slide 22: AirNow: International
US Embassies and Consulates | AirNow.gov
Notes: AirNow also provides international air quality metrics based on monitoring data from U.S. embassies and consulates.​

## Slide 23: Section 5: Example
1. Intro to AQI
2. AQI Communication
3. Calculating AQI
4. Source Data
5. Example

## Slide 24: Example: Santiago, Chile
Santiago experiences extreme, multi-day thermal air inversions resulting in sustained high pollutant levels
Ministry of Environment developed a method for informing the public of a “critical episode” on days when air quality is predicted to be poor
On “critical episode” days, restrictions are placed on industry and transportation depending on the episode status
  Episode status determined from AQI as Good, Alert, Pre-emergency, and Emergency
  Restrictions include: parking restrictions, restricting road type access, prohibiting agricultural burning and use of non-certified heaters, etc.
https://www.shutterstock.com/image-vector/inversion-layer-pm-25-vector-dust-1296240271​

## Slide 25: Example: Santiago’s Converted Air Quality Index (AQI) to PM levels
*ICAP is a Spanish acronym for AQI

## Slide 26: Thank you!