## Slide 1: Combined Air Emissions Reporting System (CAERS) Reporting Control Devices in CAERS January 27, 2026
Notes: On behalf of the US EPA, I’d like to welcome you to the Combined Air Emissions Reporting System or CAERS.

## Slide 2: Before we begin…
Keep yourselves muted. Type your questions in the chat box as we go through the training.
Disclaimer: This training on reporting control devices is intended for instructional purposes only. Data shown in the training are illustrative, and do not represent a real report for any facility or inventory year. None of the examples represent a complete report.
This training does not cover examples of all possible control device configurations. You should always consult with your SLT to discuss specific cases you may have questions about.

## Slide 3: Outline of Training
Control-related concepts and data fields
Entering data for different control configurations
  No control devices
  Single control device
  Controls in series
  Controls in parallel
  Complex control device configurations
Examples of Different Control Configurations
Questions

## Slide 4: Control-related Concepts and Data Fields

## Slide 5: Release Point Apportionment
Percent release point apportionment: The average annual percent of an emissions process that is vented through a release point. The percent of emissions that are sent to a stack release point through controls is also referred to as “capture efficiency”. Percent captured = Percent pollutant stream routed to the device going to “stack” type release points (X%). Percent not captured = Percent going to “fugitive” release point (100-X)%
Process
Uncontrolled Emissions
X%
Control (s)
…
Stack
(100-X)%
Fugitive
Note that 100% of the original emissions must be assigned to one or more release points

## Slide 6: Release Point Apportionment - User Interface
Found in the screen for each existing process under the “Release Points Associated with this Process” heading.
The process and release point(s) must exist in CAERS before emissions can be apportioned.
Must be entered when control devices are present.

## Slide 7: Release Point Apportionment - Bulk Upload
Found in the “Apportionment” tab and can be entered for existing release points.
Must be entered when control devices are present.

## Slide 8: Percent Control Device Effectiveness
Percent control effectiveness: The percentage of time or activity throughput that a control device is operating as designed, including the capture and reduction devices. This percentage accounts for the fact that controls typically are not 100% effective because of equipment downtime, upsets and decreases in control efficiencies. This could be estimated from the amount of time the control is operational, versus down for maintenance or repairs. When the control is not effective, the pollutant is not removed from the emissions stream.
Control (s)
% when control is effective
Removed Emissions
% when control is not effective
Stack
        Example:
        Control Effectiveness =
        (2000-200)/(2000) *100 = 90%, where:
        the emissions Process or Unit ran for 2000 hours.
        the Control Scenario was operationally down for 200 hours for maintenance.

## Slide 9: Control Device Effectiveness - User Interface
Found in the screen for each new or existing control device.

## Slide 10: Control Device Effectiveness - Bulk Upload
Found in the “Control Device” tab.

## Slide 11: Control Percent Pollutant Reduction Efficiency
Percent Pollutant Reduction Efficiency: The percent reduction achieved for the pollutant when all control measures are operating as designed. This information could be obtained from the vendor or test data, for example.
Control (s)
Removed Emissions
Stack
% when control is effective
% pollutant reduction efficiency
Example:
The control device removes 95% of the pollutant.

## Slide 12: Control Percent Pollutant Reduction Efficiency - User Interface
Found in the screen for each existing control device, under “Control Device Pollutants”.

## Slide 13: Control Percent Pollutant Reduction Efficiency - Bulk Upload
Found in the “Control Device Pollutants” tab and can be entered for existing controls.

## Slide 14: Flow of Uncontrolled Emissions
Fugitive Emissions
Process
Uncontrolled Emissions
Release point apportionment (% Captured)
Release point apportionment (% Not captured)
% Effective
% Not effective
Stack Emissions
Removed Emissions
Control
Device
% Efficient
% Not efficient
Stack Emissions
% Not captured = 100 - % Captured
% Not effective = 100 - % Effective
% Not efficient = 100 - % Efficient

## Slide 15: Controlled (Post-Control) Emissions
Fugitive Emissions
Process
Uncontrolled Emissions
Release point apportionment (% Captured)
Release point apportionment (% Not captured)
% Effective
% Not effective
Stack Emissions
Removed Emissions
Control
Device
% Efficient
% Not efficient
Stack Emissions
Overall Controlled (Post-control) emissions = Uncontrolled emissions * [ 100 – (% Captured * % Control Effectiveness * % Control Pollutant Reduction Efficiency)]
Controlled Emissions
=
+
Stack Emissions
Fugitive Emissions

## Slide 16: Accounting for the Entire Emissions Stream
Uncontrolled emissions apportioned to release points = fugitives + captured emissions (emissions apportioned to non-fugitive or stack release points)
Captured emissions = emissions when control is effective + emissions when control is not effective
Emissions from effective control = removed + not removed if control is not 100% efficient
Removed emissions = uncontrolled emissions * capture * control effectiveness * control pollutant reduction efficiency
Overall Controlled (Post-control) Emissions = uncontrolled emissions * (1 – captured * control effectiveness * control pollutant reduction efficiency)

## Slide 17: Reporting Control Devices
Individual control devices are listed for the facility.
Pollutants removed by each control device are listed with it.
Control device configuration is defined:
  Single
  In series
  In parallel
  Combinations / Complex Configurations
Are placed in paths individually or with other control devices to associate them between a units/processes and release points so we may track the emissions stream flow.

## Slide 18: Paths
Path: A “container” of one or more control devices that are connected, and through which an emissions stream flows.
Child Path: is a path contained within another path
Parent Path: contains one or more child paths and may also contain additional control devices. A parent path can be a child path to a larger parent path
Primary or Main Path:
  Contains one or more control devices and/or child paths
  Is the path ultimately associating the control devices/paths it contains from a unit/process to a release point
Child Path
Parent Path

## Slide 19: Paths Continued
Paths may be contained in other paths, but paths cannot intersect.
Path 1
Path 2

## Slide 20: Simplest Example of a Path
Unit 1
Process 1
Control A
Release Point 1
Path A
Release Point 2

## Slide 21: Path Concepts
Control/Path Assignment: the position that a control device occupies within a path with respect to other control devices contained in that path. The first control device in a path is assigned 1.
Control/Path Apportionment: the percentage of the emissions that are being directed to the next control or path.
Path Effectiveness: The combined effectiveness of the controls in that path. Must be reported on a main or primary path.
Path Pollutant Percent Reduction Efficiency: The combined percent reduction efficiency of the pollutant for the entire path. Must be reported on a main or primary path.

## Slide 22: Single Control Device
For a single control device one path is needed. The control is placed in that path. That path will be the primary path, and it will associate the process to the release point. Because there’s only one control, path assignment is just equal to 1.
Unit 1
Process 1
Control A
Path A (primary)
Release Point 1
Information You Need: release point apportionment (% to Release Point 1 and 2), control effectiveness, pollutant reduction efficiency, path assignment = 1, control apportionment = 100%, path effectiveness = control effectiveness, path efficiency = control efficiency.
Release Point 2

## Slide 23: Single Control Device on Multiple Units/Processes
Note that once this path is created for a single control device, any process sending emissions to the same release point can also use that path. So, you only have to create that path once, then reuse it as needed for each process.
Unit 1
Process 1
Process 2
Process 3
Control A
Path A (primary)
Release Point 1
Information You Need: release point apportionment, control effectiveness, pollutant reduction efficiency, path assignment = 1, control apportionment = 100%, path effectiveness = control effectiveness, path efficiency = control efficiency.
Release Point 2

## Slide 24: Multiple “Single Control Devices”
Unit 1
Process 1
Process 2
Process 3
Control A
Path A (primary)
Release Point 1
Unit 2
Process 1
Process 2
Process 3
Control B
Path B (primary)
Release Point 2
Unit 3
Process 1
Process 2
Process 3
Control C
Path C (primary)
Release Point 3
The case of multiple control devices that are “single” controls between a unit/processes and release point is the same as for a single control. One path is created for each control and each path associates the unit/process with the respective release point.
Path assignment = 1 and control apportionment = 100%, path effectiveness = control effectiveness, path efficiency = control efficiency, for each control device in each of its paths.
Release Point 4
Release Point 5
Release Point 5

## Slide 25: Single Control Device on Multiple Units/Processes/Release Points
Unit 1
Process 1
Process 2
Process 3
Unit A
Process A
Process B
Process C
Control A
Path A (primary)
Release Point 1
Release Point 2
A path can be shared by units/processes if they all direct their emission through the control(s) in that path and also “share” release points
Information You Need: release point apportionment (% to Release Points 1, 2, and 3), control effectiveness, pollutant reduction efficiency, path assignment = 1, control apportionment = 100%, path effectiveness = control effectiveness, path efficiency = control efficiency.
Release Point 3

## Slide 26: Control/Path Assignment
A Control/Path Assignment defines the order in which control devices are configured, each control or child path is given a sequence number:
  Increasing “sequence number” if in sequence
  The same “sequence number” if in parallel

## Slide 27: Multiple Control Devices – In Series
Multiple controls in series can be placed in a path and that path can be reused by many processes going to the same release point(s), if it is the primary path between each process and release point(s), as in the previous slide.
Unit 1
Process 1
Control A
Control B
…
In Series Path (primary)
Release Point 2
Information You Need: release point apportionment, control effectiveness, pollutant reduction efficiency, path assignment ( in the sequence; assignments control A=1, Control B=2,…), control apportionment = 100%. Path efficiency and effectiveness are a combination of the efficiency and effectiveness of the individual controls. Consult your SLT for appropriate calculation method to use.
Release Point n
Release Point 1
1
2

## Slide 28: Multiple Control Devices – In Parallel
Multiple control devices in parallel can be placed in on path and that path can be reused if it is the primary path, so long as it associates units/processes with the same release point(s).
Unit 1
Process 1
Control A
Control B
…
In Parallel Path (primary)
Release Point 1
Information You Need: release point apportionment, control effectiveness, pollutant reduction efficiency, path assignment (position of control in the sequence, if parallel, all controls have the same sequence number), control apportionment (e.g. 33% per control). Path efficiency and effectiveness are a combination of the efficiency and effectiveness of the individual controls. Consult EPA for appropriate calculation method to use.
Release Point n

## Slide 29: Control/Path Assignment - User Interface
Found in the screen for each existing path.

## Slide 30: Control/Path Assignment - Bulk Upload
Found in the “Control Assignments” tab using existing controls and paths as the sequence number.

## Slide 31: Control/Path Apportionment
Flow of emissions from one control device to the next will be tracked via the Control/Path Apportionment
  % of the emissions are routed to the next control or path.
  100% of the emissions are tracked, a control apportionment percentage < 100% for a control device means that some emission are also being routed to another control device or path.
  Are entered when entering control path assignment data.
Release Point Apportionment (revisited)
  Different than control apportionment
  Total uncontrolled emissions generated at the unit/process must be accounted for in terms of where they were ultimately released:
    Different types of release points
      Stack (captured)
      Fugitive
    100% of the original emissions must be assigned to one or more release points

## Slide 32: Control/Path Apportionment - User Interface
Found in the screen for each existing path.

## Slide 33: Control/Path Apportionment - Bulk Upload
Found in the “Control Assignments” tab using existing controls and paths.

## Slide 34: Percent Path Effectiveness
Required on main paths (those associated with a release point apportionment).
If only one control device is in the path, it is equal to the percent control effectiveness for that control.
Depends control device configuration (in sequence, parallel, a combination):
  In series: the multiplication of % control effectiveness,
  In parallel: the average or weighted average of control device effectiveness.
Consult your SLT on the best way to represent path effectiveness, especially if you have a complex control configuration.

## Slide 35: Path Effectiveness - User Interface
Found in the screen for each path.

## Slide 36: Path Effectiveness - Bulk Upload
Found in the “Control Paths” tab.

## Slide 37: Path Pollutant Percent Reduction Efficiency
Required on main paths (those associated with a release point apportionment).
If there is only one control device, then it is the same as the control percent reduction efficiency.
If there are more than one control device reducing the same pollutant, it is a combination of the reduction efficiency of all those devices.
Depends on the control device configuration (in sequence, parallel, a combination).
Consult your SLT on the best way to represent path effectiveness, especially if you have a complex control configuration.

## Slide 38: Path Pollutants - User Interface
Can be added in the screen for an existing path.

## Slide 39: Path Pollutants - Bulk Upload
Can be entered, for an existing path, in the “Control Path Pollutants” tab of the bulk upload template.

## Slide 40: Overall Percent Control - CAERS
Not required. CAERS will factor in the overall percent control in your emissions calculation if you have entered it:
  Single Control Overall Percent Control = percent captured * efficiency * effectiveness.
  Parallel Controls that control the same pollutant: add individual overall %.
  In Series Controls that control the same pollutant: multiply individual overall % controls.
  Complex Controls that control the same pollutant: may need average, weighted average. Consult your SLT on the best approach.
You may also need to factor in control apportionments.
Select a method of calculation that does not include control reductions to avoid double counting the reductions. E.g. EPA Factor (no control efficiency).

## Slide 41: Overall Percent Control - User Interface
Found in the emissions estimation screen

## Slide 42: Overall Percent Control - Bulk Upload Template
Found in the “Emissions” tab and can be entered for an existing unit/process and pollutant.

## Slide 43: Steps to Enter Data

## Slide 44: General Data Entry Steps for Control Devices and Paths
Ensure unit/process and release point data are available first
Enter control device data: effectiveness, pollutant and % pollutant reduction efficiency
Place the control into a path: assignment (sequence #), control apportionment
  Control into path
  Child path into parent path
  Controls and/or children paths into a primary path
  Associated efficiency and effectiveness
Apportion emissions from the process to the release point (release point apportionment)

## Slide 45: Control Data in User Interface

## Slide 46: Select Control Devices and Add New Control Device
Notes: In the user interface, click on the “Control Devices” link on the left hand side menu. Add data about new control device suc has control ID, control measure, operating status and status year, operating months, and percent control effectiveness.

## Slide 47: See New Control in List of Control Devices
Notes: After adding the control it can be seen in the list of existing control devices for the facility.

## Slide 48: Select Control Device and Add Pollutant Data
Notes: Click on the control device from the list, and it will open it again, now allowing you to add more data. Add pollutant and pollutant control efficiency.

## Slide 49: Select Control Paths and Add New Path
Notes: Click on “Control Paths” on the left hand side menu and this will take you to a list of existing paths. Click on the plus sign to add path data. Add path data. Control device effectiveness is the same as that for the control device for the case of a single control.

## Slide 50: See New Path in List of Paths
Notes: Click save and you’ll be able to see the path in the list of control paths.

## Slide 51: Select Path and Add Data
Notes: Click on the newly created path from the list of paths. Add Control Path assignment and pollutants

## Slide 52: Control/Path Assignment Data
Enter the sequence number for each control device in the path.
Note a child path may also have a sequence number.
Notes: Add control sequence number and the percentage of the pollutant stream coming from the process.

## Slide 53: Add Path Pollutants
Must contain all pollutants from all control devices.
Notes: Add control path pollutant information (pollutant and percent pollutant control reduction efficiency). Now your path information is complete.

## Slide 54: Select the Process for the Control Device
Notes: Now you need to tell the system which release points these emissions go to. Go to the process page by clicking on the unit and process you are looking for from the left hand side menu. Once in the page for that process, add a release point.

## Slide 55: Select Release Point for that Process
Notes: Add a release point apportionment. Or if a release point already exists there that you want to associate with the pollutant just click on it to edit it.

## Slide 56: Associate Process and Release Point
Notes: If your device capture isn’t 100% then you have fugitives and you would enter those as well.

## Slide 57: See Release Point(s) Linked to Process and Associated Paths
Notes: Note that release point apportionment of emissions from that process to its release point(s) should add up to 100% (i.e. all emissions from the process have to go somewhere).

## Slide 58: Option 1: Use Pre-Control Emission Factor
You must add control equipment to use the overall control %
Notes: Conversely you can select a “pre-control” emission factor and include an overall control %. If you chose that overall control % then your emissions will be calculated using that %.

## Slide 59: Option 2: Can Use Post-Control Emission Factor
If using post control factor, do not enter Overall Control %
Notes: If the “plus control efficiency” emission factor is available for the control, you can select it.

## Slide 60: Control Device in Bulk Upload

## Slide 61: Enter Data in Control Devices Tab
Notes: Click on the Control Devices tab. Data to enter includes the control description, percent control effectiveness, operating status and operating status year, and the control measure. Other data include control start, end date, and modification date if it has been modified.

## Slide 62: Enter Data in the Control Paths Tab
Notes: In the Control Paths tab enter the Path ID, description and percent control effectiveness. The effectiveness is the same as for the control device when there is only one control.

## Slide 63: Enter Data in the Control/Path Assignments Tab
Enter the sequence number for each control device in the path.
Note a child path may also have a sequence number within a parent path.
Notes: In the case of one control you only enter the control into the primary path.

## Slide 64: Enter Data in the Control/Path Apportionment Tab
Notes: In the apportionment tab, enter data for the release point such as the type, description and the apportionment from its path. In this example, Path A captures 85% of emissions and those are routed to Stack 1. 15% of emissions aren’t captured so they are apportioned to a fugitive release point.

## Slide 65: Enter All Pollutants for Each Control Device
Notes: Note that if your control device controls more than one pollutant, you should enter all of those pollutants here. In this case we show as an example, Toluene, which is a hazardous air pollutant.

## Slide 66: Enter Control Efficiency Control Device Pollutant Tab
Notes: In the Control Device Pollutant Tab enter the control ID and the pollutant and percent reduction efficiency.

## Slide 67: List Pollutants in Emissions Tab
Notes: Make sure that the same pollutants listed in the control, are listed in the process associated with it in the Emissions tab.

## Slide 68: Option to List Overall in the Emissions Tab
Option 1: If using post control factor, do not enter Overall Control %
Option 2: If entering Overall % use calculation method pre-controls.
Notes: Note that in the Emissions tab you can enter a pre-control emission factor and include the overall percentage control. When you upload the workbook CAERS will give you a QA check to recalculate your emissions.

## Slide 69: Considerations to Keep in Mind
Please don’t re-label or delete controls that existed in a previous year report, instead, mark them as “Permanently Shut Down” or your inventory in EPA will be out of sync.
You could enter your control data in UI to help guide you, then download in BU template to continue the rest of your report and vice-versa. Never work on both at the same time, BU will override UI.
Reach out to your SLT when you have questions.

## Slide 70: Examples for Different Configurations

## Slide 71: No Control Device Example
RP 3
B102
P102
Release Point RP3 Apportionment 95%
Release Point RP4 Apportionment 5%
RP 4
Indicates a Release Point Apportionment

## Slide 72: Single Control Device Example
RP 1
Control 1
B301
P301
RP 2
Path 1
Sequence # = 1
Release Point RP1 Apportionment 90%
Release Point RP2 Apportionment 10%
Control/Path Apportionment = 100%
Path 1 Reduction efficiency VOC = 96%
Path 1 Reduction effectiveness VOC = 98%
Effectiveness = 98%
Efficiency VOC = 96%
Overall Control % for VOC =
90% * 98% * 96% = 84.67%
Indicates a Release Point Apportionment
Indicates a Control Apportionment

## Slide 73: Example of Two Processes Sharing a Path
Planer
Planer Trim Block Hog
Planer Mill Cyclofilter
Path 1
Release Point
In this example we have two processes sending emissions into the Planer Mill Cyclofilter. Path 1 can be the primary path for the single control and can be used for both processes. Path 1 goes from the processes to the release point.
Path ID | Sequence Number | Control or Child Path Assignment | Assigned Control or Child Path Apportionment
Path 1 | 1 | Planer Mill Cyclofilter | 100%
Unit ID | Process ID | Path ID | Release Point ID | Release Point Apportionment
Planer | Process 1 | Path 1 | Stack 1 | 100%
Planer Trim Block Hog | Process 2 | Path 1 | Stack 1 | 100%
Paths
Release Points

## Slide 74: Pause for Single Control Device Q&A
If you only have one control device or single control device configurations in your facility, this concludes your training.
You are welcome to stay, and/or you may also refer to the remaining slides for further details.
The rest of the training is for reporters whose facilities have multiple controls.

## Slide 75: Example Facility with Many Configurations
RP 3
RP 1
Control 1
B301
P301
RP 2
B101
P101
Control 3
Control 2
B201
P201
Control 4
Control 5
RP 4
B102
P102
Indicates a Release Point Apportionment
Indicates a Control Apportionment

## Slide 76: Example of Paths for a Facility with Many Configurations
RP 3
RP 1
Control 1
B301
P301
RP 2
B101
P101
Control 3
Control 2
B201
P201
Control 4
Control 5
Path 1
Path 2
Path 3
RP 4
B102
P102
Indicates a Release Point Apportionment
Indicates a Control Apportionment

## Slide 77: Example Controls in Series
RP 1
RP 2
B101
P101
Control 3
Control 2
Path 2
Release Point RP1 Apportionment = 90%
Release Point RP2 Apportionment = 10%
Sequence # = 1
Sequence # = 2
Path Apportionment = 100%
Effectiveness = 95%
Efficiency SO2 = 95%
Effectiveness = 99%
Efficiency PM10 Fil = 93%
Efficiency PM2.5 Fil = 93%
Efficiency SO2 = 90%
Overall PM 10 Control % =
90% * 99% * 93% = 82.86%
Overall PM 2.5 Control % =
90% * 99% * 93% = 82.86%
PM 10 Fil & PM2.5 Fil: Assume calculation method was manufacturer specification (pre control) emission factor
SO2: Assume calculation method was pre-control plus control efficiency, then must assuming presence of both controls.
Path 2 Reduction efficiency
PM10 = 93%
PM2.5 = 93%
SO2 = 99.5% or (1-(1-0.95)*(1-0.9))*100
Path 2 effectiveness = 97% (average)
Control/Path Apportionment = 100%

## Slide 78: Example Controls in Parallel
RP 3
B201
P201
Control 4
Control 5
Path 3
RP 4
Sequence # = 1
Sequence # = 1
Release Point RP3 Apportionment 90%
Release Point RP4 Apportionment 10%
Path Apportionment = 50%
Effectiveness 98%
Efficiency VOC 95%
Effectiveness 97%
Efficiency VOC 95%
Path Apportionment = 50%
Overall VOC Control % =
90% * {[50% * (97% * 95%)]+ [50% * (98% * 95% )]} = 90% * (46.07% + 46.55%) = 83.35%
Path 3 Reduction efficiency
VOC = 95% (average of both controls)
Path 2 effectiveness = 97.5 (average of both controls)

## Slide 79: Overall Pollutant Control % for Multiple Controls
For more than one control for the same pollutant, then your overall control % may be:
In series for same pollutant: capture % * average effectiveness * [1- ((1-control1 pollutant reduction efficiency)*(1-control2 pollutant reduction efficiency) *…)]
In parallel for same pollutant: (overall controlled emissions 1 + overall controlled emissions 2+…)
Complex controls configuration for same pollutant, estimate (discuss with your SLT):
  For example, (controlled emissions in series + controlled emissions in parallel)/uncontrolled emissions
  For example, average, weighted average, depending on the control device configuration
Ensure you have used calculation methods that do not include controls (e.g., EPA factor no control device)

## Slide 80: Control Device Tab for this Example

## Slide 81: Control Paths Tab for this Example

## Slide 82: Control Assignments for this Example

## Slide 83: Control Device Pollutants for this Example

## Slide 84: Control Path Pollutants for this Example

## Slide 85: Release Point Apportionment for this Example

## Slide 86: Emissions for this Example

## Slide 87: Examples of More Complex Control Device Configurations

## Slide 88: In Series
Stack 3
Stack 2
Stack 1
Boiler 2
Control 1
Control 2
Control 3
Boiler 1
Path 1
Path 2
Process 1
Process 2
Control devices 1, 2, 3, and 4 are set up in sequence. Boiler and Process 2 send emissions to control 1. Boiler and process 1 send emissions to control 2. Path 1 is the primary path between Boiler and Process 1 to Stack 1. Path 2 is the primary path between boiler and process 2 and stack 1. Path 1 is a “child” path of Path 2. Path 2 is a “primary” path.
Control 4

## Slide 89: Numerical Example of Controls in Series and their Paths
Control 1
Path 1
Control 2
Control 3
Control 4
Path 2
Control ID | % Effectiveness | Pollutant | % Efficiency | Overall % Reduction
Control 1 | 95% | VOC | 80% | 76%
Control 1 | - | CO | 95% | 90%
Control 2 | 90% | PM10-PRI | 90% | 81%
Control 2 | - | PM-CON | 100% | 90%
Control 3 | 90% | NOX | 90% | 81%
Control 4 | 90% | SO2 | 90% | 81%
Path ID | Sequence Number | Assignment (Control or Path) | Apportionment (Control or Path)
Path 1 | 1 | Control 2 | 100%
Path 1 | 2 | Control 3 | 100%
Path 1 | 3 | Control 4 | 100%
Path 2 | 1 | Control 1 | 100%
Path 2 | 2 | Path 1 | 100%
Unit ID | Process ID | Path ID | Release Point ID | Release Point Apportionment
Boiler 1 | Process 1 | Path 1 | Stack 1 | 100%
Boiler 2 | Process 2 | Path 2 | Stack 1 | 100%
Controls
Paths
Release Points
In this example we assume 100% of emissions are routed to the release point (% capture = 100%, no fugitives).
Notes: The table shows how the different data elements would be entered in CAERS for this example. The numbers are fictious and are for illustration purposes only.

## Slide 90: In Parallel
Stack 3
Stack 2
Stack 1
Boiler 2
Control 1
Control 4
Control 2
Control 3
60%
40%
Control 5
Path 1
Path 2
47%
47%
Process 1
Path 1 is a child path of Path 2. Path 2 is a “primary path” between the process and Stack 3. Path 2 is a child path of Path 3. Path 3 is a “primary path” between the process and Stack 1.
Control 6
Path 3
Fugitive
3%
3%
Notes: 50% of total emissions from boiler 2 process 1 go to stack 3, the other 50% go to stack 1.

## Slide 91: Numerical Example of Controls in Parallel and Series
Control 1
Control 2
Control 4
Path 1
Control 3
Control 5
Path 2
Control 6
Path 3
Control ID | % Effectiveness | Pollutant | % Efficiency | Overall % Reduction
Control 1 | 95% | VOC | 80% | 68%
Control 2 | 90% | PM10-PRI | 90% | 81%
Control 2 | - | PM-CON | 100% | 90%
Control 3 | 90% | CO | 95% | 86%
Control 4 | 95% | NOX | 99% | 75%
Control 5 | 90% | Pb | 95% | 81%
Control 6 | 98% | SO2 | 97% | 95%
Controls
Notes: The new path method provides more detailed data. The table shows how the different data elements would be entered in CAERS for this example with a combination of controls in parallel. The numbers are fictious and are for illustration purposes only.

## Slide 92: Controls in Parallel and Series Paths and Release Points
Control 1
Control 2
Control 4
Path 1
Control 3
Control 5
Path 2
Control 6
Path 3
Path ID | Sequence Number | Assignment (Control or Path) | Apportionment (Control or Path)
Path 1 | 1 | Control 2 | 100%
Path 1 | 2 | Control 4 | 100%
Path 2 | 1 | Control 1 | 100%
Path 2 | 2 | Control 3 | 40%
Path 2 | 2 | Path 1 | 60%
Path 2 | 3 | Control 5 | 100%
Path 3 | 1 | Path 2 | 100%
Path 3 | 2 | Control 6 | 100%
Unit ID | Process ID | Path ID | Release Point ID | Release Point Apportionment
Boiler 2 | Process 1 | Path 2 | Stack 3 | 47%
Boiler 2 | Process 1 | Path 3 | Stack 1 | 47%
Boiler 2 | Process 1 | Path 2 | Fugitive | 3%
Boiler 2 | Process 1 | Path 3 | Fugitive | 3%
Paths
Release Points

## Slide 93: Example with a Back-Up Process
Tanks
Loading Rack
vapors
VRU (VOC)
Release Point
Liquid return
Bypass N/C
VCU (VOC, NOx, CO)
Propane
Release Point
1. The emissions only go to the VCU when the VRU is not working, per permit. The VCU is a backup to the VRU and was only used about 1% of 2019 or about 100 hours.
2. Only one runs at a time, taking 100% of the inlet/emissions.
3. Two different release points. A vent off the VRU, the VCU is a stack/flare.
4. Gasoline vapor is only emissions off the loading rack. So VCU emissions are VOCs. Because we use propane in the VRC it has VOC and NOx/CO.
Notes: In this example, the VRU is a vapor recovery unit. The VCU is a vapor combustion unit.

## Slide 94: VRU and VCU Example Continued
Process 1
VRU
VOCs
Path 1
Release point 1
Process 2
VOC, NOX and CO
Propane
VCU
Path 2
Release point 2
Process 1 (VOC)
Path 1:
VRU sequence 1
If individual control capture isn’t 100% then rel apportionment should be adjusted to reflect % going to fugitives.
Process 2 (VOC, NOX and CO)
Path 2
VCU Sequence 1
Recall VCU is a “backup” for the first process. When the VRU is offline, the VCU is running.

## Slide 95: We have three processes that feed two scrubbers and one common stack. Only two out of three processes operate at a time and only one scrubber is in service. Emission Factors for each scrubber may be different. How is this set up?
Stack Release Point
Process 1
Scrubber 1
Scrubber 2
Process 2
Process 3
If both scrubbers remove the same pollutant/s: Path 1 contains both scrubbers set up in parallel (both have sequence = 1 position).
Path 1
Example with Two Scrubbers

## Slide 96: Steps
Enter processes as normal, with their operating hours in operating details
Enter two control devices, one per scrubber in parallel and assuming an equal 50% split of the air stream between them, and enter individual values for the:
  control efficiencies (% removal of pollutant/s) - e.g. 99% for 1, and 95% for 2, and
  effectiveness (% the device operates as intended) – e.g. scrubber 1 operates 39% of the time, scrubber 2 operates 59% of the time
Put both controls in a path as running in parallel and enter path values: Path efficiency: 99% * 95% = 94.05%
Path Effectiveness = 39% + 59% = 98% - no control is 100% effective

## Slide 97: How to Get Help
Regardless of what help you need always send your SLT:
1. Facility name and ID
2. Screenshot(s) of error you are getting
3. BU template (if using) that is giving you errors
4. Diagram -even if by hand and scanned in- of the controls set up you have (especially for complex controls)
Steps:
1. If CAERS issue: Help Desk first (Click Help in UI top right of your screen)
2. If questions about calculations: Your SLT (they will elevate to EPA as needed)

## Slide 98: Questions