## Slide 1
Notes: Welcome to the Emergency Planning and Community Right-to-Know Act, Section 313, Toxics Release Inventory online training for the 2025 reporting year. This is the Advanced Concepts Module of a two-part training course that is made up of this module and a Basic Concepts module. The Advanced Concepts module assumes a basic understanding of the Toxics Release Inventory, or TRI, requirements and focuses on recent changes to the requirements as well as key concepts that will help to ensure accurate TRI reporting. The Basic Concepts module covers the process of determining whether or not your facility is required to report to TRI and, if so, how you prepare and submit information to TRI.

## Slide 2: TRI Training Module Agendas
Basic Concepts Module
  Covered Sectors
  Listed Chemicals and Activity Thresholds
  Reporting Exemptions
  Threshold Determination
  Overview of Form R
  Form R Calculation Examples
  Alternate Threshold Rule (Form A)
  TRI-MEweb Introduction
Advanced Concepts Module
  Recent TRI Program Changes
  Advanced Reporting Guidance
  Detailed Guidance for Chemicals of Special Concern
  Tools and Assistance
  TRI-MEweb
v
v
Notes: In this Advanced Concepts course we will cover: updates on recent changes to the TRI program; advanced guidance on threshold determinations and reporting; guidance on how to report for chemicals with special requirements, such as Chemicals of Special Concern; where you can go to get additional information and assistance with TRI requirements, including information on the EPA audit policy; and information on how to submit TRI Forms through TRI-MEweb on EPA’s Central Data Exchange (CDX).

## Slide 3: TRI Reporting Requirements
Notes: Let’s briefly review the process for determining if facility needs to report to TRI and how to report to TRI, which was covered in detail in the Basic Concepts Module.
To be required to report to TRI, your facility must meet the criteria shown here. A stepwise process can be used to determine if and what you would need to report to TRI. The first step is determining if your facility is covered under EPCRA Section 313 and would, therefore, need to consider its toxic chemicals for TRI reporting. Whether or not your facility is covered is based on the types of activities carried out at the facility and the number of employees working for your facility. NAICS is the North American Industry Classification System, which assigns numeric codes to characterize the activity taking place at the facility. We will talk more about the NAICS codes requirement shortly.
Alternatively, if your facility has been included in a determination by the EPA Administrator under their discretionary authority to extend reporting requirements to specific facilities, you need not consider your NAICS code or employees for the purposes of determining whether a TRI report is needed.
Then, if you’ve met one of the two criteria above (either are both in a covered sector AND have at least ten full-time employee-equivalents, OR were included in discretionary authority determination), then you proceed to the final step.
The next step is to determine for which TRI-listed chemicals you must submit a TRI report. Covered facilities need to look at the TRI-listed chemicals that may be present at the facility. Next, facilities need to look at how the chemicals are used. Are they manufactured? Processed? Or otherwise used? These are the TRI threshold activities. We will be describing each of these in more detail.
Next, facilities must calculate the quantity of the TRI-listed chemical that is manufactured, processed, or otherwise used, and compare those quantities to the TRI activity thresholds. Only when activity thresholds are exceeded would the facility be required to complete and submit a TRI report, either a Form R or a Form A.

## Slide 4: TRI Reporting Process
Notes: Completing your TRI forms is a two-step process. In the first step, you determine if your facility is required to report to TRI, and, if so, you determine which TRI-listed chemicals you handle in your facility, and then which of these you would need to report on.
Step 2, shown on the right, is the release and waste management reporting. This is the information that you would put on a TRI form. What information do facilities report to TRI? For the Form R, which is the more common means of TRI reporting, facilities report on how the TRI-listed chemical is managed as waste, including on-site releases, treatment, energy recovery, recycling of the TRI-listed chemical and off-site transfers, and pollution prevention activities that are conducted at the facility for that chemical.

## Slide 5: SECTION 1: RECENT TRI PROGRAM CHANGES

## Slide 6: TRI Program Changes Beginning RY 2025
Key program changes and changes to TRI Reporting Form R are listed in TRI-MEweb and in GuideME at
guideme.epa.gov/ords/guideme_ext/f?p=guideme:rfi-home#summary
Advanced TRI Reporting Concepts: Recent TRI Program Changes
Notes: It is very important to be aware of the program changes each year before preparing your TRI reports. Program changes can be found on the TRI Website at www.epa.gov/tri, and in GuideME. Program changes are also presented in TRI-MEweb, the TRI online reporting tool.

## Slide 7: TRI Program Changes Beginning RY 2024
PFAS as Chemicals of Special Concern and Supplier Notification Changes
  EPA published a final rule on October 31, 2023 (88 FR 74360) to classify all PFAS added to the TRI chemical list via the FY2020 NDAA as chemicals of special concern.
  This designation removes certain burden reduction options, including the de minimis exemption, the use of Form A, and limits the use of range reporting. The final rule also removes the use of the de minimis exemption for any chemical of special concern for the purpose of supplier notifications.
  This rule is effective beginning with RY 2024. Affected facilities should update their tracking of chemical activities involving PFAS accordingly. Find more information about the rule at: www.epa.gov/toxics-release-inventory-tri-program/changes-tri-reporting-requirements-and-polyfluoroalkyl
Advanced TRI Reporting Concepts: Recent TRI Program Changes
Notes: Effective for Reporting Year 2024, all TRI-listed PFAS are designated as Chemicals of Special Concern. These PFAS are subject to the same reporting requirements as other chemicals of special concern. They are no longer eligible for use of the de minimis exemption or the option for facilities to use the reporting Form A, and are also subject to limits on range reporting.
The rule also makes the de minimis exemption unavailable for purposes of supplier notification requirements to downstream facilities for all chemicals on the list of chemicals of special concern, which also includes certain persistent, bioaccumulative, toxic chemicals like lead, mercury, and dioxins. This change helps ensure that purchasers of mixtures and trade name products containing these chemicals are informed of their presence in mixtures and products they purchase.

## Slide 8: TRI Program Changes Beginning RY 2024
Per the requirements of 40 CFR §372.38(a), the de minimis levels for the following two chemicals have been changed from 1.0% to 0.1% since these chemicals are classified as carcinogens due to assessments by the International Agency for Research on Cancer (IARC):
Some cobalt compounds (N096): soluble cobalt(II) salts, cobalt(II) oxide
Some antimony compounds (N010): trivalent antimony
Advanced TRI Reporting Concepts: Recent TRI Program Changes
Notes: Effective for RY2024, de minimis levels for some cobalt and antimony compounds have been changed from 1.0% to 0.1%.

## Slide 9: Chemical List Changes: DINP Category
For RY 2024, EPA added a diisononyl phthalates (DINP) category to the TRI chemical list. This category includes branched alkyl di-esters of 1,2-benzenedicarboxylic acid in which alkyl ester moieties contain a total of nine carbons.
It includes but is not limited to the chemicals covered by the CAS Registry Numbers and names listed here:
Bis(3-ethylheptan-2-yl) benzene-1,2- dicarboxylate (111983-10-9)
Bis(7-methyloctyl) phthalate (20548-62-3)
Bis(3,5,5-trimethylhexyl) phthalate (14103-61-8)
Branched diisononyl phthalate (71549-78-5)
Di(C8–10, C9 rich) branched alkyl phthalates (68515-48-0)
Diisononyl phthalate (28553-12-0)
Advanced TRI Reporting Concepts: Recent TRI Program Changes
Notes:   EPA finalized a rule on July 14, 2023 (88 FR 45089) to add a diisononyl phthalates (DINP) category to the list of toxic chemicals subject to the TRI reporting requirements effective beginning RY 2024, with TRI forms due by July 1, 2025. The DINP category includes branched alkyl di-esters of 1,2-benzenedicarboxylic acid in which alkyl ester moieties contain a total of nine carbons. This category (N125) includes but is not limited to the chemicals covered by the CAS numbers and names listed here.

## Slide 10: Chemical List Changes: PFAS
Section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA) adds certain per- and polyfluoroalkyl substances (PFAS) to the TRI chemical list.
  Additional PFAS may be added to the TRI list for future reporting years due to the automatic addition of PFAS to the TRI list mandated by NDAA Section 7321(c) that occur under certain circumstances:
      EPA finalizing a toxicity value for a PFAS,
      Issuing certain Significant New Use Rules (SNURs) under TSCA for a PFAS, or adding a PFAS to certain existing SNURs,
      Adding a PFAS as an active chemical on the TSCA Inventory.
  PFAS are individually listed and subject to manufacturing, processing, and otherwise use reporting thresholds of 100 pounds.
  www.epa.gov/tri/pfas
Advanced TRI Reporting Concepts: Recent TRI Program Changes
Notes: Section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA) added per- and polyfluoroalkyl substances (PFAS) to the TRI list of reportable chemicals. Additional PFAS may be added to the TRI list for future reporting years due to the automatic addition of PFAS to the TRI list mandated by NDAA Section 7321(c) that occur under certain circumstances.

## Slide 11: Chemical List Changes: PFAS
Beginning RY 2025, nine PFAS have been added to the TRI chemical list, per the requirements of the NDAA.
These are:
Perfluoro-3-methoxypropanoic acid (377-73-1)
Ammonium perfluorodecanoate (PFDA NH4) (3108-42-7)
Sodium perfluorodecanoate (PFDA-Na) (3830-45-3)
6:2 Fluorotelomer sulfonate acid (27619-97-2)
6:2 Fluorotelomer sulfonate anion (425670-75-3)
6:2 Fluorotelomer sulfonate potassium salt (59587-38-1)
6:2 Fluorotelomer sulfonate ammonium salt (59587-39-2)
6:2 Fluorotelomer sulfonate sodium salt (27619-94-9)
Acetic acid, [(γ-ω-perfluoro-C8-10-alkyl)thio] derivs., Bu esters (3030471-22-5)
Advanced TRI Reporting Concepts: Recent TRI Program Changes
Notes: Per the requirements of section 7321 of the National Defense Authorization Act for Fiscal Year 2020 (NDAA), nine per- and polyfluoroalkyl substances (PFAS) have been added to the TRI list of reportable chemicals. These additions are effective for the 2025 TRI reporting year.

## Slide 12: SECTION 2: ADVANCED REPORTING GUIDANCE

## Slide 13: Chemicals with 25,000/10,000-pound Activity Thresholds
A TRI-covered facility must submit a reporting form for a TRI-listed chemical with 25,000/10,000-pound reporting threshold if it:
Manufactured (including imported)
more than 25,000 pounds of the chemical in the reporting year
Processed
more than 25,000 pounds of the chemical in the reporting year
Otherwise Used
more than 10,000 pounds of the chemical in the reporting year
OR
OR
Most of the 800+ chemicals and chemical categories on the TRI list have 25,000/10,000-pound activity thresholds.
Some have qualifiers (see the Reporting Forms and Instructions, Table II). Guidance documents for many chemicals are available at guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd-list#chemical.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Let’s briefly review the threshold quantities that would trigger TRI reporting. For chemicals that are not considered to be Chemicals of Special Concern, the thresholds for manufacturing are 25,000 pounds; for processing, 25,000 pounds; and for otherwise use, 10,000 pounds. These are the thresholds for most of the TRI-listed chemicals.
Certain TRI-listed chemicals in Table II of the Reporting Forms and Instructions have parenthetic “qualifiers.” These qualifiers indicate that these TRI-listed chemicals are subject to the section 313 reporting requirements if manufactured, processed, or otherwise used in a specific form or when a certain activity is performed.

## Slide 14: PFAS Activity Thresholds
A TRI-covered facility must submit a reporting form a TRI-listed PFAS if it:
Manufactured (including imported)
more than 100 pounds of the chemical in the reporting year
Processed
more than 100 pounds of the chemical in the reporting year
Otherwise Used
more than 100 pounds of the chemical in the reporting year
OR
OR
205 TRI-listed PFAS are reportable for RY 2025.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: For chemicals that are per- or poly-fluoroalkyl substances (PFAS), the thresholds for manufacturing, processing, and otherwise use are 100 pounds.

## Slide 15: Chemicals of Special Concern and Activity Thresholds
Chemicals of special concern are subject to separate, lower activity thresholds. (40 CFR § 372.28)
100 lb/yr (manufactured, processed, or otherwise used):
  Aldrin
  Hexabromocyclododecane
  Lead*
  Lead compounds
  Pendimethalin
  PFAS
  Polycyclic aromatic compounds
  Tetrabromobisphenol A
  Trifluralin
  Methoxychlor
  1,3,4,6,7,8-Hexahydro-4,6,6,7,8,8-hexamethylcyclopenta[g]-2-benzopyran
10 lb/yr (manufactured, processed, or otherwise used):
  Chlordane
  Heptachlor
  Mercury
  Toxaphene
  Isodrin
  Polychlorinated biphenyls
  Benzo[g,h,i]perylene
  Hexachlorobenzene
  Mercury compounds
  Octachlorostyrene
  Pentachlorobenzene
0.1 g/yr (manufactured, processed, or otherwise used):
  Dioxin and dioxin-like compounds
*Excluding lead in stainless steel, brass, or bronze alloys
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: The actual threshold quantities that trigger reporting vary depending on the chemical. For some of the chemicals, the thresholds are 100 pounds per year. For those chemicals that are considered highly persistent and bioaccumulative, the thresholds are 10 pounds per year. And for dioxin and dioxin-like compounds, the thresholds are 0.1 grams per year, which reflects the highly toxic nature of this chemical category.

## Slide 16: Threshold Guidance
The following activities are not considered “manufacturing,” “processing,” or “otherwise use”:
Remediation
  Chemicals being remediated are not manufactured, processed, or otherwise used.
  Chemicals used to remediate waste ARE counted as otherwise used.
  Chemicals manufactured when treating or remediating waste ARE counted toward the manufacturing threshold
Treatment of wastes generated on site
  Wastes brought in from off site for treatment or other management count towards the otherwise use threshold.
Storage
Recycling on site for use on site
Transferring chemicals off-site for further waste management (except off-site transfers for recycling)
  Chemicals sent off-site for recycling are counted as processed.
These activities do not constitute threshold activities but are not exempt from reporting if a threshold is exceeded through other activities unless specifically eligible for one of the reporting exemptions.
Chemicals coincidentally manufactured during waste treatment or remediation must be considered.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Now we will go over some reminders regarding threshold calculations. Facilities should be aware that there are some activities that are not considered to be threshold activities under TRI. In other words, the activities are not considered manufacturing, processing, or otherwise use. None of the TRI-listed chemicals undergoing these activities would need to be considered towards an activity threshold. These activities are shown here and include: remediating chemicals; treating chemicals in waste generated on-site; storing chemicals; recycling on-site for use on-site; and transfers sent off-site for further waste management, not including recycling.
For example, let’s say a facility stores 50,000 pounds of a chemical on-site. The act of just storing that chemical is not a threshold activity. It’s not manufacturing. It’s not processing. It’s not otherwise use. However, the fact that they are storing the chemical on-site probably means that they are also using it in their process. At some point they will pull quantities out of storage and process or otherwise use it in their production process. At that point, they are processing the quantity of the chemical removed from storage, and that quantity gets counted towards their processing threshold. However, if the facility were to stop making a certain product line and continued to store the chemical for the reporting year and never used it, they would not need to consider it towards any threshold.
Facilities should be aware that while these activities are not threshold activities, that is not the same as being exempt from TRI. The activities listed here are not exempt from reporting; but they are not counted toward the threshold determination. However, if a TRI activity threshold is exceeded in some other manner at the facility, then the reporting requirement has been triggered, and any release or waste management associated with the non-threshold activities must be included in the reported quantities for release and waste management for the chemical.
Also, note that TRI chemicals that are coincidentally manufactured, or unintentionally manufactured, during waste treatment or remediation must be considered in manufacturing threshold amounts.

## Slide 17: Threshold Guidance: Combustion
TRI-listed chemicals may be coincidentally manufactured during combustion of:
  Oil
  Coal
  Natural gas
  Waste
  Other materials
Includes acid aerosols and metal compounds manufactured as by-products of fuel combustion.
Any TRI-listed chemicals in fuels combusted for energy are considered otherwise used.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Some industrial activities may involve more than one TRI threshold activity. For example, combustion may exceed thresholds for both manufacture and otherwise use. Here is some guidance on combustion. Many facilities have on-site combustion processes where TRI-listed chemicals may be present in fuels used, and may be coincidentally manufactured during the combustion of oil, coal, natural gas, waste or other materials. Any TRI-listed chemical in the fuel is considered otherwise used and the quantity would be applied towards the otherwise use threshold. Any TRI-listed chemical generated when the fuel is combusted is considered coincidentally manufactured and the quantity would be applied to the manufacturing threshold. TRI-listed chemicals commonly coincidentally manufactured during combustion include acid aerosols, such as sulfuric acid aerosols. Metal compounds are also coincidentally manufactured as byproducts of fuel combustion.
So, when combusting fuels and other materials, be sure to consider both aspects of the combustion process: How much of each TRI-listed chemical is otherwise used, and how much is manufactured?
Note that the non-Chemicals of Special Concern in the fuel otherwise used are eligible for the de minimis exemption, and many of the TRI-listed chemicals found in fuels ARE present below de minimis concentrations. However, TRI-listed chemicals that are coincidentally manufactured during combustion are not eligible for the de minimis exemption.

## Slide 18: Exemptions
TRI regulations provide exemptions for specific scenarios.
These exemptions allow a facility to not consider quantities of TRI-listed chemicals for certain threshold determinations and waste management calculations.
More about TRI exemptions:
  guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd-list#exemption
Exemption List
Articles
De Minimis
Coal Extraction
Intake Air and Water
Laboratory Activities
Janitorial or Facility Grounds Maintenance
Metal Mining Overburden
Motor Vehicle Maintenance
Operators of Establishments on Leased Property
Owners of Leased Property
Personal Use
Structural Component of the Facility
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: TRI regulations provide exemptions for specific scenarios. These exemptions allow for a facility to not consider quantities of toxic chemicals for certain threshold determinations and waste management calculations. The available exemptions are listed on this slide. To learn more about TRI exemptions, please visit the website shown on this slide. The website includes a summary of each exemption and links to exemption-specific guidance.

## Slide 19: Exemption Guidance
Reminder:
  Even where your activity is covered by an “otherwise use” exemption such as motor vehicle maintenance, if TRI-listed chemicals are manufactured as by-products, coincidentally as impurities, or otherwise manufactured, they must be considered toward the manufacturing threshold.
  TRI-listed chemicals in fuels added to motor vehicles as part of the facility’s service or product do not qualify for the motor vehicle maintenance exemption.
  The laboratory activities exemption only applies to certain activities that take place in a laboratory, and they must be under the direct supervision of a technically qualified individual.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: The Basics Concepts module of the online training goes into more detail on each of the TRI exemptions, but here we have a few reminders.
Any TRI-listed chemicals contained in fuels combusted are otherwise used and count toward the otherwise use threshold. And those TRI-listed chemicals coincidentally manufactured during combustion must be considered towards the manufacturing threshold. This is true even if the activity is covered by an “otherwise use" exemption such as motor vehicle maintenance. If TRI chemicals are manufactured as by-products, coincidentally as impurities, or otherwise manufactured, they must be considered toward the manufacturing threshold.
Only TRI-listed chemicals in fuels added to motor vehicles operated exclusively by the facility qualify for the motor vehicle maintenance exemption. Other TRI-listed chemicals would count towards the processing threshold and this exemption only applies to the otherwise use of TRI-listed chemicals. For example, some facilities that manufacture vehicles add a few gallons of fuel before the vehicles leave the facility for distribution into commerce. Because those vehicles and the fuel in them are part of the facility’s product going into commerce, the TRI-listed chemicals in the fuel are considered processed.
Similarly, the laboratory activities exemption applies to TRI-listed chemicals that are manufactured, processed, or otherwise used in certain activities that take place in a laboratory. Facilities should take care not to apply this exemption more broadly than it should be. If an activity involving a TRI-listed chemical takes place in a laboratory, it does NOT mean that it is necessarily exempt. Only certain activities are exempt.

## Slide 20: Metals and Metal Compound Category
Elemental metals (metals in their neutral state) and their corresponding metal compound categories are listed separately under Section 313.
  These have separate activity threshold determinations.
  Report for each listing (e.g., nickel or nickel compound) only if a threshold for each listing is exceeded.
  For metal compounds calculations:
    Use full compound mass for threshold determination.
    Use only parent metal mass for release and waste quantities.
  If threshold is exceeded for both the elemental metal and metal category compound (e.g., nickel and nickel compounds), you may report separately or submit one combined report.
    If combined, file as metal and metal category compound.
    The elemental metal and its compound may be reported on the same form because while the entire weight of the compound is used to determine the threshold, only the amounts of the parent metal are reported.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Now we will move on to some other chemicals that have unique reporting requirements for which reporting errors more frequently occur. First, let’s look at the unique requirements associated with reporting for metals and metal compound categories. Note that metals and metal category compounds are separately listed under TRI. They each have a separate activity threshold determination – report on the metal only if the threshold for the metal is exceeded, and report for the metal compound only if the threshold for the metal compound is exceeded.
So if a facility handles elemental nickel and nickel compounds at their facility, they should look at the two separately when determining if they need to report. They look at the elemental nickel and see if they manufacture, process, or otherwise use quantities exceeding a threshold for nickel. Separately, they look at their nickel compounds and see if the quantity manufactured, processed, or otherwise used exceeds a threshold for nickel compounds. They look at the two as unrelated chemicals.
However, if the thresholds are exceeded for both the elemental metal and for the metal compound – for example, both for nickel and for nickel compounds, then the facility may submit two separate reports or one combined report for the compound category. Combined reports for elemental metals and metal compounds will need to indicate they are reporting for both under this combined form. So, if the facility exceeded the threshold for nickel and they exceeded the threshold for nickel compounds, they could file a combined report for both elemental nickel and nickel compounds.

## Slide 21: Cyanide Compounds and Hydrogen Cyanide
Cyanide compounds have the form X+CN- where X = any other group (except H+) where a formal dissociation can be made. For example, KCN or Ca(CN)2
  Includes metal (cyanometalates, such as ferricyanides) and non-metal (such as ammonium cyanide) dissociative cyanide complexes.
  For threshold determinations, use weight of the entire compound.
  For release and other waste management reporting, report weight of entire compound.
Hydrogen cyanide (74-90-8)
  An individually-listed toxic chemical.
  The Corrections to TRI Reporting Requirements rule clarified that hydrogen cyanide is not part of the cyanide compounds category.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Cyanide compounds are a listed chemical category, which includes the cyanide ion and any group where a formal dissociation can be made. When reporting for cyanide compounds, the full weight of the compound must be used for both threshold determinations as well as releases and other waste management reporting. This requirement is different from that of metal compound categories and nitrate compound categories where only the metal or nitrate ion is included for calculating releases and other waste management.
Hydrogen cyanide is an individually-listed chemical. While hydrogen cyanide meets the structural definition of cyanide compounds, current EPA guidance is to not count hydrogen cyanide as part of cyanide compounds for thresholds and release and waste management reporting.

## Slide 22: Metal Cyanide Compound Guidance
A metal cyanide compound, such as cadmium cyanide, requires separate reporting under both the corresponding metal category compound and cyanide compounds*.
For reporting the metal category compounds, such as cadmium compounds:
  For threshold determinations, use entire weight of compound.
  For release and other waste management reporting, report only the weight of metal portion of the compound.
For cyanide compounds:
  For threshold determinations, use weight of entire compound.
  For release and other waste management reporting, report weight of entire compound.
*Category description for cyanide compounds states: X+CN- where X+ = any group (except H+) where a formal dissociation can be made. For example, KCN or Ca(CN)2
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Metal cyanide compounds, more formally called cyanometalates, are reportable under both the metal compound categories and the cyanide compounds category. Facilities that manufacture, process, or otherwise use a metal cyanide compound need to consider if they exceed a threshold for the cyanide compound category and also for the corresponding metal compound category.
For example, if a facility processes cadmium cyanide, they need to consider if reporting is required for both cadmium compounds and cyanide compounds. In this example, they would use the entire weight of the cadmium cyanide for the cadmium compound category threshold determination and only the weight of the metal portion of the cadmium for the release and waste management reporting. For the cyanide compounds category, they would also use the entire weight for the cadmium cyanide in the threshold determination, just like for the metal compound. However, for the release and other weight management reporting, they also use the entire weight of the cadmium cyanide for reporting under the cyanide compounds category.

## Slide 23: Nitrate Compounds Category
Qualifier: “Water dissociable; reportable only when in aqueous solution”
  For threshold determinations, use weight of entire nitrate compound.
  Calculate only weight of nitrate ion portion when reporting releases and other waste management quantities on the Form R.
Common nitrate compounds sources
  Nitrate compounds are produced most commonly when nitric acid is neutralized or in biological treatment of wastewater.
  Nitrate compound releases to surface water may result from stormwater runoff.
  Exemption may apply for nitrates in intake water (used for processing or non-contact cooling).
v
v
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: The nitrate compounds category also deserves special consideration.
The TRI chemical category is actually ‘water dissociable nitrate compounds’. So, nitrate compounds are only reportable when they are in an aqueous solution.
Nitrate compounds are treated much like metal compounds under TRI. When calculating whether a reporting threshold was exceeded, facilities use the weight of the entire nitrate compound to see if they have manufactured or processed more than 25,000 pounds, or otherwise used more than 10,000 pounds.
If one of these thresholds is exceeded, a TRI form is required. When estimating the quantities released or managed as waste, use only the weight of the nitrate ion portion of the compound. A common error is using the whole weight of the nitrate compound in the release and waste management estimates, and thereby, over-reporting the quantities released or the quantities managed as waste.
Nitrate compounds are most commonly produced when nitric acid is neutralized, or in biological treatment of wastewater. Note that there is an exemption for the otherwise use of TRI chemicals contained in intake water that is used for processing or non-contact cooling.

## Slide 24: Quiz #1: Question 1
A facility processes 200,000 lb of a mixture containing 10% zinc chromate and 15% chromium dioxide by weight.
For which of the following chemical categories was the processing threshold exceeded?
A. Chromium compounds only
B. Zinc compounds only
C. Neither
D. Both
Advanced TRI Reporting Concepts: Advanced Reporting Guidance

## Slide 25: Quiz #1: Question 2
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby waterbody.
The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. One mole of HNO3 generates one mole of NaNO3.
Does the facility exceed the manufacturing threshold for nitrate compounds?
Select Yes or No
Advanced TRI Reporting Concepts: Advanced Reporting Guidance

## Slide 26: Quiz #1: Question 3
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby waterbody.
The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. One mole of HNO3 generates one mole of NaNO3. The MW of the nitrate ion NO3 = 62.
In this example, should the facility report release of 27,000 lb of nitrate compounds into a stream or waterbody (Section 5.3 on Form R)?
Select Yes or No
Advanced TRI Reporting Concepts: Advanced Reporting Guidance

## Slide 27: Ammonia Guidance
Ammonia
  Aqueous ammonia: threshold determination and release and other waste management quantity calculations for aqueous ammonia from any source (i.e., anhydrous ammonia placed in water or water dissociable ammonium salts) is based on 10% of the total ammonia present in aqueous solutions.
  Anhydrous ammonia: include 100% for threshold determinations and release calculations
    Including air releases from aqueous ammonia
  Amounts from aqueous sources and anhydrous sources get added together for threshold determinations and ammonia release reporting.
v
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Ammonia also has some unique requirements. For aqueous ammonia, your threshold determination and your release and waste management quantity calculations are based on 10% of the ammonia present in the aqueous solutions. Remember that the 10% applies only to aqueous solutions. If you have anhydrous ammonia you need to consider 100% for threshold determinations and release calculations.

## Slide 28: Ammonia Calculation Examples
In a calendar year, a facility places 25,000 pounds of anhydrous ammonia in water for processing and processes 25,000 pounds of aqueous ammonia from an ammonium salt.
The facility must include all 25,000 pounds of anhydrous ammonia in the determination of the processing threshold, but only 10 percent (or 2,500 pounds) of the aqueous ammonia from the ammonium salt in the processing threshold determination.
In a calendar year, a facility uses 30,000 pounds of anhydrous ammonia to neutralize acids in a wastewater stream. The neutralized waste stream (containing aqueous ammonia from dissociated ammonium salts) is then transferred to a POTW.
The quantity to be applied toward threshold determinations is the total quantity of anhydrous ammonia used in the waste stream neutralization, or 30,000 pounds. The quantity of ammonia reported as transferred is 10 percent of the total quantity of aqueous ammonia transferred, or 3,000 pounds.
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Two examples of calculating thresholds and releases of anhydrous and aqueous ammonia are provided on the slide. These examples are from the Ammonia guidance document.

## Slide 29: Acid Aerosols
Hydrochloric and sulfuric acids are only reportable if in the aerosol form.
  These aerosols are common products of coal and other fuels combustion.
  Includes mists, vapors, gas, fog, and other airborne forms of any particle size.
Threshold determination for closed-loop reuse systems that generate acid aerosol:
  Acid aerosols are manufactured and otherwise used.
  Applicable for sulfuric and hydrochloric acid only.
Total Amount of Acid in Reuse System
Total Virgin Acid Added in RY
=
Amount Acid Aerosols Manufactured/ Otherwise Used
Closed-loop Acid Reuse System
+
* See EPA’s Guidance for Reporting Sulfuric Acid and Guidance for Reporting Hydrochloric Acid for specific calculations
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Acid aerosols are also chemicals with unique requirements. Note that both hydrochloric and sulfuric acids have a chemical qualifier that specifies that they are reportable only if they are in the aerosol form. These aerosols are common products of coal and other fuel combustion. For example, sulfuric acid can be coincidentally manufactured when combusting fuels containing sulfur.
Hydrochloric and sulfuric acids are also used by facilities in closed-loop acid reuse systems. In some cases, the acid can be aerosolized to apply it to a material or product for the purpose of etching or cleaning. The acid aerosol is typically condensed back to liquid only to be re-aerosolized again and again. Because of the chemical qualifier, facilities would be manufacturing the TRI chemical every time it is aerosolized and otherwise using it again and again in the process.
EPA developed a simplified method for determining whether a threshold has been exceeded. The guidance directs facilities to calculate their threshold quantity by adding the total amount of acid in the reuse system plus the total virgin acid added in the reporting year to get the threshold quantity manufactured and otherwise used.
EPA has developed two separate reporting guidance documents for sulfuric acid and hydrochloric acid where facilities can get more information pertaining to these chemicals.

## Slide 30: Chemical Migration Guidance
How to report migration of a TRI-listed chemical contained in waste disposed or released from one environmental medium to another within the reporting year:
  For example, volatilization from a landfill
  Release estimates must be calculated and reported for all media in Part II, Sections 5, 6, and 8 of Form R.
1,000 lb to air
(Form R: 1,000 lb in Section 5.1)
2,000 lb to surface impoundment
(Form R: 1,000 lb in Section 5.5.3B)
Year 1
Year 1
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Now we will discuss EPA’s Guidance on how to report chemicals that migrate from their initial disposal or release location. Shown is an example of a reportable chemical that is disposed of in an on-site surface impoundment.
If in Year One, a facility placed 2,000 pounds of the chemical into a surface impoundment, and in the same year, 1,000 pounds volatilized to the air, the facility would put the 1,000 pounds released to air on their Form R. And 1,000 pounds would be reported on the Form R as disposed of in the surface impoundment, not 2,000 pounds.
When the initial disposal and subsequent migration occur during the same reporting year, facilities should put each amount in the appropriate section of the form to show the medium in which it actually ended up.

## Slide 31: Chemical Migration Guidance
How to report migration of a TRI-listed chemical contained in waste disposed or released from one environmental medium to another within the reporting year:
  For example, leachate from a landfill
  Release estimates must be calculated and reported for all media in Part II, Sections 5, 6, and 8 of Form R.
500 lb leachate in year 2
Not reported on Year 2 Form R
2,000 lb to surface impoundment
(Form R, Section 5.5.3B)
Year 1
Year 2
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: However, if chemical migration occurs in a subsequent year from the initial disposal, the chemical migration should not be reported. Facilities are only required to report amounts released or otherwise managed in the year that the amounts were released or otherwise managed.
For example, in Year One, 2,000 pounds of this chemical were disposed of in the on-site surface impoundment. That 2,000 pounds will go on your Form R as an on-site land disposal, under the surface impoundment section. A year later, leachate has migrated from this surface impoundment, and you know that 500 pounds of the original 2,000 pounds has migrated out of the impoundment. Because the migration occurred in a different reporting year, the 500 pounds does not get reported on the Year Two Form at all. It was already reported the previous year in the 2,000 pounds disposed to land on-site.

## Slide 32: EPA Compliance Incentives
July 1 is the TRI reporting deadline. Facilities have a legal obligation to file an accurate and complete Form R or Form A for each chemical by July 1 each year. EPA may take enforcement action and assess civil administrative penalties regarding corrections to errors on Form Rs that are not changes based on previously unavailable information or procedures that improve the accuracy of the data initially reported.
The Agency implements policies that reduce or waive penalties under certain conditions for facilities that discover, disclose, correct, and prevent future violations.
Current Compliance Incentive Policies, Guidance, and Audit Protocols:
  www.epa.gov/compliance/audit-protocols
V v
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Facilities are reminded that they have a legal obligation under EPCRA to submit accurate TRI reporting forms by July 1, if they met TRI reporting requirements for the prior reporting year. If facilities do not submit accurate and timely forms by the reporting deadline, EPA may take enforcement action.
Compliance Incentives are a set of policies and programs that eliminate, reduce, or waive penalties under certain conditions for business, industry, and government facilities which voluntarily discover, promptly disclose, correct noncompliance, and prevent future environmental violations. Information about these incentives, self-disclosure programs, related tools such as environmental audit protocols, Environmental Management Systems, Pollution Prevention, other innovation projects and programs and the environmental benefits achieved by such programs can be found at the website shown here.

## Slide 33: EPA Self-Disclosure Audit Policy
Conditions to qualify (nine criteria):
Systematic Discovery of the Violation Through Environmental Audit or the Implementation of a Compliance Management System
Voluntary Discovery
Prompt Disclosure
Discovery and Disclosure Independent of Government or Third-Party Plaintiff
Correction and Remediation
Prevent Recurrence
No Repeat Violations
Other Violations Excluded
Cooperation
For more information, including a copy of the Audit Policy, visit:
  www.epa.gov/compliance/epas-audit-policy
v
1
v
2
v
3
v
4
v
5
v
7
v
8
v
9
v
6
V v
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Conditions to qualify for the Audit Policy are as follows. The violation had to be from a systematic discovery through an environmental audit or due diligence. It has to have been a voluntary discovery made by the facility. The facility must promptly disclose the violation to the Environmental Protection Agency and the discovery and disclosure must be independent of a government or third-party plaintiff.
The facility must fix the problem to prevent it from recurring and this audit policy cannot be used repeatedly for the same violations. It only covers the violations for which you are reporting. If other violations are identified over the course of using the audit policy, they may not be covered. You have to cooperate fully with the EPA and other authorities. More details on the audit policy are available from the EPA Website at the address shown here.

## Slide 34: EPA Self-Disclosure Audit Policy
EPA Compliance Incentive Policy is available only to small businesses
  Small businesses employ 100 or fewer individuals across all facilities and operations.
Small businesses that meet all four conditions of the policy may have 100% of the gravity-based penalty waived. However, EPA reserves the option to collect any significant economic benefit that may have been realized by the facility.
Four Qualification Conditions:
Good Compliance Record
Voluntary Discovery
Prompt Disclosure
Correction and Remediation
v
1
v
2
v
3
v
4
V v
For more information, including a copy of the Small Business Compliance Policy and a Q&A document, visit:
  www.epa.gov/compliance/small-business-compliance
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: EPA offers a compliance incentive policy to small businesses that self-disclose violations. The Small Business Compliance Policy is only available to businesses with 100 or fewer employees. If a small business meets the conditions, they may be eligible for 100 percent reduction in the gravity-based penalty. The conditions to qualify are: a good compliance record, voluntary discovery of the violation, prompt disclosure, and correction and remediation of the violation. More information on the Small Business Compliance Policy can be found at the website shown here.

## Slide 35: Submitting Revisions and Withdrawals
To replace a previously submitted Form A Certification Statement with a Form R: .
  You must withdraw the previously filed Form A Certification Statement and then submit a Form R. EPA will consider the Form R to be a late submission if submitted after the July 1 reporting deadline.
To change what chemical is being reported (including a metal to a metal compound):
  You must withdraw the original submission and re-submit for the new chemical. This is not a revision.
EPA may audit reporting form revisions or withdrawals at any time.
V v
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Here are a few more reminders regarding revisions and withdrawals. Submitting a Form R to replace a previously filed Form A is not considered a revision (do not check the revision box). It is considered a late submission of Form R. You would also need to request that the Form A be withdrawn.
Note that submitting a Form A when a Form R is required is considered a less severe violation than failing to submit either form, but it is considered a late submission if submitted after the reporting deadline.
A common revision is to change the chemical reported from a metal to a metal compound or vice versa. In that case, the original submission must be withdrawn and the form for the new chemical should be submitted. This is not considered a revision.

## Slide 36: EPCRA Section 313 Enforcement
Owners and operators of covered facilities violating any statutory or regulatory requirement are subject to penalties of up to $40,779 per day per violation (periodically adjusted for inflation).
Owners and operators of covered facilities subject to citizen suits could also be liable for attorney fees and litigation costs (EPCRA § 326(f)).
Government’s penalty for Section 313 of EPCRA is determined by applying the statutory penalty factors as described in the Enforcement Response Policy (ERP) to each violation.
  For EPA’s EPCRA enforcement policies, see:
    www.epa.gov/sites/production/files/2017-03/documents/epcra313erpamendments2017.pdf
Advanced TRI Reporting Concepts: Advanced Reporting Guidance
Notes: Companies violating any statutory or regulatory requirement are subject to penalties of up to $40,779 per day per violation. The government’s Enforcement Response Policy is what is used to determine what the penalty will be. More information on EPA EPCRA enforcement policies can be found at the website shown here.

## Slide 37: SECTION 3: DETAILED GUIDANCE FOR CHEMICALS OF SPECIAL CONCERN

## Slide 38: Chemicals of Special Concern
Organic Compounds:
  Benzo[g,h,i]perylene, Dioxin and dioxin-like compounds category, Hexabromocyclododecane, Hexachlorobenzene, 1,3,4,6,7,8-Hexahydro-4,6,6,7,8,8-hexamethylcyclopenta[g]-2-benzopyran, Octachlorostyrene, Pentachlorobenzene, Polycyclic aromatic compounds (PAC) category, Polychlorinated biphenyls, and Tetrabromobisphenol A
Metals and Metal Compounds:
  Mercury, Mercury compounds category, Lead, and Lead compounds category
Pesticides:
  Aldrin, Chlordane, Heptachlor, Isodrin, Methoxychlor, Pendimethalin, Toxaphene, Trifluralin
PFAS
Chemicals of special concern are subject to separate, lower reporting thresholds and different reporting requirements than the other TRI chemicals.
  Facilities must use Form R (cannot use Form A)
  Quantities can be reported to decimal amounts
  Cannot use range codes for release reporting
  Cannot use the de minimis exemption
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Chemicals of Special Concern include chemicals that are persistent, bioaccumulative, and toxic (PBTs), meaning that they’re persistent in that they don’t break down in the environment. They’re bioaccumulative in that they tend to accumulate in living tissue, and they’re toxic chemicals. Because of these characteristics, these chemicals have much lower reporting thresholds and they have unique reporting requirements under TRI.
Here are the PFAS and non-PFAS chemicals and chemical categories that are designated as Chemicals of Special Concern. Of the non-PFAS, nine are organic compounds, two are metals and two are metal compounds, and eight are pesticides. Several of these Chemicals of Special Concern are either banned or severely limited in their use.
The threshold quantity that would trigger reporting for Chemicals of Special Concern varies depending upon the individual chemical. However, when reporting for any of the Chemicals of Special Concern the Form R must be used, quantities reported can include decimal amounts, range codes are not allowed, and you cannot use the de minimis exemption.

## Slide 39: Dioxin and Dioxin-like Compounds
Dioxin and dioxin-like compounds are reported in grams.
The manufacture, process, or otherwise used activity thresholds are 0.1 grams.
Dioxins can be formed as unwanted by-products when chlorinated materials are involved in combustion or other high-temperature processes, such as:
  Fossil fuel and wood combustion
  Waste incineration
  Metallurgical processes
What does it take to exceed the 0.1-gram activity threshold?
  64,462 tons of coal combusted in a utility boiler
  8.31 million gallons of fuel oil combusted in a utility boiler
  1,230 tons of copper scrap fed to a secondary copper smelter
v
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: “Dioxin and Dioxin-like Compounds” is a Chemicals of Special Concern category and, unlike any other TRI chemicals, dioxin and dioxin like compounds are reported using gram units. The dioxin and dioxin-like compound category has a Chemicals of Special Concern activity threshold of 0.1 grams for a reporting year. Facilities manufacturing, processing or otherwise using 1/10th of a gram of dioxin or dioxin-like compounds, would report for this chemical category.
Dioxins can be formed as byproducts when chlorinated materials are involved in combustion or other high-temperature processes. Examples of such processes where dioxins may form includes: fossil fuel and wood combustion, waste incineration, or metallurgical processes.
What does it take to exceed a 0.1-gram activity threshold? The list shown here is from the dioxin and dioxin-like compounds guidance document. Using typical concentrations, 64,462 tons of coal combusted in a utility boiler in the reporting year would exceed the dioxin threshold. 8.31 million gallons of fuel combusted would exceed the threshold, again, at typical concentrations of dioxins. Or 1,230 tons of copper scrap fed into a secondary copper smelter would exceed the dioxin threshold.

## Slide 40: Dioxin and Dioxin-like Compounds
Dioxin and dioxin-like compounds category is composed of 17 specific compounds.
  In addition to the total mass grams released for the entire chemical category, facilities that have the data are required to report the quantity of each of the 17 individual members, which must add up to the total mass for the category.
Dioxin and Dioxin-like Compounds Toxicity Equivalency (TEQ)
  Each compound has an assigned Toxic Equivalency Factor (TEF) that is multiplied with the compound mass to yield TEQ.
  TEQ for each of the compounds are summed to provide a category TEQ.
  TEQ values are made available to the public along with mass data.
Emission factors, listed compounds, TEFs, and other guidance:
  guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd-title:::::title:dioxin
v
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: The dioxin and dioxin-like compounds category is composed of 17 individually listed compounds.
In addition to reporting the total amount of this chemical category in grams, facilities must also report the quantity in grams of each of the 17 individual compounds in the category, if this information is available. Emission factors for dioxin and dioxin-line compounds are typically for individual compounds within the category.
EPA will use the quantities reported to calculate the Toxicity Equivalency Values, or TEQ values, for the dioxin and dioxin-like compounds reported. This information will be made available to the public along with the mass values reported. The dioxin and dioxin-like compounds guidance document has additional information about this category, including the listed chemicals and commonly used emission factors.

## Slide 41: Lead and Lead Compounds
Raw materials processed by a variety of facilities may contain metallic lead or lead compounds:
  Metal ores
  Coal
  Wood
  Oil & Oil products: heating oils, gasolines
Lead used in solder and other alloys is in the elemental NOT the compound form (i.e., this is lead, not a lead compound).
Lead-acid batteries will typically meet the articles exemption.
Sending old paint containing lead off site for disposal or treatment is not a threshold activity.
Other sources of lead and lead compounds for Chemicals of Special Concern threshold:
  Lead solder, lead babbitt, castings/molds, contaminants of aluminum and other common base alloys, X-Ray film
  Cement, asphalt, graphite brushes, leaded glass
  Transfers of lead and lead compounds off-site for recycling
v
Pb
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: “Lead and Lead Compounds” can be found in a variety of raw materials, such as in metal ores, coal, wood, and in oil products such as heating oils and gasoline.
Lead is also found in circuit board facilities where it is used as solder. And, lead is found in many metal alloys. Lead in solder and alloys is in the elemental, not the compound form. So, facilities using lead solder and metal alloys should consider the quantities of elemental lead in these materials.
Lead acid batteries would typically meet the articles exemption, assuming there are no TRI chemical releases associated with the lead acid batteries.
Old paint can also contain lead. However, removing old paint containing lead and sending it off-site for disposal or treatment is not considered a threshold activity under TRI. Simply transferring a waste containing a TRI-listed chemical off-site for waste management other than recycling is not in itself a threshold activity.

## Slide 42: Lead and Lead Compounds
Under TRI, lead is classified as a Chemical of Special Concern except for lead contained in stainless steel, brass, and bronze alloys
Chemicals of special concern activity thresholds:
  Lead: 100 pounds (not contained in stainless steel, brass, or bronze)
  Lead compounds: 100 pounds
25,000/10,000-pound reporting thresholds apply to lead contained in stainless steel, brass, or bronze*
  25,000-pound thresholds for manufacturing or processing
  10,000-pound threshold for otherwise use
  0.1% de minimis level applies to lead contained in stainless steel, brass, or bronze
* If elemental lead is removed from the qualified alloy, such as vaporization during melting of an alloy, the 100 lb threshold applies.
v
Pb
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Elemental lead that is not contained in stainless steel, brass or bronze alloys is considered a Chemical of Special Concern and has a 100-pound threshold. The lead compounds category always has a 100-pound threshold.
There is also a 25,000/10,000-pound reporting threshold for lead, which applies only to lead that is contained in stainless steel, brass, or bronze: 25,000 pounds for manufacturing and processing, and 10,000 pounds for otherwise use.

## Slide 43: Lead Threshold Determination Flow Chart
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Because there are two different ways to look at lead, for facilities that have both lead in stainless steel, brass and bronze, AND lead not in these alloys, this flowchart can be helpful in determining which thresholds have been exceeded and what reporting requirements apply.
The first step is to quantify all of the lead manufactured processed or otherwise used at the facility, including lead in stainless steel, brass, or bronze and lead in the Chemicals of Special Concern form. If so, the lead in these alloys is not a Chemical of Special Concern and compare that to the thresholds of 25,000 and 10,000 pounds. Then the facility looks only at lead not in stainless steel, brass, or bronze and compares that to the 100 pound threshold for the Chemicals of Special Concern form of lead.
Following this flow chart, if neither threshold is exceeded, then no reporting is required. If only the threshold for the Chemicals of Special Concern form of lead is exceeded then the facility is only required to report on the lead not in stainless steel, brass, or bronze and cannot use a Form A and must follow the reporting requirement specific to Chemicals of Special Concern.
If only the 25,000/10,000-pound reporting thresholds lead is exceeded, then the facility reports on both the lead in the stainless steel, brass or bronze and the lead not in these alloys, and they follow the reporting requirements for chemicals with 25,000/10,000-pound Reporting Thresholds, including the use of the Form A, if they meet those criteria.
Finally, if both the thresholds for the Chemicals of Special Concern form of lead and for the chemicals with 25,000/10,000-pound reporting thresholds form of lead are exceeded, then the flowchart shows that the facility must report using a Form R on both forms of lead and must follow the reporting requirements for Chemicals of Special Concern.

## Slide 44: Quiz #2: Question 1
A facility combusts 13,600,000 lb of coal to fire its boilers. The coal contains elemental lead (Pb) at 7.0 ppm by weight. In combusting the coal, the facility otherwise uses lead and coincidentally manufactures lead compounds. The facility has no other information about the chemical makeup of the lead compounds manufactured and assumes it is the lowest-weight oxide - PbO. Based on molecular weights (Pb = 207, PbO = 223), the facility knows that 223 lb of PbO is formed for every 207 lb Pb used.
Which of the following thresholds have been exceeded for lead or lead compounds?
A. Otherwise Use only
B. Manufacturing only
C. Neither
D. Both
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern

## Slide 45: Quiz #2: Question 2
The facility in the previous question combusted 13,600,000 pounds of coal in the reporting year and has exceeded the reporting threshold for lead compounds. The facility has no monitoring data on their point source lead emissions from combusting the coal. They determined that their best available information for calculating their point source air emissions is the published emission factor for lead from controlled coal combustion from EPA’s AP-42, which is 4.2E-04 lb Pb/ton of coal combusted.
What are the facility’s point source emissions of lead from coal combustion?
A. 2.86 lb
B. Range Code ‘A’
C. 95.2 lb
D. Either 2.86 lb or Range Code ‘A’
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern

## Slide 46: Polycyclic Aromatic Compounds (PACs) and Benzo[g,h,i]perylene
Chemicals of Special Concern activity thresholds
  PACs category threshold: 100 pounds
  Benzo[g,h,i]perylene threshold: 10 pounds
Present in coal, fuel oil, other petroleum products, such as asphalt and roofing tars
Asphaltic concrete (blacktop) typically contains 4 - 10% paving asphalt
Some uses of paving asphalt (blacktop) are NOT EXEMPT
  Paved process areas and roads for process vehicles (e.g., on-site haul trucks) – NOT EXEMPT
  Employee parking lot and non-process access roads – EXEMPT
See also EPA’s PACs and Persistent Bioaccumulative Toxic (PBT) guidance
  guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd-title:::::title:pacs
  guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd-title:::::title:pbts
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Polycyclic Aromatic Compounds (PACs) and benzo(g,h,i)perylene are both Chemicals of Special Concern. The PACs have a 100-pound threshold. Benzo(g,h,i)perylene has a 10-pound threshold. These chemicals are usually found in the same sources including in coal, fuel oil, petroleum products, and roofing tars. These chemicals can also be coincidentally manufactured during the combustion of fossil fuels.
Because they are found in asphalt, they are typically present in blacktop. Blacktop used for paving an employee parking lot is exempt under the structural exemption, but other uses of blacktop at a facility probably are not because these uses are process-related. For example, blacktop used for roadways that trucks use to bring materials in and product out of the facility would not be exempt. EPA has developed a guidance document that provides much more information on PACs along with specific examples that will help facilities determine their requirements associated with PACs. A similar document for PBTs includes information on benzo[g,h,i]perylene.

## Slide 47: PACs (cont.)
FUEL MATERIAL | TYPICAL PAC CONCENTRATION | QUANTITY NEEDED TO EXCEED THRESHOLD (GALLONS)
No. 6 Fuel Oil (Bunker C) | 2,461 ppm | 5,140
No. 2 Fuel Oil | 10.0 ppm | 1,410,000
Crude Oil | depends on type of crude | 
Gasoline | 17 ppm | 1,060,000
Paving Asphalt | 178 ppm | 51,800
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: This table is an excerpt from the PAC Guidance Document. The guidance document provides typical concentrations for PACs in a number of sources. The table also shows the quantity that would need to be used to meet the threshold at these concentrations. For example, the first line shows No. 6 fuel oil at a typical concentration of 2,461 parts per million of PACs. At this concentration, if a facility uses more than 5,140 gallons for No. 6 Fuel Oil during the reporting year, they would exceed the 100-pound reporting threshold.
Whereas for No. 2 fuel oil, the typical concentration of PACs is significantly lower at 10 parts per million. So, the table shows that a facility would have to use 1.41 million gallons of No. 2 fuel oil at that concentration before you exceed the 100 pound PACs threshold. Again, these are typical concentrations. If your facility has better information, more specific to the fuels actually used at your facility, that information should be used.
Similar data for benzo[g,h,i]perylene in certain fuels are provided in the PBTs guidance document.

## Slide 48: Mercury and Mercury Compounds
Chemicals of Special Concern activity thresholds:
  10 pounds for mercury
  10 pounds for mercury compounds
Combustion of fuels is expected to be a main source of mercury, exceeding an activity threshold.
Combustion involves the otherwise use of mercury compounds in fuel and the manufacture of elemental mercury.
Amount of fuel required to exceed a threshold:
  No. 2 Fuel Oil: 1.41 x 109 gallons
  No. 6 Fuel Oil: 1.89 x 109 gallons
  Coal: 11,000 – 120,000 tons
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Now let’s look at mercury and mercury compounds. The Chemicals of Special Concern activity thresholds are 10 pounds for mercury and 10 pounds for mercury compounds. Note that mercury and mercury compounds are two separately listed TRI chemicals. The combustion of fuels is the main source of mercury triggering reporting to TRI. Combustion typically involves the otherwise use of mercury compounds in fuels and the manufacture of elemental mercury.
If you do not know the mercury compound present in a fuel, EPA recommends using mercurous oxide for threshold calculations of otherwise use. In the absence of better information, EPA also recommends that facilities assume that all releases and other waste management quantities of mercury from the combustion of coal are in the form of elemental mercury.
EPA has developed a mercury guidance document that provides the amounts of fuels required to exceed the 10 pound threshold for typical concentrations of mercury in those fuels.
However, if a facility has better, more specific information on the fuel that they are actually using, they should base their calculations on that information. If they do not have other information, they can use the default information in the mercury guidance.
Some information from that guidance document is shown here. For example, in the case of No. 2 fuel oil, you would need to use about 1.41 billion gallons of Number 2 fuel oil to exceed the reporting threshold, IF the concentration of mercury in the fuel oil was 1 part per Billion. For Number 6 fuel oil, it would take about 1.89 billion gallons. So, this helps give a sense of whether reporting might be required. Alternatively, if the uses of these fuels is not even close to these quantities and there are no other sources of mercury at the facility, reporting would probably not be required.

## Slide 49: Mercury and Mercury Compounds
Present in some switches and lights
  Bulbs and switches may qualify as articles for which the articles exemption would apply IF less than 0.5 pound of TRI-listed chemicals are released from all like items as a result of processing or otherwise use of the items during the year.
Mercury may be present in measurement devices such as thermometers or manometers. The addition of mercury to these devices needs to be considered in threshold and release calculations.
Present in Caustics/Acids (if produced in mercury cell process – not common)
May be present in mined ores
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Here are a few other things to consider regarding mercury. In addition to petroleum products, mercury and mercury compounds might be found in switches and lights. Note, however, that the otherwise use of bulbs and switches would be exempt as an article if you are not a bulb or switch manufacturer AND less than half a pound of the mercury is released during the reporting year from all like items during normal conditions of processing or use.
For example, if a facility purchases and installs mercury switches in a piece of equipment that they manufacture, it would likely meet the article exemption, as long as all like items do not release more than half a pound of 313 chemical as a result of processing or use of the items during the year. If mercury is being added to an instrument, that would NOT be covered by the article exemption.
Facilities should also be aware that mercury might be present in caustics and acids – if it is produced using the mercury cell process, which is not now common. In addition, mined ores may be another source of mercury.

## Slide 50: Polychlorinated Biphenyls (PCBs)
Chemicals of Special Concern activity thresholds: 10 pounds
Manufacturing:
PCBs may be manufactured as a product of incomplete combustion (PIC)
Otherwise use:
  On-site treatment or disposal of PCB-contaminated waste received from off site
  Combusting PCB-contaminated oil
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Polychlorinated biphenyls have a reporting threshold of 10 pounds. Facilities should consider where in their process that they may be using or generating polychlorinated biphenyls. Polychlorinated biphenyls can be manufactured as a byproduct of incomplete combustion. Be aware that recycling of polychlorinated biphenyls is considered processing. Also, using polychlorinated biphenyls by: adding them into your process equipment; treating them on-site; or disposing of polychlorinated biphenyl-contaminated waste received from off-site – or combusting polychlorinated biphenyl-contaminated oil; are all counted towards the otherwise use threshold.

## Slide 51: PCBs
Activities NOT considered manufacturing, processing, or otherwise use:
  On-site disposal or treatment of PCBs
    Exception: if PCBs were received as wastes from off site they are counted towards the “otherwise use” threshold.
  Off-site shipment of PCBs for disposal or treatment
Transformers containing PCBs may be considered articles and thus exempt from consideration towards reporting and release thresholds.
  Leaks may negate article exemption if 0.5 pounds of PCBs are released in a reporting year.
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: Many facilities ask about how they should report when they ship an old polychlorinated biphenyl-containing transformer off-site for disposal. Polychlorinated biphenyl transformers are considered exempt as articles if no polychlorinated biphenyls are released during their normal use. Note that leaks may negate that article exemption. Also, shipping a product off-site for disposal is not a manufacturing, processing, or otherwise use activity– in other words, it is not a threshold activity. Other activities that are not threshold activities include on-site disposal or treatment of polychlorinated biphenyls not received from off-site or the off-site shipment of polychlorinated biphenyls for disposal or treatment.
So, facilities with old transformers that contain polychlorinated biphenyls, and that are just getting rid of them by sending them off-site for disposal, would not need to report on the polychlorinated biphenyls, assuming they had no other sources of polychlorinated biphenyls at the facility. Just shipping a waste off-site for the purposes of further waste management is not a threshold activity.

## Slide 52: PFAS
PFAS have been used to formulate some firefighting foams (e.g., aqueous film forming foam (AFFF)) that have been stored and used at facilities for fire suppression, fire training, and flammable vapor suppression.
Chemicals present in fire suppression equipment that is used and maintained on site
Use of a fire suppression system for system testing, training, or to suppress a fire as part of an emergency response would constitute otherwise use of the TRI-listed chemicals in the firefighting foam, per the definition of otherwise use in the TRI Reporting Forms and Instructions, Section B.3.a.
Chemicals present in fire suppression equipment that is not used
Storage is not considered a M/P/OU activity.
A facility receiving and incorporating AFFF into a fire suppression system on site is considered to be storing the AFFF for intended future use. The placement of AFFF into a fire suppression system is not an otherwise use activity for TRI reporting purposes, until the AFFF is released from the system.
An accidental release is not otherwise use and is therefore not a threshold activity. Note that, while an accidental spill is not itself a threshold activity, an accidental spill may be a reportable release if a reporting threshold is otherwise exceeded.
See guideme.epa.gov/ords/guideme_ext/f?p=GUIDEME:GD::::RP:gd:pfas_resources for more on TRI PFAS reporting.
Advanced TRI Reporting Concepts: Guidance for Chemicals of Special Concern
Notes: PFAS have been used to formulate some firefighting foams (e.g., aqueous film forming foam (AFFF)) that have been stored and used at facilities for fire suppression, fire training, and flammable vapor suppression.
Chemicals present in fire suppression equipment that is used and maintained on site
Use of a fire suppression system for system testing, training, or to suppress a fire as part of an emergency response would constitute otherwise use of the TRI-listed chemicals in the firefighting foam, per the definition of otherwise use in the TRI Reporting Forms and Instructions Section B.3.a.
Chemicals present in fire suppression equipment that is not used
Storage is not considered a manufacturing, processing, or otherwise use activity. However, if the facility exceeds the manufacturing, processing, or otherwise use threshold for the same toxic chemical elsewhere at the facility, the facility must consider these quantities towards the maximum amount on-site and include any releases from the storage of the toxic chemical in the Form R (e.g., accidental discharges, emissions, leaks, spills, etc.).
A facility receiving and incorporating AFFF into a fire suppression system on-site is considered to be storing the AFFF for intended future use. A fire suppression system is not a closed-loop, nor is the AFFF reused. The placement of AFFF into a fire suppression system is not an otherwise use activity for TRI reporting purposes, until the AFFF is released from the system.
An accidental release is not otherwise use and is therefore not a threshold activity. Note that, while an accidental spill is not itself a threshold activity, an accidental spill may be a reportable release if the reporting threshold is otherwise met.

## Slide 53: SECTION 4: TOOLS AND ASSISTANCE

## Slide 54: www.epa.gov/tri
TRI website for reporting materials and guidance includes:
  Electronic versions, or links to electronic versions, of the statutes, regulations, executive orders, chemical-specific guidance documents, and industry-specific guidance documents
TRI GuideME
  Available at guideme.epa.gov
  View the Reporting Forms and Instructions
  Browse frequently asked questions and answers
  Browse guidance materials
  View interactive TRI-listed chemical lists
Advanced TRI Reporting Concepts: Tools and Assistance
Notes: TRI reporters should be aware that the TRI homepage contains a great deal of information to assist facilities with their TRI reporting. All of the relevant statutes and regulations are available, as well as guidance for specific chemicals and industry sectors.
In addition, the TRI Program has developed a guidance database hosted in GuideME. It allows facilities to browse questions and answers, the reporting forms and instructions, and other guidance materials. GuideME can be accessed at the website shown here or via the TRI website.

## Slide 55: Reference Sources
EPA Industry Guidance:
  guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd-list
AP-42: Compilation of Air Pollutant Emission Factors:
  www.epa.gov/air-emissions-factors-and-quantification/ap-42-compilation-air-emissions-factors
Technology Transfer Network:
  www.epa.gov/technical-air-pollution-resources
  AP-42
  WATER9 program
  TANKS program
Perry's Chemical Engineer's Handbook; CRC Handbook of Chemistry and Physics; Lange's Handbook of Chemistry
Advanced TRI Reporting Concepts: Tools and Assistance
Notes: Here are some additional sources of information and assistance with the TRI reporting, in general. The first is the TRI program webpage which has a great deal of chemical-specific and industry-specific guidance and all of the reporting forms and instructions.
In addition, EPA’s air pollution emission factors are available in a document called the AP-42. The Website for that is also shown here.
There is also a software program called the WATER9 program. This is a PC-based software that assists with estimates of the fate of organic compounds in various wastewater treatment units.
TANKS is also a PC-based program used to estimate emissions of organic chemicals from several different types of storage tanks. This software uses a database of over 100 different liquid organic chemicals. It includes meteorological data which – from over 250 cities in the US to help with those calculations. Those are both also available from the EPA Website shown here.

## Slide 56: Pollution Prevention (P2) Information
Visit the TRI Pollution Prevention webpage
  www.epa.gov/tri/p2
P2 Reporting Guide
  guideme.epa.gov/ords/guideme_ext/f?p=guideme:gd:::::gd:p2_reporting_guide
P2 Resources Search Tool:
  www.epa.gov/p2/p2-resources-search
Contact Info:
  Helpline: www.epa.gov/p2/forms/contact-us-about-pollution-prevention#helpline
  E-mail: p2hub@epa.gov
  Phone: (202) 566-0799
Advanced TRI Reporting Concepts: Tools and Assistance
Notes: Facilities that are interested in using source reduction techniques to reduce their TRI chemical use and wastes can get assistance from the EPA’s office of Pollution Prevention and the P2 Hub Resource Center, at the websites and telephone number shown here.

## Slide 57: TRI Contact Information
TRI Regulatory and Technical Support
  For regulatory assistance, contact TRI.help@epa.gov.
  For technical questions related to TRI-MEweb and the Central Data Exchange (CDX), please contact the CDX Hotline at helpdesk@epacdx.net or call toll-free at (888) 890-1995.
TRI Regional Coordinators
  www.epa.gov/toxics-release-inventory-tri-program/tri-regional-coordinators
Advanced TRI Reporting Concepts: Tools and Assistance
Notes: If you want more information about TRI-MEweb and the central data exchange, please use the CDX hotline and email address shown here. For regulatory reporting assistance, facilities can contact the email shown here. Regional coordinators are useful for issues regarding self-disclosing EPCRA 313 violations, compliance with and enforcement of EPCRA 313 (reporting late, data quality, non-reporting, recordkeeping), registering, completing, and submitting Form Rs, and threshold calculations.

## Slide 58: SECTION 5: TRI-MEweb

## Slide 59: TRI-MEweb and Submitting Via CDX
EPA requires electronic filing via TRI-MEweb
  No paper submissions are accepted (except for trade secrets), including for revisions and withdrawals.
  TRI-MEweb supports new reporting, revisions & withdrawals for RY 1991 – current year.
  TRI-MEweb resources including tutorials are available to help users at www.epa.gov/tri/trimeweb
EPA will not accept any paper submissions except for trade secret claims.
Use hard-copy form only for trade secret reporting
  Information about trade secret reporting is available at:
    guideme.epa.gov/ords/guideme_ext/f?p=guideme:rfi:::::rfi:apx_a
All TRI reporting forms must be prepared, certified, and submitted by July 1 following the calendar year’s (aka Reporting Year (RY)) activities
July 1, 2026 deadline for RY 2025 (January 1 - December 31, 2025) activities
v
v
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: All TRI reporting forms must be submitted via TRI-MEweb except for forms claiming a trade secret. Electronic reporting is also required for all withdrawals or revisions for Reporting Years 1991 through the present.
TRI-MEweb has features to help reporters with their submissions including pre-populating forms with information from prior year reporting, validation and error checking steps, and e-mail confirmation of transmitted and certified submissions. Additionally, tutorials to help users with TRI-MEweb are available on the TRI website.
Paper submissions should only be used for trade secret reporting. Information about trade secret reporting is available on GuideME.

## Slide 60: Accessing TRI-MEweb
TRI-MEweb is accessed through EPA’s Central Data Exchange (CDX)
  CDX is available at https://cdx.epa.gov.
  TRI-MEweb users must have a CDX account.
  Select the appropriate TRI-MEweb user role: Preparer or Certifying Official.
Within TRI-MEweb, new users must gain access to their facility before preparing forms.
  Option 1: Enter facility’s access key.
  Option 2: Enter TRIFID and Technical Contact Name.
  Option 3: Begin a new facility profile if the facility has never reported to TRI or has changed physical location.
For assistance with accessing your facility, contact the CDX Helpdesk at helpdesk@epacdx.net or call toll-free at (888) 890-1995.
v
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: To begin using TRI-MEweb, you must register and log into EPA’s Central Data Exchange, also known as CDX, which also hosts many other reporting applications for EPA programs. Users register either as a preparer or a certifying official. Preparers may perform every portion of the submission process except for the final electronic signature or certification step, which must be performed by a certifying official. The certifying official should be in senior management role for the reporting facility or company. Anyone representing the facility may be a preparer.
To begin reporting for a facility, all uses must gain access to their facility’s profile, using one of three options: the first option is to enter the TRI Facility ID and the facility’s technical contact name and phone number. The second option is to enter the facility’s access key, which is provided to the technical contact. The third option is to begin a new profile for a facility that has never reported to TRI.
For CDX and TRI-MEweb related help, including registering for CDX, password resets, accessing your facility profile in TRI-MEweb, or completing an ESA, please contact the CDX helpdesk.

## Slide 61: Starting a Form in TRI-MEweb
To start a new chemical form from scratch (Part II Sections 1.1-1.2, 2.1):
  Select CAS Registry Number or category code and name of chemical or chemical category; or
  Select “Add generic chemicals,” if supplier claims trade secret.
  Indicate if using Reporting Form R or From A (only for non-chemicals of special concern).
TRI-MEweb preloads previous year’s reporting details using “Import Prior Year Form(s).”
The XML uploader handles forms generated by third-party tools.
v
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: To begin a Form R or Form A Certification Statement, first facilities identify the TRI chemicals on which they are reporting. Facilities select chemical name, the “chemical abstract service” number or the TRI chemical category code or select it from the list provided in TRI-MEweb. For those facilities that are claiming a trade secret the chemical name is only entered and the public version of the TRI Form R or A shows only the generic descriptive for the chemical.
In some cases, the facility’s chemical supplier may have claimed a trade secret for a particular TRI chemical and the facility does not know the actual name of the TRI chemical for which they are submitting a report. In this scenario, the facility enters the generic descriptive provided.
TRI-MEweb can generate new forms based on prior year reporting use the “Import Forms” feature.
Some third-party form preparation software generates XML output of forms that may be loaded into TRI-MEweb using the XML uploader.

## Slide 62: Production-Related Waste Managed (Section 8.1-8.7)
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: Reporting on production-related waste managed often creates questions from reporters.
In Section 8.1, the quantity of the chemical released is reported. In Sections 8.2 and 8.3, the quantities of the chemical used for energy recovery on-site and off-site are reported. Remember, to be reported as energy recovery, the TRI chemical must have a significant heat value and that heat must be recovered. In Sections 8.4 and 8.5, the quantities of the chemical recycled on-site and off-site are reported. And, in Sections 8.6 and 8.7, the quantities of the chemical treated on-site and off-site are reported. Under TRI, treatment means “destroyed”, so metals, which cannot be destroyed, should not be reported in these sections.
Adding up the quantities in section 8.1 through 8.7 gives the total quantity of waste generated from production activities at the facility. This includes the total quantity released, treated, recycled, or used for energy recovery. Some of these quantities may have already been calculated to complete Form R section 5 for on-site releases and section 6 for off-site transfers. The TRI-MEweb application includes a Section 8 calculator tool that will help with these calculations. However, the quantities reported in sections 5 and 6 of the form can differ from those reported in Sections 8.1 through 8.7. The sections 5 and 6 quantities should include any TRI chemicals released and transferred as part of a remedial clean-up action or catastrophic one time event. These non-production-related quantities are NOT included in Sections 8.1 through 8.7. TRI-MEweb will ask if any of the quantities reported in sections 5 and 6 were associated with remedial actions or catastrophic one time events, and if so, how much. Then, using the information already entered into TRI-MEweb, the Section 8 calculator will populate the quantities for the current year column of Section 8. In the Source Reduction and Waste Management portion of the Form R, as shown here, facilities are not only required to report on the current year’s activities, but also the previous year’s quantities and estimates for the next two years.
If your facility reported on this chemical in the previous year, TRI-MEweb will pre-populate the prior year column. Facilities then only need to estimate quantities for the following two years.

## Slide 63: Certifying Official Information
All non-trade secret forms must be certified by an electronic signature from a senior management official.
New Certifying Officials must submit an electronic signature agreement (ESA) and a facility certification agreement form before pending submissions can be certified.
Returning Certifying Officials do not need to submit an ESA if they continue to represent the same facility year to year.
TRI-MEweb now includes a built-in Certification module, accessible by users registered as Certifying Officials.
New Certifying Officials will answer personalized security questions in addition to their CDX password for digital procedures.
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: Forms must be signed electronically or certified by certifying officials, who should be in senior management roles for the reporting facility or company. This step certifies that the information reported on the TRI form is accurate and complete.
Certifying officials must submit an electronic signature agreement, also known as an ESA. The ESA is only submitted once so long the certifying official remains with the facility. Thus, existing certifying officials will not need to resubmit an ESA. New certifying officials should complete their ESA well in advance of the July 1st filing deadline to ensure they will be able to certify forms on time.
Certifying officials now certify new reporting, revisions and withdrawals from a Certification module with-in TRI-MEweb. To complete the certification, certifying officials must also answer personalized security questions in addition to their CDX password.

## Slide 64: Signing and Certifying Forms
New Certifying Officials must complete the following two requirements:
  Electronic signature agreement (ESA)
    Must be completed only once, not annually, applicable to all facility profiles
    Option 1: Real-time ESA approval – verify user’s identity electronically
    Option 2: Mail in signature form – minimum of 5 business days to process
  TRIFID Certification Agreement Form
    Must be completed after access to TRI-MEweb is granted by ESA approval
    Facility profiles are added to TRI-MEweb using access keys or prior-year information
    Certifying Officials must have a digitally signed TRIFID Certification Agreement for each facility profile before receiving access to any pending submission (s) for certification
New Certifying Officials must submit an ESA and digitally sign a TRIFID certification agreement form before pending submissions can be reviewed and certified.
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: In order to certify forms, certifying officials must complete two steps. The first step is to submit an electronic signature agreement, also known as an ESA, to be able to certify forms. An ESA is submitted only once so long the certifying official continues to represent the facility. There are two options for submitting an ESA. The first option uses a third-party vendor to verify the certifying official’s identity, and is completed in real time. The second option is to mail in a signed paper form generated by TRI-MEweb, which takes a minimum of five business days to process. Certifying officials should complete their ESA well in advance of the July 1st filing deadline to ensure they will be able to certify forms on time.
Secondly, after the ESA is submitted, certifying officials must complete a TRIFID Certification Agreement for each facility they represent, confirming they are authorized to certify forms for the facility. The TRIFID Certification Agreement is completed within TRI-MEweb in the ‘Certification’ section of TRI-MEweb. Similar to the ESA, the TRIFID Certification Agreement is only submitted once so long the certifying official remains with the facility.

## Slide 65: eReceipts
Facilities can obtain a copy of their electronic receipt (formerly known as the electronic Facility Data Profile report (eFDP)) under the Submission History tab within TRI-MEweb.
Review your eReceipt immediately after certifying TRI reporting forms in CDX to verify that EPA processed your data correctly.
It allows EPA to highlight errors and possible issues with your submission.
If you have problems accessing your eReceipt, email tridpc@epa.gov
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: Facilities that have filed in the past should be familiar with the Facility Data Profiles report. The facility data profile reports were designed for the paper processing system that ceased to exist in 2014. TRI-MEWeb has renamed these reports “eReceipts”. This report is generated after TRI’s Data Processing Center receives and processes facilities’ forms. The Data Processing Center conducts data quality checks before the form data is accepted into TRI’s database, they also run various data validation of the facility’s location profile. If no discrepancies are found, the form data is flagged for public release and an eReceipt report to confirm completion of data processing is sent to the TRI-MEweb application. The eReceipt has two purposes: First, it’s also called an “echo back” because it echoes back to you the information of the form data that was processed by EPA and is on stand-by for public release. That gives facilities a chance to confirm that the data was captured correctly. Second, it identifies potential errors. Potential errors include: 1) non-technical errors, such as transposing a CAS Registry Number; or 2) technical errors, such as an invalid NAICS code; or 3) a significant error, which would be missing information like a chemical identifier, or the certifying signature. Third, it also identifies data quality alerts. Data quality alerts are indications of any significant reporting changes compared to the prior year or any reporting abnormalities that the facility needs to be aware of. Facilities may respond to significant errors pointed out in the eReceipts by submitting a revision.
Facilities may contact the e-mail address shown here if they have any problems accessing their eReceipts reports.

## Slide 66: TRI-MEweb Tutorials
TRI-MEweb has integrated tutorials to assist users with features and common functions, such as:
    Overview
    Registration
    Accessing Your Facility
    Nominating a Certifying Official
    Section 8 Calculator
    Submitting Data
    Certifying Data
    Getting Help
For a list of tutorials:
  www.epa.gov/toxics-release-inventory-tri-program/electronic-submission-tri-reporting-forms#q2
v
Advanced TRI Reporting Concepts: TRI-MEweb
Notes: There are other tools available to assist you with your TRI reporting and using the TRI-MEweb application. EPA has developed on-line tutorials that all of the steps needed to access, submit, and certify TRI forms using TRI-MEweb.
These tutorials are available from the EPA Website shown here. There is audio along with the tutorials, so you need to have speakers or a headset. Alternatively, closed captioning is available.

## Slide 67: END OF MODULE

## Slide 68: Quiz Answers
68
Notes: 68

## Slide 69: Quiz #1: Question 1
A facility processes 200,000 pounds of a mixture containing 10% zinc chromate (ZnCrO4) and 15% chromium dioxide (CrO2) by weight
For which of the following chemical categories was the processing threshold exceeded?
Answer: A is correct
A. Chromium compounds only B. Zinc compounds only
C. Neither D. Both
Chromium compounds only
Zinc compounds only
C. Neither
D. Both
Total chromium compounds processed: (10% + 15%) × (200,000 lb) = 50,000 lb
Total zinc compounds processed: (10%) × (200,000 lb) = 20,000 lb
The processing threshold (25,000 lb) was exceeded for chromium compounds, but not zinc compounds. Both are chemicals with 25,000/10,000-pound reporting thresholds

## Slide 70: Quiz #1: Question 2
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby water body.
The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. 1 mole of HNO3 generates 1 mole of NaNO3.
Does the facility exceed the manufacturing threshold for nitrate compounds?
Answer: Yes
The quantity of nitrate compounds manufactured = (quantity of HNO3 neutralized) × (MW of NaNO3 / MW of HNO3)
NaNO3 manufactured = (20,000 lb) × (85/63) = 26,984 lb (rounded to 27,000)
Nitrate compounds are subject to 25,000/10,000-pound reporting thresholds.
The manufacturing threshold (25,000 lb) is exceeded, so the facility must submit a TRI form for nitrate compounds

## Slide 71: Quiz #1: Question 3
A facility neutralizes 20,000 lb of nitric acid (HNO3) with sodium hydroxide (NaOH) in an on-site wastewater treatment system. The neutralization is 100% complete and generates sodium nitrate (NaNO3), which is discharged to a nearby water body. The molecular weight (MW) of HNO3 = 63 and the MW of NaNO3 = 85. 1 mole of HNO3 generates 1 mole of NaNO3
In this example, should the facility report release of 27,000 lb of nitrate compounds as to a stream or water body? (Section 5.3 on Form R)? Yes or no
Answer: No
Releases of nitrate compounds are reported on nitrate ion (NO3-) basis. Based on molecular weights (NaNO3 = 85, NO3- = 62), 62 lb of nitrate ion are generated for every 85 lb of nitrate compounds.
To calculate the quantity of nitrate ion released to the water body in the example described above: (lb of NaNO3) x (MW of NO3- / MW of NaNO3) = (26,984 lb) x (62/85) = 19,682 lb (rounded to 20,000 lb)
On the Form R for nitrate compounds, the facility would report 20,000 lb of the nitrate ion releases to the stream or water body.

## Slide 72: Quiz #2: Question 1
A facility combusts 13,600,000 lb of coal to fire its boilers. The coal contains elemental lead (Pb) at 7.0 ppm by weight. In combusting the coal, the facility otherwise uses lead and coincidentally manufactures lead compounds. The facility has no other information about the chemical makeup of the lead compounds manufactured and assumes it is the lowest-weight oxide – PbO. Based on molecular weights (Pb = 207, PbO = 223), the facility knows that 223 lb of PbO is formed for every 207 lb Pb used.
Which of the following thresholds have been exceeded for lead or lead compounds?
Answer: B is correct
Pb in coal: (13,600,000 lb) * (7 x 10-6) = 95.2 lb
PbO formed: (95.2 lb) * (223/207) = 103 lb
Total lead combusted (95.2 lb) does not exceed the threshold for otherwise using lead not in stainless steel, brass, or bronze (100 lb)
Total lead oxide manufactured (103 lb) exceeds the threshold for manufacturing of lead compounds (100 lb)
A. Otherwise Use only
C. Neither
B. Manufacturing only
D. Both

## Slide 73: Quiz #2: Question 2
The facility in the previous question combusted 13,600,000 pounds of coal in the reporting year and has exceeded the reporting threshold for lead compounds. The facility has no monitoring data on their point source lead emissions from combusting the coal. They determined that their best available information for calculating their point source air emissions is the published emission factor for lead from controlled coal combustion from EPA’s AP-42* which is 4.2E-04 lb Pb/ton of coal combusted.
What are the facility’s point source emissions of lead from coal combustion?
Answer: A is correct
A. 2.86 lb
C. 95.2 lb
B. Range Code ‘A’
D. Either 2.86 lb or Range Code ‘A’
Point Source Emissions (lb) = EF × W where: EF = emission factor for controlled coal combustion (lb Pb/ton coal), and W = weight of coal combusted (ton)
Weight of coal combusted: (13,600,000 lb coal)/(2,000 lb/ton) = 6,800 tons coal
Point Source Emissions = 4.2E-4 (lb Pb/ton coal) × 6,800 tons coal = 2.86 lb Pb
  Assuming coal combustion was the only source of point source air emissions for this facility, the facility would report 2.86 lb in Section 5.2 of their Form R for lead compounds.
  Range codes cannot be used for Chemicals of Special Concern.
  While threshold determinations are based on the weight of the lead compounds, release and waste management calculations are based on the weight of the parent metal (lead) in the metal compound (lead oxide).