## Slide 1: Laws, Regulations, Standards
1
Chapter 3
Lead Abatement
for Workers Course
Notes: Slide 1.
When teaching this Chapter, the instructor may choose to select slides that convey the main points of this Chapter and utilize the skits and exercises provided to reinforce the other important aspects of this Chapter.
Direct the students to Chapter 3.

## Slide 2: Learning Objectives
2
You will learn about:
  The Federal guidelines on lead
  The Federal laws and regulations that protect workers and the environment
  Your State, Tribal, and local laws and regulations for lead
Notes: Slide 2.
Discuss the objective of this Chapter.
Reassure the students that they will be responsible for understanding and remembering the major points and purposes of each regulation, but not all of the details. Be sure to cover adequately the points which will be included on the post-course examination.

## Slide 3: Laws
3
Occupational Safety and Health Administration (OSHA)
  Worker safety and health
Environmental Protection Agency (EPA)
  Worker, public, and environmental protection
Department of Housing and Urban Development (HUD)
  Guidelines and requirements for lead-based paint hazard control
Notes: Slide 3.
Explain that there are several Federal agencies that have regulations and laws which protect the worker, the environment, and the general public.

## Slide 4: OSHA
4
Know the laws that protect you!
Workers have the right to:
  A safe workplace
  Be protected from hazards such as lead or chemicals
  File a complaint with OSHA
  Exercise health and safety rights without being fined or harassed
Notes: Slide 4.
Stress the importance to the student of knowing what laws there are to protect their health and safety. Show them in the course notebook where the additional information on these points is located.
Introduce them to OSHA and inform them that OSHA has many safety and health laws to protect them from hazards in the workplace. These laws and worker rights apply regardless of lead levels in the workplace. The employee must follow the safe work practices taught in this course to protect themselves.
Remind them that this EPA course does not include many of the topics required by OSHA and that, unless this course is extended beyond two days, their employer is required to provide them the additional training.

## Slide 5: OSHA Interim Final Lead in Construction Standard
5
Applies to all workers doing construction work
Sets limits on how much lead you can breathe
  Action Level (AL)
    30 µg/m3
  Permissible Exposure Limit (PEL)
    50 µg/m3
Notes: Slide 5.
Discuss different activities that are included under “construction.”
Remind them how little a microgram of lead is and explain a cubic meter and how sampling is conducted.
Discuss the importance of knowing how much lead is in the air the worker is breathing. Discuss that these levels DO NOT factor in the respiratory protection the worker is wearing. These are exposure levels without regard to respiratory protection; but these levels tell the employer what type of respirator to use.

## Slide 6: Air Sampling
6
Must be done to find out how much lead you are exposed to
Each job must be sampled
Each shift must be sampled
You must be told how much lead you are exposed to
Notes:   Slide 6.
  Remind the student that they play an important role in keeping the levels of lead in the air LOW.
  Discuss what is meant by “each job” (e.g., one worker using a heat gun while another is doing component replacement; each would have to be sampled to determine exposure for that job or activity).
  The personal air sampling must be done on each shift or the shift with the highest exposure. Discuss expected versus known exposures.
  Explain the requirements for notification of the employees exposure levels.

## Slide 7: OSHA’s Lead-related Tasks
7
Class 1 tasks
  Manual demolition
  Manual scraping or sanding
  Using a heat gun
  Power tool cleaning with dust collection systems
  Spray painting with lead-based paint
Notes: Slide 7.
Discuss the reason for the Lead-related Tasks and the minimum worker protections required.
The OSHA lead standard requires your employer to protect you even if air sampling hasn’t been done yet. It does this by placing jobs into three separate categories. It is assumed that each category exposes you to a certain amount of lead.
If you do one or more of the lead-related tasks, you must wear a respirator until air sampling results show that the air levels are below the PEL.

## Slide 8: OSHA’s Lead-related Tasks
8
Class 2 tasks
  Using lead-based mortar
  Burning lead
  Rivet busting
  Power tool cleaning without dust collection systems
  Cleanup activities where abrasives are used
  Moving or tearing down the enclosure used for abrasive blasting
Notes: Slide 8.
Important: Burning of lead-based paint is not allowed by HUD or EPA/State/Tribal regulations on residential dwellings or child-occupied facilities.
Discuss the minimum worker protection requirements when conducting Class 2 tasks.

## Slide 9: OSHA’s Lead-related Tasks
9
Class 3 tasks
  Abrasive blasting
  Welding
  Cutting
  Torch burning
Notes: Slide 9.
Important: Burning of lead-based paint is not allowed by HUD or EPA/State or Tribal regulations on residential dwellings or child-occupied facilities.
Discuss the minimum worker protection requirements when conducting Class 3 tasks.

## Slide 10: Which respirator?
10
Depends on exposure
  Class 1
    Must protect you as if your exposure is above the PEL (> 50 µg/m3)
  Class 2
    Must protect you as if your exposure is above 10 times the PEL (>500 µg/m3)
  Class 3
    Must protect you as if your exposure is above 50 times the PEL (>2,500 µg/m3)
Notes: Slide 10.
Briefly discuss the differences between the respirators and the importance of respirator fitting and medical qualification before putting on a respirator.
Your employer must give you a respirator whenever:
1) You ask for one
2) You do a lead-related task
3) Your work exposure to lead exceeds the PEL
Introduce the students to the Respirator Standard (1910.139). Inform them of their employer’s responsibilities.
Discuss Protection Factor (the degree of protection that a respirator provides) and what affects it.
Much more information on respiratory protection and protection factors will be discussed in the OSHA training your employer is required to provide.

## Slide 11: What does my employer have to do?
11
Your employer has to protect you from the hazards in your workplace!
Your employer has to do everything possible to keep the levels of lead in the air LOW!
Notes: Slide 11.
Discuss slide. Give examples of other hazards present on a lead abatement job and the standards which cover that hazard (confined space, noise, chemicals, etc.)

## Slide 12: What other PPE do I need?
12
If the work area has lead in the air above the PEL
  Coveralls
  Gloves
  Disposable shoe covers (booties)
  Face shield or vented goggles
  Hat
    Adequate head protection based on the hazards present in the work area
Notes: Slide 12.
Discuss the importance of PPE; not just a respirator.
Give examples of jobs or activities which would require specific PPE which might not be conventional (e.g., chemically resistant clothing when using caustic or organic chemical strippers).
Disposable shoe covers worn over boots can present a slip hazard. They also most often will not hold up to the wear and tear of a construction site. The best option is for the employer to provide safety shoes or boots that remain at the job site.
A common item spotted on construction and lead abatement sites is the baseball cap; make sure the students understand that any hat or cap worn in the work area becomes lead-contaminated and MUST NOT be worn or taken home unless it has been cleaned first! This is one source of “take-home lead.” If there are hazards present in the workplace that requires the use of adequate head protection, a baseball cap is not acceptable!
Address MSDSs as a good source to determine special PPE required when using chemicals/products.
PPE should be covered in the OSHA training provided by the employer.

## Slide 13: Your workplace
13
Should be kept clean
Should have a clean place for you to change and wash
Should have warning signs posted
WARNING
LEAD WORK AREA
POISON
NO SMOKING OR EATING
Notes: Slide 13.
Discuss continuous cleaning as a means to keep worker exposures down, aid in final cleanup and passing clearance.
Emphasize the importance of personal hygiene.
Discuss the importance of posting signs to prevent untrained, unprotected people from walking into a contaminated area. Also emphasize the importance of sign comprehension (address other language needs).

## Slide 14: You must be trained!
14
If you work with lead at or above the AL
Doing any of the tasks listed under Class 1, 2, or 3
Using any lead compounds that cause eye or skin irritation
Notes: Slide 14.
OSHA’s training requirements are different from EPA, State, or Tribal training requirements. Your employer must provide training on specific topics if any of the above items apply.
This course is designed to satisfy EPA/State/Tribal training requirements; your employer may be combining EPA/State and OSHA training OR you may have to go to another course just on OSHA requirements. Check with your employer!

## Slide 15: Recordkeeping
15
Your employer must keep records of
  Your exposure
  Types of respiratory protection worn
  Your name and social security number
  All medical surveillance information
  Training
  Medical removal situations
Notes: Slide 15.
OSHA requires that these records be kept for a long time.
Ensure that students understand why record keeping is so important and what each of these types of records are.

## Slide 16: Recordkeeping
16
These records must be kept for at least 30 years
  Exception: training records have to be kept for 1 year after you leave that employer
You have the right to see these records
Notes: Slide 16.
You, or your representative, have a right to see your records.
Mention that if you change employers, you might want to get copies of your records to keep with you.

## Slide 17: Medical Surveillance
17
Special exams are required when you work with lead
Two types
  Biological monitoring
  Medical surveillance program
Notes: Slide 17.
Define in general terms the meaning of “medical surveillance.”
Explain the difference between “biological monitoring” and “medical surveillance program.” Remind the students that all the technical terms used in this course are defined in Chapter 10—Glossary and Resources.
Since there may be workers who are familiar with the medical surveillance requirements of working with asbestos, explain that this is a different program and the hazards and the requirements of the lead standard are different.

## Slide 18: Biological Monitoring
18
Two blood tests
  Blood lead level
  Zinc protoporphyrin (ZPP)
Notes: Slide 18.
Make sure they understand that blood tests are invasive, but are the only way to determine if a worker has been overexposed to lead. Explain the difference between air levels and blood levels.
Explain that even though the air levels are low, a worker could have a high blood level (usually due to poor or inadequate decontamination after finishing work). Stress the importance of thorough hand and face washing whenever leaving the work area.

## Slide 19: Medical Surveillance Program
19
Required if you are exposed to lead at or above the AL for more than 30 days in a year
Three types of exams
  Blood tests
  6-part medical exam
  Medical exam and consultation
Notes: Slide 19.
Discuss slide. (Note to instructor: There is no need to go into detail about the medical exam; just indicate the types of tests and body systems that will be involved. If time allows, you may refer back to Chapter 2 and the body systems discussed and the effect of lead on those systems.)

## Slide 20: Medical Exam
20
You have the right to ask for an exam if:
  You feel sick with any signs or symptoms of lead poisoning
  Your BLL is 40 µg/dL or above
  You want to have children
  You have difficulty breathing while wearing a respirator
Notes: Slide 20.
Discuss slide; remind the students of the symptoms of lead poisoning, and the effects of lead on the reproductive system.

## Slide 21: Medical Removal
21
You must be medically removed from the lead exposure on your job if
  Your BLL reaches 50 µg/dL
  Your doctor gives you a written medical opinion
Jorge cannot work with
lead until he is reexamined
in 2 months.
John Q. Public, MD
Notes: Slide 21.
Emphasize the importance of working wet, working smart, and working clean to keep the air and blood lead levels down.
Discuss the medical removal benefits.

## Slide 22: Title X (“Ten”)
22
Title X was passed to
  Make sure people working with lead are trained
  Reduce childhood lead poisoning
  Come up with less expensive ways to get rid of lead-based paint hazards
  Let the public know about the dangers and sources of lead poisoning
Notes: Slide 22.
Explain to the student why Title X was passed by Congress. Discuss the U.S. history of dealing with LBP over the past 30+ years (concentrated on peeling, chipping paint, but initially ignored DUST).
Remind them that Title X was passed to focus more on LBP hazards than just on whether paint is LBP according to the Federal standard of 1.0 mg/cm2 or 5,000 ppm or 0.5 % by weight.
Discuss other important purposes of Title X listed.

## Slide 23: Who has to be trained?
23
EPA or your State/Tribe requires you to be trained and certified.
The other people working with lead that must be trained and certified are:
  Contractors/supervisors
  Inspectors
  Risk assessors
  Abatement planners (designers)
Notes: Slide 23.
If the training is in a State/Tribe with training and certification or licensing regulations, explain the worker certification and/or licensing requirements specific to that State or Tribe. If EPA administers the training and certification program for the State or Tribe, discuss the Federal requirements. Provide them with at least the name, address and telephone number of the agency which handles certification/licensing. Also provide them with an application form, if applicable (some States/Tribes require the approved training provider to give out the application at each class).
Explain the differences between the OSHA training and the State/EPA training requirements. Discuss the possible differences in refresher timing (each year for OSHA; every 1-3 years for State/EPA).

## Slide 24: When does lead-based paint become a hazard?
24
Has deteriorated
Is on a friction or impact surface
Is on a chewable surface and there are teeth marks
Notes: Slide 24.
Discuss EPS’s definitions of LBP hazards.
The Federal government has established, by statute, the level of 1.0 mg/cm2 or 5,000 ppm or 0.5% by weight as LBP.
EPA issued definitions for paint-lead hazards, dust-lead hazards, and soil-lead hazards. It is important for workers to understand the difference between lead-based paint and a paint-lead hazard. Intact LBP is not a hazard (as long as it remains intact)!
Discuss importance of levels for worker protection and cleanup.

## Slide 25: When does lead-based paint become a hazard?
There is lead in the dust equal to or greater than the EPA levels
  Dust level on floors 10 µg/ft2
  Dust level on window sills 100 µg/ft2
There is lead in the soil equal to or higher than the EPA levels
  400 parts per million (ppm) in a play area
  Average of 1,200 ppm in the rest of the yard
<number>
Notes: Slide 25.
Children can come in contact with lead in dust and soil through normal activities.
The soil levels will be determined during a risk assessment, but some projects may require post-abatement soil testing to prove that the contractor and workers did not contaminate the exterior soil.
EPA also established clearance levels for lead in dust. There is more discussion of LBP hazards and clearance in Chapters 4, 8, and 9.

## Slide 26: How do you protect the people living in the housing?
Your State/Tribe or EPA requires an occupant protection plan be written before abatement begins!
Occupant
Protection
Plan
<number>
Notes: Slide 26
Explain that their employer is required to develop an occupant protection plan. Emphasize the importance of the worker’s role in following the plan to protect the health and safety of the people living in the housing.