## Slide 1: What is Lead? Where is it Found?
Chapter 1
Lead Abatement
for Workers Course
Notes: Slide 1.
Direct students to Chapter 1 in their notebook.

## Slide 2: Learning Objectives
2
In this section you will learn:
  What lead is
  Why lead was used
  Where lead is found today
  How you can be exposed to lead
  About the lead paint problem in the U.S.
Notes: Slide 2.
Discuss what aspects of each learning objective are important for the student to learn and understand.

## Slide 3: What is Lead?
3
Lead is a heavy, soft, flexible, blue-gray metal
The chemical symbol for lead is “Pb”
Notes: Slide 3.
Discuss how lead was mined (as a byproduct of smelting silver).
Explain the origin of the symbol for lead (Pb, from the Latin word for lead—“plumbum”).
Discuss some of the historic uses of lead (solder, cosmetics, building materials, drinking water vessels, etc.) and why it was such a useful element.
PICTURE SLIDE(S) TO FOLLOW: Slides 4-6.

## Slide 4
Notes: Slide 4.
Lead ore in its natural state. Called “galena.”

## Slide 5
Notes: Slide 5.
Collection of items which could contain lead.

## Slide 6
Notes: Slide 6.
Advertisement for paint produced by National Lead Company, one of the largest producers of lead-based paint.

## Slide 7: Lead-based paint is . . .
7
“Paint, varnish, shellac, or other coating on surfaces that contain 1.0 mg/cm2 or more of lead or 0.5% (5,000 ppm) or more lead by weight.”
Notes: Slide 7.
Discuss the Federal definition of “lead-based paint.” Explain that this level is only used for paint that is already on a surface.
Explain the difference between the numbers 1.0 mg/cm2, 0.5%, and 5,000 ppm.
Discuss what actions are recommended at these levels of lead if the paint is deteriorated, will be disturbed by renovation, or is creating lead dust.

## Slide 8: Why was lead used?
8
It prevents corrosion
It kills mold and mildew
It is easy to shape
It is strong
It blocks radiation
It blocks sound
It helps paint dry faster
It adds color to and brightens paint
Notes: Slide 8.

## Slide 9: Where is lead found?
9
Paint
Dust
Air
Soil
Gasoline
Industrial releases
Food
Water
Hobbies
Other
Notes: Slide 9.
Clarify that some of these sources are former sources of lead while others are current sources. For example, lead in gasoline is no longer a major source in the U.S. but may have contributed to current levels of lead in the soil.
Discuss reasons that each of these sources may contain lead.
Explain how lead-based paint deteriorates and results in lead dust.

## Slide 10: How You Can Be Exposed
10
Lead dust particles, not even visible to the eye, can be breathed or swallowed
Touching surfaces covered with lead dust may result in eating the dust
Children are especially at risk for lead poisoning because they often put their fingers into their mouths
Symptoms of lead poisoning are the same as other common illnesses
Notes: Slide 10.
In addition to discussing lead dust, talk about lead fumes resulting from heating or burning components painted with lead-based paint.
Discuss the “hand-to-mouth” action of a child and how this is a route of exposure for children.
Discuss how lead abatement workers may ingest lead dust by smoking, eating, or drinking on a lead-abatement site.
Explain how the symptoms of lead poisoning are similar to those of fatigue, the common cold, flu, stress, food poisoning, etc. Note: The next chapter will cover these symptoms in greater detail.
PICTURE SLIDE(S) TO FOLLOW: Slides 11 & 12

## Slide 11
Notes: Slide 11.
Toddler sitting on sister’s lap. Note the basket of cars in his lap.

## Slide 12
Notes: Slide 12.
Toddler putting toy into mouth—a normal activity for young children. If the object has lead dust on it, the dust is now in the child’s mouth.

## Slide 13: Jobs and Hobbies with Lead Exposure
13
Jobs
  Construction trades (e.g., lead abatement workers, carpenters, plumbers, remodelers/renovators, painters, etc.)
  Industrial trades (e.g., lead miners, lead smelter workers, lead crystal makers, etc.)
  Other trades (e.g., firing range employees, police officers, artists, car mechanics, printers, etc.)
Notes: Slide 13.
Discuss how these occupations or hobbies may expose someone to lead.

## Slide 14: The Lead Problem in the U.S.
14
About 38 million homes contain lead-based paint—
  87% of homes built before 1940
  24% of homes built between 1960-1979
Paint containing more than 0.06% lead cannot be used in homes, on furniture, or on toys
Notes: Slide 14.
Discuss geographic locations of homes and components that are likely to contain lead and why.
Discuss the Lead-Based Paint Poisoning Prevention Act.
Explain that lead exposure can occur in any home regardless of the wealth, gender, or race of the occupants. Also explain that home renovation may cause lead poisoning of a child if proper precautions are not taken.
Explain the difference between the CPSC level (600 ppm) of lead in paint and the HUD level (5,000 ppm) of lead in paint.
PICTURE SLIDE(S) TO FOLLOW:
Slide 15 - Peeling paint on the exterior wall of a home.
Slide 16 - Window trough. This is an area where one is most likely to find highest levels of lead dust generated by deteriorating lead-based paint. Note: This is also an impact and friction area.

## Slide 15
Notes: Slide 15 - Peeling paint on the exterior wall of a home.

## Slide 16
Notes: Slide 16 - Window trough. This is an area where one is most likely to find highest levels of lead dust generated by deteriorating lead-based paint. Note: This is also an impact and friction area.

## Slide 17: For More Information
17
Many resources are available
  Protect Your Family From Lead in Your Home
  Home Water Treatment Units: Filtering Fact From Fiction
  Lead Paint Safety: A Field Guide for Painting, Home Maintenance, and Renovation Work
  Toxics Information Series on Lead
Other resources
Notes: Slide 17.
Discuss the available literature on lead-based paint and lead hazards and where students can get a copy of the pamphlets listed in their books.
Discuss the National Lead Information Center, The Lead Listing, etc.
Some students may have access to the Internet—instructors may provide them with the addresses of EPA, HUD, and other information providers.
EPA: www.epa.gov/lead
HUD: www.hud.gov/offices/lead
National Lead Information Center: www.epa.gov/lead/nlic.htm
The Lead Listing: www.leadlisting.org OR 1-888-LEADLIST