## Slide 1: Chapter 6: Putting Skills Together
Lead Dust Sampling Technician
Initial Training Course

## Slide 2: Objectives
Practice the skills taught in the class:
  Choosing appropriate sampling locations
  Taking lead dust samples
  Interpreting results
Notes: This chapter will outline the steps a lead dust sampling technician must take from start to finish when conducting an examination. This chapter includes five activities to help practice implementing the protocols.
By the end of this chapter, students will be able to demonstrate that they can:
  Choose appropriate sampling locations
  Take lead dust samples
  Interpret Results

## Slide 3: Activity 1: Where To Take Samples
You are now going to practice sampling area strategies.
Your instructor will provide you with a hypothetical renovation scenario and diagram.
Read the scenario and mark the location(s) of where you think dust wipe samples should be taken.

## Slide 4: Remember…
Be strategic about laying out sampling area to capture areas were the highest dust generating tasks occurred during the job.
Refer to the Field Guide or Chapter 3 to determine the appropriate places to take your samples.

## Slide 5: Activity 2: Dust Wipe Sampling
You are now going to practice taking dust wipe samples again.
Everyone must demonstrate proficiency.
Follow your instructor’s directions for taking samples.
Notes: Activity 2: Now that the sampling locations have been determined, you will take samples on a variety of surfaces – window sills and troughs, and floors.

## Slide 6: Activity 3: Interpreting the Results
Analyze the results
  Your instructor will provide you with laboratory results to interpret.
  Use EPA lead dust-lead action levels for guidance:
    Floors: < 5 µg/ft2
    Interior window sills: < 40 µg/ft2
    Window troughs: < 100 µg/ft2
Notes: Results and Report Writing
When analyzing the data, follow the guidelines provided in Chapter 4.
Use the EPA action levels/HUD clearance standards when evaluating sample results.

## Slide 7: Activity 4: Translating Results into a Written Report
Translate analyzed results into a written report
  Using the result from the previous activity (Interpreting the Results), write up a report that can be easily understood by the client.
  Use the format introduced in Chapter 5: Writing the Report as a guide.
Notes: Use the information in Chapter 5 (Writing the Report) as a guideline to translate the results into an easy to understand report.