## Slide 1: Chapter 2: Visual Inspection
Lead Dust Sampling Technician
Refresher Training Course

## Slide 2: Objectives
Learn what a visual inspection is
Learn the steps for performing a visual inspection under both EPA’s and HUD’s regulations
Learn when to look for deteriorated paint, visible dust or debris, and paint chips
Record results on a visual inspection form
Notes: This chapter will outline the steps a lead dust sampling technician must take to perform a visual inspection. A visual inspection is the first activity to perform on site for any dust-lead testing. This chapter will also highlight the differences in visual inspection between EPA’s RRP Rule and HUD’s LSHR.

## Slide 3: Visual Inspection
Under both EPA’s and HUD’s rules, visual inspection is the first step in the post-work dust-lead testing process.
The visual inspection determines whether the unit/work area (interior and exterior) is clear of visible dust and debris before lead-dust testing can begin.
Notes: The visual inspection determines whether the unit/work area is clear of conditions that can result in exposure to lead-based paint hazards, such as paint chips, debris, visible dust, and deteriorated paint. If these conditions are present, the unit does not meet EPA’s and HUD’s rules for dust-lead testing. HUD generally requires visual inspection and clearance of an entire unit, with worksite-only clearance allowable under certain conditions.

## Slide 4: Visual Inspection – EPA RRP Dust-Lead Testing
At the conclusion of the renovation, the certified renovator may have conducted a visual inspection to look for paint chips, dust, and debris.
The LDST must conduct a separate visual inspection of the work area to ensure that the area is free of debris and ready for dust-lead sampling.
If any paint chips, dust, or debris are found, the renovation firm should re-clean these areas before the LDST begins to collect dust wipe samples.
Notes: It is important for the lead dust sampling technician to understand that the renovation firm may perform his or her own preliminary visual inspection. The lead dust sampling technician should also perform a visual inspection of the work area. If the lead dust sampling technician observes paint chips, dust, or debris in the work area, these conditions must be brought to the attention of the certified renovator for re-cleaning.

## Slide 5: Visual Inspection – HUD LSHR 1
Addresses entire unit unless worksite-only clearance is allowed.
Do not perform dust-lead testing if unit/work area does not pass visual inspection.
If deteriorated paint, dust, or debris is found, it must be eliminated before dust sampling may begin.
  See Attachments 2-A and 2-B
Notes: Why look for deteriorated paint?
In order to address lead dust in a housing unit, you need to address its sources, including deteriorated lead-based paint. If paint contains lead, deteriorated paint can create chips and dust, which can cause exposure to lead.
NOTE: The LSHR refers to this process as a “visual assessment,” but for purposes of this curriculum, the term “visual inspection” is used.

## Slide 6: Visual Inspection – HUD LSHR 2
Inspect exterior area if:
  Exterior painted surfaces have been disturbed by renovation activity
  Openings to exterior were not sealed during interior work
Inspect ground and outdoor living areas close to affected surfaces
Visible dust or debris must be removed
Deteriorated paint must be eliminated
Dust sampling is not performed for exterior work
Notes: EXTERIOR VISUAL INSPECTION IS NOT REQUIRED IF ONLY INTERIOR WORK IS PERFORMED.
An independent third party is needed to do an exterior visual inspection if the exterior work was done under HUD’s LSHR. A certified lead-dust sampling technician is qualified to perform this inspection.
For more information, see Appendix B or 24 CFR 35.1340.
HUD Note: HUD requires sampling technicians to verify with renovator that openings to the exterior are closed during interior work. If not closed, exterior visual inspection is required for interior work. Dust-lead sampling is not required for exterior work. There are no dust-lead action levels for porches, balconies, railings, or other horizontal exterior features.

## Slide 7: Exterior Debris

## Slide 8: Visual Inspection – HUD LSHR 3
Identify any paint that is not intact:
  Chipping
  Peeling
  Chalking
  Cracking
  Holes, moisture, and friction damage
Hairline cracks and nail holes are not considered deteriorated paint
Notes: Deteriorated paint is any paint that is not intact. It does not have to be peeling paint.
As seen in the following photographs, deteriorated paint can include:
Chipping paint on door and window trim
Peeling paint and flaking paint on walls and window sashes
Paint with small bubbles that look like blisters
Paint with lines and cracks that make it easy to peel the paint away
Paint that is “chalking” or creating chalk-like dust
Note: Hairline cracks and nail holes are not considered deteriorated paint.

## Slide 9: Visual Inspection – HUD LSHR 4
Dust
  Dust you can see
Debris
  Pieces of wood, bits of plaster, and various other building pieces covered in paint
Paint chips
  Small pieces of paint
Notes: What do visible dust, paint chips, and debris look like?
Visible dust is dust you can see.
Debris can be pieces of wood, bits of plaster, and various other building pieces covered with paint that are left in the room or near where the work was done.
Paint chips are little pieces of paint. Chips can be even smaller than your fingernail or larger than your hand. Look for paint chips on floors and windows.

## Slide 10: Visual Inspection – HUD LSHR 5
Chipping Paint

## Slide 11: Visual Inspection – HUD LSHR 6
Holes in wall

## Slide 12: Visual Inspection – HUD LSHR 7
Deteriorated Paint

## Slide 13: Visual Inspection – HUD LSHR 8
Cracking Paint

## Slide 14: Visual Inspection – HUD LSHR 9
Moisture Damage
Notes: Moisture can be the cause of many paint problems. In this case, it is causing the paint to bubble.

## Slide 15: Visual Inspection – HUD LSHR 10
Friction Damage

## Slide 16: Visual Inspection – HUD LSHR 11
Be precise about locations.
Write down results as you go.
Write down other information, indicating source.
See sample visual inspection form (Attachment 2-B)
Notes: When recording the results of a visual inspection, take the following steps:
Be precise about locations (e.g., room descriptions and/or specific areas in room) where visible dust, debris, paint chips, and deteriorated paint were found.
Write down results as you go along.
Write down other information the client provides about the surface in question.
See Completed Sample Visual Inspection Form in Attachment 2-B.

## Slide 17: Review
Visual inspection is the first step in the post-work dust-lead testing process.
EPA’s visual inspection determines that the area is free of dust and debris before dust-lead testing can begin.
HUD’s visual inspection also checks for deteriorated paint and generally covers the entire unit unless worksite-only clearance is allowed.
Visual inspection as part of post-work dust-lead testing is the responsibility of the certified lead-dust sampling technician.
Be methodical in your visual inspection, and record results in a consistent manner.
Notes: See Slides 2-3 through 2-16 for information and answers.
See Slide 2-3 for information and answers.
See Slides 2-3 through 2-9 for information and answers.