## Slide 1: Chapter 4: Selecting a Laboratory and Interpreting Results
Lead Dust Sampling Technician
Refresher Training Course

## Slide 2: Objectives
Select an EPA-recognized lab
Maintain a chain of custody
Review and interpret lab results
Notes: After performing lead dust wipe sampling, you will need to submit the samples to a laboratory for analysis and interpret the laboratory results to determine the levels of lead dust in a unit. This chapter describes the steps you will need to take.
At the end of this chapter, you will be able to do the following:
  Select an EPA-recognized laboratory and explain why proper selection is important
  List the important steps to ensure samples are not tampered with or lost, maintaining a chain of custody
  Review and interpret the laboratory results

## Slide 3: Selecting a Laboratory
Submit samples to a lab recognized by EPA’s National Lead Laboratory Accreditation Program (NLLAP)
To locate a lab
  Call the National Lead Information Center (NLIC) at 1-800-424-LEAD
  Visit the EPA web site at https://www.epa.gov/lead/nllap
See the fact sheet “Selecting a Lead Laboratory” at the end of this chapter.
Notes: All samples must be submitted to a laboratory recognized by the EPA’s National Lead Laboratory Accreditation Program (NLLAP) to be proficient in lead in dust analysis.
  The NLLAP provides the public with a list of recognized laboratories for analyzing lead in dust samples. You can contact the National Lead Information Center (NLIC) at 1-800-424-LEAD, or visit the EPA website at www.epa.gov/lead/nllap for an up-to-date list of NLLAP-recognized laboratories. The “Selecting a Laboratory” fact sheet (EPA 740-F-26-003) with basic information is available online.
  For a laboratory to become EPA-NLLAP recognized, it must participate in the Environmental Lead Proficiency Analytical Testing (ELPAT) Program and undergo a quality system audit, including an onsite assessment by a laboratory outside accreditation body participating in the NLLAP, such as the American Industrial Hygiene Association.
It is important to recognize that not every recognized laboratory will meet your needs. Taking the time to select a good laboratory will save you time and effort in the long run. Knowing the costs associated with laboratory supplies and the analysis will also help you calculate the fees you will charge customers. Even if your company has selected a laboratory for you to work with, it is a good idea to ask a few simple, straightforward questions so you can find out whether the laboratory meets some basic quality criteria.
See Attachment 4-A: Questions to Ask Laboratory.

## Slide 4: Questions To Ask Laboratories
Tell the lab you will be collecting dust wipe samples for lead.
Ask:
  Is the laboratory recognized to analyze for lead in dust by NLLAP?
  Will sampling materials be provided?
  What is the turnaround time for analysis?
  Can the laboratory analyze composite samples? (If the client wants composite samples)
  What is the cost per sample?
Notes: Review Attachment 4-A: Questions to Ask a Laboratory.

## Slide 5: Quality Control in the Field
Submit blank wipe samples.
Duplicate, or side by side sampling can be used to check lab consistency.
Review all of your sample collection and chain-of-custody forms.
Carefully review all lab results.
Notes: Dust-lead testing and analysis require a great deal of care and precision by both you and the laboratory. Follow the steps above to help control the quality of the lab results. Each step is discussed in further detail on the following slides.

## Slide 6: Review Your Sample Collection Form
Confirm all information is recorded clearly and correctly.
  Sample numbers
  Sample locations
  Sample dimensions
Keep a copy for your records and note blanks.
Notes: In Chapter 3, we described how to record sample information on the sample collection form clearly and accurately. Before you send the samples to the laboratory, you should check your sample collection form to confirm that all of the following information is recorded clearly and correctly.
  Sample numbers - Samples should be numbered sequentially, in the order you took them. (This information must be included accurately on the laboratory chain-of-custody form.)
  Sample locations - These should be precise. For example, “left window on back wall in master bedroom” is better than “bedroom window.”
  Sample dimensions for dust wipe samples - As discussed in Chapter 3, these dimensions are extremely important and should be recorded to the nearest 1/8 of an inch.
After completing the form, it is essential that you keep a copy for your records and to note the ID numbers of your blank samples.

## Slide 7: Chain of Custody
A record of each person who handles the sample from the time it is collected until it is sent to the lab.
The lead dust sampling technician is responsible for maintaining chain of custody until he or she transfers custody of the samples.
Include information on sampling form
A sample chain-of-custody form is shown on the next slide, and as an attachment to this chapter.
Notes: It is important that samples are not lost before or during the analysis process. To trace the path of the sample, you should establish a “chain of custody.” This simply means that every person who handles the sample must sign and date a form.
Who is in the chain of custody? People in the chain of custody may include:
  Lead dust sampling technician
  Technician’s supervisor
  Person packing the samples for shipment
  Person picking up and shipping the samples
  Person receiving the shipment at the laboratory
Maintaining the chain of custody - Ensure that the chain of custody is maintained from when you take the samples until you transfer custody of the samples.
  Space for documenting the chain of custody may be included as part of the sample collection form or you may use a separate form. There should be enough space for each individual handling the sample to sign and date the form – 5 to 7 lines should be sufficient.
  You should also keep a copy of any shipping or mailing forms documenting when the samples were sent to the laboratory.
  You should send the package with delivery confirmation and return receipt requested, or the equivalent shipping record.

## Slide 8: Chain-of-Custody Form
Notes: This is the chain-of-custody form that can be found at the end of the chapter as Attachment 4-B.

## Slide 9: Evaluating Laboratory Results for Single Samples
Check for appropriate units (g/ft2)
Compare results to the EPA action levels/HUD clearance standards:
  Floors < 5 µg/ft2 passes
  Sills < 40 µg/ft2 passes
  Troughs < 100 µg/ft2 passes
Notes: When you receive the results from the laboratory, you must interpret them to determine whether they pass or fail to clear below the dust-lead action levels. This section describes dust lead hazards and the process used to evaluate the sample results. Specifically, you will need to evaluate the laboratory results, converting them if necessary, and comparing them to the federal or state standards.
To evaluate the laboratory results, you may need to take the steps listed below. These steps should be implemented as follows:
Step 1: Check the units. If results are not reported in µg/ft2, use the conversion table (see Attachment 4-C: Worksheet for Performing Mathematical Conversions for Dust Samples).
Step 2: Compare the results to the EPA dust-lead actions levels. Once you have made the necessary conversion, you can compare the laboratory results to the appropriate EPA dust-lead actions levels. EPA action levels have been developed for lead dust on floors, interior window sills, and window troughs. It is important to recognize that the levels for lead dust are different for each of these three surfaces. If test results equal or exceed the action levels, the unit, worksite, or common area represented by the sample fails to clear the dust-lead test.

## Slide 10: Activity: Interpreting Laboratory Results
Turn to Attachment 4-D.
Answer the questions.
Be prepared to explain your answers.

## Slide 11: Evaluating Laboratory Results for Composite Samples
Location | 2 Subsamples | 3 Subsamples | 4 Subsamples
Floors | 5 µg/ft2 | 7 µg/ft2 | 2.5 µg/ft2
Sills | 40 µg/ft2 | 27 µg/ft2 | 20 µg/ft2
Troughs | 100 µg/ft2 | 67 µg/ft2 | 50 µg/ft2
Notes: Composite samples determine the average of the dust lead levels on the surfaces that make up the composite.
To minimize the chance that any individual surface included in the composite does not fail to clear below the action levels, composite samples that contain more than two subsamples are compared to more stringent standards than are single-surface samples.

## Slide 12: Avoiding Common Mistakes
Mistaking weight (mass) for surface loading by using incorrect units (g for g/ft2)
Not submitting blank samples
  Labeling or recording in the sample log blank samples as blanks
Not maintaining a chain of custody
Notes: Listed above are some common mistakes you might make while performing any of the activities listed on the previous slide.
  Mistaking the units. One common mistake is not understanding the units of measurement provided in the lab report. When the results come from the laboratory, check whether they are provided in µg or µg/ft2. If they are in µg, you must convert them to µg/ft2 before recording them on your report and interpreting results. Discuss with your laboratory how results are reported.
  Failing to submit blank samples. Another common mistake is not submitting blank samples. Without this mechanism, you have no way of verifying if the laboratory results were uncontaminated, or that you used good sampling techniques. Submit one blank sample for every unit sampled.
  Failing to maintain the chain of custody. This is your only mechanism to track the handling of the sample. The chain-of-custody form must be maintained from the time you take the dust wipe sample until you transfer custody. Re-sampling is recommended if this document is not maintained.

## Slide 13: Summary
Select an EPA-recognized lab.
  Call 1-800-424-LEAD
  Visit www.epa.gov/lead/nllap
  Ensure that the lab is EPA-recognized for the analysis of lead in dust
Maintain a chain of custody.
Interpret lab results.