## Slide 1: Module 1: Why Should I Be Concerned About Lead Paint?
Lead Safety for Renovation, Repair, and Painting
Initial Training Course

## Slide 2: Overview
Definition of lead-based paint
Health effects related to lead exposure
Why lead-contaminated dust is a problem
Notes: Upon completion of this module, you will be able to explain:
What lead-based paint is and why it is a problem for renovators
The health risks of lead to children and adults
Why we are concerned with lead-contaminated dust

## Slide 3: What Is Lead-Based Paint?
Federal standards define lead-based paint as:
  Any paint or surface coatings that contain lead equal to or in excess of 1.0 milligram per square centimeter or more than 0.5 percent by weight
  Some states and localities regulate paint with lower concentrations of lead
  It is the primary source of lead-contaminated dust in housing
Why was lead used in paint?
Lead was added for color and durability
Lead-based paint was banned for residential use in 1978
Notes: Federal standards define lead-based paint.
  Lead-based paint is any paint or surface coatings that contain lead equal to or in excess of 1.0 milligram per square centimeter or more than 0.5 percent by weight.
  Paint with concentrations of lead lower than the definition above can still cause health problems. Even paint with a small amount of lead can account for a lot of lead in airborne or settled dust.
  Information on how to determine if a property contains lead-based paint is provided in Module 3.
Some states and localities regulate paint with lower concentrations of lead.
  You should check with your state and local health departments to see if they have requirements that are more stringent than the federal requirements.
Why was lead added to paint?
  Lead was added for color and durability.
  Lead was also added to some other surface coatings, such as varnishes and stains.
Lead-based paint was banned from residential use in 1978
  In 1978, the Consumer Products Safety Commission banned the sale of lead-based paint for residential use. In practice, this means that homes built in 1978 could still have used lead-based paint, because existing supplies of paint containing lead would still have been available.
  This is why the year of construction is such an important consideration.

## Slide 4: Health Effects of Lead
Hazardous to children
  Damages the brain and central nervous system
    Can cause decreased intelligence, learning and behavioral problems, hyperactivity, and growth and development problems
  Damage can be long-term, affecting children throughout their lives
Hazardous to pregnant women
  Harm the fetus
Also hazardous to workers and other adults
  Heart related problems and high blood pressure
  Infertility
  Fatigue
Notes: Children under six are most at risk from small amounts of lead.
Children are especially vulnerable to lead because their growing bodies and brains are more sensitive to lead’s harmful effects. During normal and frequent playing or hand-to-mouth activity, children may swallow or inhale dust from their hands, toys, food or other objects.
In children, lead exposure can cause:
  Damage to the brain and nervous system and kidney damage
  Lower IQ, underperformance in school, decreased ability to pay attention and hyperactivity
  Learning and behavior problems
  Hearing and speech problems
  Growth and developmental effects
Pregnant women: Lead can build up in the body over time, settling, in the bones. This stored lead can be passed from the mother to the fetus during pregnancy and can cause increased risk of:
Miscarriages
The baby being born too early or too small
Harm to a developing fetus’ brain, kidneys and nervous system
In adults lead exposure can cause:
Heart related problems and high blood pressure
Infertility in men and women
Digestive problems
Nerve disorders
Learning, memory and concentration problems
Muscle and/or joint pain

## Slide 5: Symptoms Of Lead Poisoning are Not Always Obvious
Lead exposure often occurs with no obvious symptoms
Someone exposed to lead may look and act healthy
Lead exposure frequently goes unrecognized and can easily be misdiagnosed
A simple blood test is the best way to determine if someone has been exposed to lead
Notes: Someone with lead poisoning may not have visible signs or symptoms.
Some of the signs and symptoms of lead poisoning are non-specific, and are frequently attributed to other causes like flu or other viruses.
Several of the symptoms people with lead exposure sometimes complain about include:
  Headache
  Stomach ache
  Irritability
  Tiredness
  Loss of appetite
  Joint and/or muscle pain
Because many signs and symptoms are non-specific or similar to flu symptoms, lead exposure in children is often difficult to see and so parents may not know they need to get immediate medical attention for their children. This is critical for young children. The longer a young child stays untreated, the higher the risk of permanent brain damage.
Workers with an occupational exposure to lead need to inform their doctors in order to give them all the background needed for an adequate evaluation of symptoms as possibly related to lead exposure.
A simple blood test is the best way to determine if someone has been exposed to lead.
The amount of lead in blood is measured in micrograms per deciliter (µg/dl) of the blood, a very small unit of measurement. A microgram is one millionth of a gram. That is like one penny out of $10,000. For reference, a standard size paper clip weighs about one gram, or one million times more than a microgram. A microgram is a very small amount of lead. Remember how small this amount of lead is as it applies to dust cleanup when we get to Module 4: Contain Dust During Work, Module 5: During the Work, and Module 6: Cleaning Activities and Checking Your Work.

## Slide 6: Why are Dust and Debris a Problem?
Renovation activities that disturb lead-based paint create dust and debris and debris becomes dust
Lead-contaminated dust is poisonous
Very small amounts of lead-contaminated dust can poison children and adults
  Children swallow dust during ordinary play activities
  Adults swallow or breathe dust during work activities
Workers can bring lead-contaminated dust home and expose their families
Notes: Dust and debris from renovation, repair, and painting jobs in pre-1978 housing and child-occupied facilities may contain lead.
Pre-1978 paint may contain lead.
Renovation, repair and painting jobs disturb paint that may contain lead. Any activity involving surface preparation, such as hand-scraping, power sanding, the use of heat guns above 1100O Fahrenheit, and open flame burning, can generate lead dust. More complicated tasks such as removing building components and demolishing walls also can create a lot of dust.
Small amounts of lead-contaminated dust can poison children and adults.
A tiny amount of lead can be extremely harmful.
Lead dust particles are often so small that you cannot see them, yet you can breathe or swallow them. These smaller, inhaled or swallowed dust particles are more easily absorbed by the body than larger particles, and can therefore more easily cause poisoning.
Lead dust may be breathed or swallowed by children, residents and workers.
Through normal hand-to-mouth activities, children may swallow or inhale dust on their hands, toys, food, or other objects. Children may also ingest paint chips.
Adults can swallow or breathe dust during work activities.
  When workers perform activities such as scraping and sanding by hand, or use a power sander or grinding tool, dust is created, which goes into the air that they breathe.
  If workers eat, drink, smoke or put anything into their mouths without washing up first, they may swallow lead dust.

## Slide 7: A Little Dust Goes a Long Way
You can’t see it
It’s hard to sweep up
It travels
One gram of lead-based paint can contaminate a large area!
Notes: A little dust goes a long way.
You can’t see it. Even a floor that looks clean can have lead dust on it. Only a laboratory test can tell you for sure if an area is contaminated with lead.
It’s hard to sweep up. Normal cleaning methods will not pick up all the dust in a work area. Sweeping is not enough. You need to use water, detergent and a HEPA vacuum to clean up dust effectively.
It travels. Once dust is released, it is easily tracked around, inside and outside the work area. And, an exterior painting job can contaminate the inside of a home as the dust, chips and soil are tracked inside.
Later in this course we will discuss in detail the EPA dust-lead reportable levels and action levels. The limits are included here to reinforce the idea that a very small amount of lead can cause health problems. These numbers represent the amount of lead measured in micrograms (1 millionth of a gram) that is allowed in an area one foot wide and one foot long (one square foot). More than this amount of lead in the specified areas is hazardous and actionable.
EPA & HUD use these standards when clearance is performed:
  Floors: 5 µg/ft2
  Interior window sills: 40 µg/ft2
  Window troughs: 100 µg/ft2
NOTE: Tribes, states, territories, and localities may enforce lower standards.

## Slide 8: Video of a Contractor Who Poisoned His Own Kids
Notes: Contractor discusses how lead safe work practices could have protected his kids from becoming lead poisoned.
In this video Kevin Sheehan, a contractor, discusses how he poisoned his family while working on older houses which contained lead-based paint. Kevin also discusses the need for lead safety precautions during renovation work, shares the lessons he learned, and reveals what can be done to keep people safe during work in older homes with lead-based paint.
Link to video on YouTube: https://www.youtube.com/watch?v=K0rM6Jglptc

## Slide 9: Video Clip of Parent of a Child Poisoned by Renovation
Notes: Parent Discusses Child Poisoned by Renovation Undergoing Treatment.
In this video Maurci Jackson, a parent whose child became lead poisoned, discusses how hard it was to watch her daughter undergo chelation therapy treatments to remove lead from her body. Maurci shares her fears about her child’s future health after being lead poisoned and her frustration that childhood lead poisoning is completely preventable if those who disturb lead-based paint would just considered the consequences of working with lead improperly. She emphasizes the need for lead safety precautions and planning to prevent childhood lead poisoning .
Note: Chelation therapy is a treatment that uses a medication to remove lead from the body when blood lead levels are very high.

## Slide 10: Now You Know…
What lead-based paint is
The adverse health effects of lead
Dust is the problem
Lead poisoning is hard to spot and the effects can be long-term
Kids are at risk for lead poisoning
Lead poisoning is preventable