## Slide 1: Module 5: During the Work
Lead Safety for Renovation, Repair, and Painting
Initial Training Course

## Slide 2: Overview
Traditional renovations create airborne dust
Prohibited practices
Protect yourself and make a personal protective equipment toolkit
Control the spread of dust.
Hands-on exercise (Skill Set #6)
Notes: Requirements in the EPA RRP Rule:
The RRP Rule prohibits the use of certain practices. These prohibited practices are discussed in this module. This module also contains recommendations regarding how to reduce dust during work activities that are not specifically required or addressed in the RRP Rule. Certain practices are prohibited by the RRP Rule. Beyond this you are free to use whatever practices get the job done, provided that all dust and debris you generate stays in the work area and does not migrate to other areas or properties. The recommendations in this section will assist you by reducing the amount of dust released during work. Dust reduction in the work area will make the workplace safer for employees, and will make cleaning easier.
Upon completion of this module, you will know:
Work practices prohibited under the RRP Rule because they create dangerous amounts of dust and paint chips
The work practices to use to control dust, debris or paint chips
The tools you will need.

## Slide 3: Traditional Renovations Create Airborne Lead Dust
* OSHA Permissible Exposure Limit (PEL) = 50 µg/m3
*
Notes: The data above is from the Lead Exposure Associated with Renovation and Remodeling Activities: Summary Report prepared by Battelle for the U.S. Environmental Protection Agency in May 1997 (Document; EPA-747-R-96-005).
Traditional work practices create large amounts of dust!
  This chart shows amounts of lead dust created by three common construction practices: hand sanding, power sanding, and interior demolition.
    Note: The RRP Rule restricts the use of power sanders, among other things, see following page for more information.
  By using safe work practices, you can control and significantly reduce the amount of dust created on the job. Controlling lead dust at the source of generation is important because dust released into the air will eventually become settled dust on the ground. Later in this chapter, you will learn safe work practices that can replace these prohibited work practices. In this section you will also find best practice recommendations for reducing dust in the work area.
Note: If you have questions regarding OSHA’s air sampling requirements, OSHA provides a consultation service that is separate from enforcement and will not result in penalties or citations. This service can be accessed at https://www.osha.gov/consultation.

## Slide 4: Prohibited Practices
Open-flame burning or torching
Heat gun above 1100°F
Power sanding, power grinding, power planing, needle guns, abrasive blasting and sandblasting, without shroud or containment system equipped with HEPA vacuum
Notes: The EPA RRP Rule does not specifically address what measures must be taken to reduce the amount of dust generated on the job. Rather, the rule lists three prohibited practices that must not be used on the job.
Open-flame burning or torching of painted surfaces.
Heat gun above 1,100º F (degrees Fahrenheit).
The use of machines designed to remove paint or other surface coatings through high-speed operation such as sanding, grinding, power planing, needle gun, abrasive blasting, or sandblasting unless such machines have shrouds or containment systems and are equipped with a HEPA vacuum attachment to collect dust and debris at the point of generation. Machines must be operated so that no visible dust release of air occurs outside the shroud or containment system.
A key to minimizing the spread of dust and paint chips is not to use certain traditional work practices known to create large amounts of dust and debris.
Open-flame burning or torching of paint and using a heat gun above 1100º F create very fine lead dust particulates (“fume”) that are dangerous for workers to breathe. The small lead dust particles created by burning and heating also settle on surrounding surfaces and are very hard to clean up.
Power sanding, power grinding, power planning, needle guns, abrasive blasting, and sandblasting create a large amount of dust that floats in the air and then settles on surfaces inside and outside of the work area.
See Appendix 5 Steps to LEAD SAFE Renovation, Repair and Painting for more information.

## Slide 5: Specialized Tools
Large jobs may require special considerations to get the job done, like:
  Power tools designed to remove paint or other coating must have shroud or containment system equipped with HEPA vacuum
  Pneumatic and battery powered tools to protect against shock hazards
  Specialized planning and containment
Notes: Only power tools designed to remove paint or other surface coatings equipped with attached HEPA-filtered local capture ventilation may be used when lead-based paint is present or presumed to be present.
  Electric power tools such as sanders, grinders, circular saws, reciprocating saws, planers and drills produce dust and debris. Because they are electric, wet methods are not safe. Pneumatic and battery powered tools prevent shock hazards. Such tools must have a shroud or containment system equipped with a HEPA vacuum attachment to contain the dangerous lead dust and paint chips that are generated by their use.
  Tools with attached HEPA-filtered capture ventilation collect and filter dust and debris as it is created. A shroud at the head of the tool helps to contain the dust and paint chips as the vacuum draws away dust and debris for safe storage in the vacuum canister. This makes the job cleaner and safer.
  Abrasive blasting is very effective at removing large areas of paint quickly, but these practices require special HEPA filtration equipment that contains the blast medium, dust and paint chips without releasing dust into the air or into the containment.
Containment is even more important when using specialized tools.
  Proper containment and cleaning are crucial even when using HEPA-filtered specialized tools. These tools generate a lot of dust inside a localized negative pressure (vacuum) environment. If the vacuum fails or if the vacuum seal created by the shroud is broken, large volumes of dust can be released. Nonetheless, HEPA-filtered specialized tools can reduce dust levels when used properly, and can aid work production by shortening the cleaning time and lowering cost.
  See the Shopping List of tools and supplies found in Appendix 5 Steps to LEAD SAFE Renovation, Repair and Painting for more information.

## Slide 6: Protect Yourself
Workers should wear:
  Disposable painter’s hat
  Disposable coveralls
    Repair tears with duct tape
    Dispose of in plastic bag
  Disposable N-100, R-100 or P-100 respirator
Wash face and hands frequently and at the end of each shift.
  Washing helps to reduce hand-to-mouth ingestion of lead dust
OSHA may require more protection depending on what work is done
Notes: Workers should protect themselves.
Painter’s hats are an inexpensive way to keep dust and paint chips out of workers’ hair. Painter’s hats can be easily disposed of, and should be disposed of at the end of each day or at the end of the job.
Disposable coveralls are a good way to keep dust off workers’ street clothes and reduce the chance of carrying dust away as they come and go. Remember to use a HEPA vacuum to remove dust and debris from coveralls or other outerwear (a “dry decon”) before exiting the work area. Some coveralls have a hood to keep dust out of hair.
Respiratory protection. Employers should consider that workers should wear respiratory protection, such as a disposable N-100, R-100 or P-100 respirator, and follow OSHA’s Respiratory Protection Standard (29 CFR 1910.134) to prevent them from inhaling lead dust. These respirators are particulate-filtering respirators and would not be appropriate as protection from chemical stripping compounds.
You should wash your hands and face at the end of each shift. Workers should wash their hands and faces periodically to avoid ingesting lead dust. You should also wash well before eating, drinking or smoking. You should not eat, drink, or smoke in the work area. Some of the dust that settles on the face around the mouth invariably finds its way into the mouth. Workers should also wash at the end of the day before getting in their car or going home to avoid taking lead dust home to their families.
Personal protection is especially important on high dust generating jobs when lead-based paint or lead- contaminated dust is disturbed, and while cleaning is being performed. However, the same level of protection is not necessary during the planning, testing or setup phases of the work when lead is not being disturbed.
The protective equipment listed above is meant to show what is needed during activities that disturb lead-based paint and lead-contaminated dust. Depending upon work practices used, OSHA rules may require employers to take further steps to protect the health of workers on the job.
OSHA provides additional information on working with lead in their Safety and Health Regulations for Lead in the Construction Industry (29 CFR 1926.62).

## Slide 7: Control the Spread of Dust
When you leave the work site, clean yourself and your tools
  Remove shoe coverings and HEPA vacuum or wipe shoes
  Walk on disposable tack pads to remove dust from your soles
  HEPA vacuum and remove coveralls, and then HEPA vacuum your clothes
  Remove gloves, if used, and carefully wash your hands and face
At the end of the day don’t take lead home to your family on your clothes or in your car
  HEPA vacuum clothes, shoes, etc.
  Change your clothes and dispose of disposable clothing or place dusty work cloths in a plastic bag to wash separately from household laundry
Don’t hug your family until are clean!
  Wash your hands and face
  Shower as soon as you get home
Notes: Precautions to take when leaving the work site
  When you leave the work site (the area covered by protective sheeting or the work room), take precautions to prevent spreading dust and paint chips on your clothes and shoes to other parts of the residence.
  Every time you leave the plastic sheeting around the surfaces being renovated, remove the disposable shoe covers and wipe or vacuum your shoes before you step off the plastic sheeting. A large disposable tack pad on the floor can help to clean the soles of your shoes.
  Every time you leave containment, HEPA vacuum and remove your disposable coveralls and disposable shoe covers. Clean and/or vacuum your shoes and wash your hands and face.
  At the end of the day:
    Change your clothes and wash yourself to reduce the risk of contaminating your car and taking lead dust home to your family.
    Before leaving the worksite, remove any protective clothing, HEPA vacuum dust from non-protective clothing, and thoroughly wash your hands and face. Throw away disposable clothing or place clothing in a plastic bag to stop dust from getting on other clothes at home.
    As soon as you arrive home, take a shower and be sure to thoroughly wash your hair, especially before playing with children. Wash your work clothes separately from regular household laundry to stop lead from getting on your other clothes.
    Be clean before you come in contact with family members, especially children. Remember the video about the contractor who lead-poisoned his own kids.

## Slide 8: Cleaning During the Job
A clean work site reduces the spread of dust and paint chips
Clean as you work
  HEPA vacuum horizontal surfaces
  Remove debris frequently
  Remove paint chips as they are created
  As building components are removed, wrap and dispose of them immediately
Clean frequently (in stages, at least daily)
Notes: Clean the work site frequently.
  Cleaning the work site frequently as the job progresses will reduce the spread of dust and paint chips. Daily cleaning need not be as thorough as the final cleaning. It should, however, keep debris, dust and paint chips from piling up and spreading beyond the immediate work site.
Daily cleaning during the job includes:
  Removing debris frequently. Seal and dispose of construction debris as it is created.
  Vacuuming horizontal surfaces frequently. HEPA vacuum dust and paint chips that settle on surfaces, including protective sheeting. As workers come and go during the work day, this debris is easily spread. Periodic cleaning throughout the work day helps minimize the spread of dust.
  Collect paint chips as they are created. When removing paint, paint chips can spread outside the immediate work area as workers come and go from the work site. To keep paint chips from spreading beyond the work site, make sure that they are collected as they are created. Periodically HEPA vacuum and dispose of paint chips.
  Wrapping and disposing of removed components. When removing painted components such as windows, trim and cabinets, wrap them in plastic sheeting and dispose of them in stages. This will prevent the spread of debris and keep residents, especially children, from coming into contact with lead dust created by the work.
  Safe Waste Disposal. All renovation waste from the work area must be contained prior to its removal, storage, or disposal to prevent releases of dust and debris. Chutes for removing waste from the work area must be covered. At the conclusion of each work day, collect waste and store it in containment, in an enclosure, or behind a barrier that prevents the release of, and access to, dust and debris. When transporting waste from the renovation work area it must be contained to prevent the release of dust and debris.
  How often should cleaning during the job take place?
  The goal is to keep dust and debris under control, not to maintain a completely spotless site at all times. Every job is different; so clean when it makes sense to, without hindering progress. Remove large amounts of dust, paint chips, and debris frequently, at least daily.

## Slide 9: Exercise: Personal Protective Equipment
Watch the instructor dress a volunteer in personal protective equipment
  Skill Set #6 – Personal Protective Equipment
Practice putting on and taking off personal protective equipment
Dispose of used equipment properly and clean up
Notes: Personal Protective Equipment
This exercise gives you a chance to learn and practice the proper steps for putting on and taking off PPE, disposing of used equipment, and decontaminating yourself. The slide provides basic instruction.

## Slide 10: Now You Know…
Work practices that produce dust
Work practices prohibited by EPA and HUD
How to work safely around lead-based paint and lead dust
Proper use of personal protective equipment
Notes: The practices you learned in this module will help you make less dust as you work.
In the next module, we will talk about how to conduct final cleaning of the work area, and how to verify that the cleaning is complete.