## Slide 1: Module 7: Recordkeeping
Lead Safety for Renovation, Repair, and Painting
Initial Training Course

## Slide 2: Overview
In this section, you will learn about records required for each job
Records must be retained and made available to EPA, upon request, for 3 years following completion of a renovation
Notes: Language of the RRP Rule is:
“Firms performing renovations must retain and, if requested, make available to EPA, all records necessary to demonstrate compliance…for a period of three years following completion of the renovation.”

## Slide 3: On-The-Job Records
Copies of the certified renovator’s initial and most recent refresher course certificates (must be kept on site)
Lead-based paint testing results when an EPA-recognized test kit is used
Laboratory results when a paint chip sample is obtained by a certified renovator
Proof of owner/occupant pre-renovation education
Non-certified worker training documentation
Notes: The certified firm must designate (in writing) a certified renovator to be responsible for each renovation job in target housing or a child-occupied facility. This is the logical person to organize and maintain on-the-job records during the work. On the jobsite, the records should be kept in a safe, secure, clean and dry place. Once the project is complete, some records can be filed with other firm records while others may need to be moved to the next job site.
Records to be maintained on site include:
Copies of the certified renovator's initial and most recent refresher course completion certificates.
Records to be maintained to document the job:
Copies of the certified renovator's initial and most recent refresher course completion certificates.
Non-certified worker training documentation.
Designation of a certified renovator to the job.
Information on and results of use of EPA-recognized test kits or paint chip samples by a certified renovator who acted as the representative of the certified firm at the job site and who conducted testing for the presence of lead-based paint on surfaces to be affected by the renovation.
Lead-based paint inspection reports provided by a certified lead inspector or risk assessor, if applicable.
Proof of owner/occupant pre-renovation education
Any other signed and dated documents from the owner(s) and/or residents regarding conduct of the renovation and requirements in the EPA RRP Rule.
All reports required from the certified firm and the certified renovator by the EPA RRP Rule.

## Slide 4: Recordkeeping: Pre-Renovation Education Records
Target Housing – Individual Units:
  Must acquire either written proof of receipt by an adult occupant or proof of delivery/unsuccessful delivery of Renovate Right pamphlet; or
  Written proof of receipt of Renovate Right pamphlet by owner or proof of mailing (if mailing, send 7 days prior to renovation)
Target Housing - Common Areas (Two Options):
  Provide written notification to each affected unit and make Renovate Right pamphlet available on request; or
  Keep copies or pictures of the signs and notices posted
Child-Occupied Facilities:
  Written proof of receipt of Renovate Right pamphlet by owner or proof of mailing required (If mailing, send 7 days prior to renovation)
  Maintain proof of receipt by owner or adult representative; or certify in writing that Renovate Right pamphlet has been delivered to facility
  Keep copies or pictures of the signs and notices posted
Notes: In addition to the requirements above, maintain all records for pre-renovation education activities that contain information about the following:
Target housing – individual units:
When contacts with the owner and occupants were attempted.
Written proof of when contacts were made.
Target housing – common areas:
Documentation of when and to whom written notification was delivered for each unit affected.
What notices were posted, and when and where they were posted.
Child-occupied facilities:
When contacts with the owner and occupants were attempted.
Written proof of when contacts were made.
Whether and when contact was made with the owner or adult representative of the child-occupied facility.
What notices were posted, and when and where they were posted.

## Slide 5: Sample Confirmation of Receipt of Renovate Right
I have received a copy of the lead hazard information pamphlet, informing me of the potential risk of the lead hazard exposure from renovation activity to be performed in my dwelling unit. I received this pamphlet before the work began.
  Recipient Signature:__________ Printed Name: __________ Date:__/__/__
Renovator’s Self-Certification Option (for tenant-occupied dwellings only) - If the lead pamphlet was delivered but a tenant signature was not obtainable, you may check the appropriate box below.
  Declined
  Unavailable for signature
Gather the following information:
  Printed name and signature of person certifying delivery
  Date and time of attempted lead pamphlet delivery
  Unit address
Notes: A sample form is provided at the back of the Lead-Safe Certified Guide to Renovate Right pamphlet that can be used to document your compliance with the federal pre-renovation education requirements. Some sample forms can also be seen on the next two pages.

## Slide 6: Recordkeeping: Non-Certified Worker Training
Worker’s name
Description of lead-safe work practices the worker is trained to perform
Completed and signed skills evaluation checklists
Date(s) of training
Name and signature of the certified renovator who conducted the training
Notes: Documentation of non-certified renovation worker training
The certified renovator who conducted the non-certified worker training must document the information taught to, and skill set proficiencies achieved by, each individual trainee. This training can be conducted in a classroom setting with simulated hands-on exercises or on the job. Documentation may vary for each trainee as not all trainees may be assigned to conduct all lead-safe work practices and the training is only required to be task specific.
To simplify this documentation, your training manual includes a form found in Appendix 6 that can be adapted for documenting hands-on and topical training for non-certified workers.

## Slide 7: Recordkeeping: Test Kit Reporting
If an EPA-recognized test kit is used to test surfaces in the work area, the firm must:
  Submit a report to the person contracting for the work within 30 days after the end of the renovation, containing:
    Manufacturer and model of the EPA-recognized test kit
    A description of the components tested
    The location of components tested
    Results of the testing
Retain a copy of the test kit documentation form
Notes: Checking for lead-based paint with EPA-recognized test kits:
Check https://www.epa.gov/lead/testkits for a list of EPA-recognized lead test kits.
Each component to be renovated or impacted by renovation must be tested. If all surfaces are found to be free of lead-based paint, the RRP Rule does not apply.
If a set of affected components make up an integrated whole (such as a stair tread or riser within a single staircase; or, a window casing, apron, stool, header or trough in a window case system), then only one of the individual components from that set needs to be tested.
EPA-recognized test kits:
Presently, EPA only requires the use of test kits that determine that lead-based paint is not present on the surfaces tested. Refer to test kit instructions to determine if lead is absent. If lead is not determined to be absent using the test kit the surface must be presumed to be coated with lead- based paint.
A negative test result will mean that lead safe-work practices are not required.
Alternatively, a certified renovator may collect a paint chip sample, or sampling may be performed by a certified lead inspector or risk assessor to determine whether or not lead-based paint is present.
If test kits are used, certified renovators must use an EPA-recognized test kit in order to test affected surfaces. EPA-recognized test kits are listed on the EPA website at https://www.epa.gov/lead/testkits.
Reporting:
When test kits are used, within 30 days of completing the renovation, the certified renovation firm must provide information on test kit manufacturers and models used for testing, a description of components tested including locations, and the results of testing, to the client who contracted for the renovation.
Retain a copy of the test kit documentation form.

## Slide 8: Recordkeeping: Paint Chip Sample Results Reporting
Paint chip sampling records must be maintained similarly to test kit results
  Submit a report to the person contracting for the work within 30 days after the end of the renovation, containing:
    Description and location of the components tested
    Dimensions of the area sampled, in cm and area in cm2
    Laboratory analysis results
  Retain a copy of lab results and client report
Notes: Reporting paint chip sample results:
Certified renovators may collect paint chip samples from components to be affected by renovation instead of using test kits to test the paint. The samples must be sent to an entity recognized by the National Lead Laboratory Accreditation Program (NLLAP) for analysis.
Prepare reports for clients and maintain records similar to that detailed for the test kit results. Submit a report within 30 days to the person contracting for the work detailed locations sampled, dimensions, and associated results.
Retain copies of the laboratory results and the client report for 3 years.

## Slide 9: Recordkeeping: Post-Renovation Reporting
Following a renovation, firms must document and share the following information
  Project information documenting compliance with renovation training, certification, and work practice requirements
  If performed, documentation of dust-lead sampling
  This information must be prepared, retained by the firm and shared with owners and occupants of housing and child-occupied facilities
Notes: Documentation of project information (compliance with renovation training, certification, and work practice requirements). This can be accomplished by completing the sample form titled “Sample Renovation Recordkeeping Checklist”(found in Appendix 4 and the next page of your manual), or a similar form.
The project information documentation must also be distributed when the final invoice is delivered or within 30 days of the completion, whichever is earlier, to the following :
The owner of the building; and, if different,
An adult occupant, or an adult representative of the child-occupied facility.
If dust-lead sampling is performed the firm must provide, when the final invoice for the renovation is delivered or within 30 days of the completion of the renovation, whichever is earlier, a copy of the dust-lead sampling report to:
The owner of the building; and, if different,
An adult occupant, or an adult representative of a child-occupied facility.
Note: When work is done in common areas of multi-unit housing, firms must post project information and dust sampling reports on how interested occupants of the housing being renovated can obtain a copy of the report. This information must be posted in areas where they are likely to be seen by all affected occupants.

## Slide 10: Now You Know…
Have records available at the work site of:
  Certifications for the certified firm and certified renovators
Retain all records for at least 3 years after completion of the renovation
Keep records of:
  Training and certifications for all renovation personnel, and for certification of the firm
  Distribution of required information
  Communications with and certifications from owners and residents
  Work activities in compliance to the RRP Rule
  Post-renovation reports